## Slide 1: Advanced Filtering
Notes: 1

## Slide 2: Alteon Filtering Objectives
Upon completion of this module, the user shall be able to:
  Understand the benefits of filtering
  Understand the switch’s filtering parameters
  Understand and configure Static and Dynamic NAT
  Understand and configure filtering IP ranges
  Understand and configure filter inverting

## Slide 3: Alteon Filtering
Alteon switches can filter packets based on:
  Source MAC address
  Destination MAC address
  By IP Source Address or Range
  By IP Destination Address or Range
  By IP Protocol Type (IP, UDP, TCP, ICMP, IGMP, OSPF, etc.)
  By Source or Destination Port Number
    HTTP, SMTP, SNMP, FTP, Telnet, etc.
    Source vs. destination depends on “direction” of frame flow
  TCP flags (ACK, RST, SYN, FIN, URG, PSH)
Notes: List of Well Known Protocols
1 ICMP
2 IGMP
6 TCP
17 UDP
89 OSPF
112 VRRP

## Slide 4: Alteon’s Policy Based Filtering Engine
Frame Ingress Port
Frame Inspection Engine
Match existing session?
  If yes, take action
  Else, inspect
Inspect in order by filter number for filters applied to port, e.g.
  Filter 2
  Filter 17
  Filter 36
Allow Frame / Express Forward
Drop
Redirect to Server Group
Possible Actions
Inspect per Unmatched Session
NAT

## Slide 5: Filter Usage
Configure filters globally, assigned them locally
Maximum number of filters-224 filters per switch
Filter number determines order of precedence
Filter numbering
Once filter fires, packet is passed
Default filters
Filtering logs

## Slide 6: Network Address Translation
Dynamic NAT filters (many to one)
  Clients with private IP addresses can have access to the Internet
Static NAT filters (one to one)
  External clients on Internet can access servers with private IP addresses

## Slide 7: Dynamic NAT Filters
Dynamic “many-to-one” filters require a single filter rule
Proxy IP address enabled on port, and as part of rule

## Slide 8: Configuring Dynamic NAT Filters
Configure dynamic NAT filter
    /cfg/slb/filt #
    invert ena (invert the filter logic – will be discussed shortly)
    dip 10.10.10.0 (anything NOT destined for the 10 network is NATed)
    dmask 255.255.255.0
    sip any
    act nat
    nat source (dynamic NAT filters work ONLY with source NAT)
    /adv/proxy ena
    ena
Configure a PIP on each port where a NAT filter is applied
    /cfg/slb/port #
    add # (add the filter to the port)
    filt ena (enable filtering on the port)
    pip 205.178.17.12
  Each port must have a unique PIP address

## Slide 9: Static NAT Filters
Static “one-to-one” filters are symmetric - they require a rule on the “inside” port on the switch and the “outside” port on the switch
One filter converts traffic from Client --> Server (IPDA conversion)
One filter converts traffic from Server-->Client (IPSA conversion)

## Slide 10: Configuring Static NAT Filters
Configure inbound NAT filter
  /cfg/slb/filt #
  dip 205.178.13.0
  dmask 255.255.255.0
  sip 10.10.10.0
  smask 255.255.255.0
  act nat
  nat dest
  proxy disable
  ena
Configure outbound NAT filter
  /cfg/slb/filt #
  dip 205.178.13.0
  dmask 255.255.255.0
  sip 10.10.10.0
  smask 255.255.255.0
  act nat
  nat source
  proxy disable
  ena
In the case of static NAT, the portion of the filter that is referenced by the “NAT” command within the filter is the corresponding address change that will be made. The other section (SIP or DIP) is a placeholder for the opposite filter.

## Slide 11: Applying the Static NAT Filters
Apply the filters
    /cfg/slb/port 1
    add 1 (add the filter to the port)
    filt ena (enable filtering on the port)
    ../port 2
    add 2 (add the filter to the port)
    filt ena (enable filtering on the port)

## Slide 12: Process Static Filters Before Dynamic Filters
Configure static filters with lower numbers than dynamic
Otherwise, one-to-one replies will use the many-to-one PIP as their IP SA

## Slide 13: Inverted Filters
Normal filters perform a logical AND on all filter parameters
  Filter fires if all filter conditions are met
Inverted filters perform a logical OR on all filter parameters
  Filter fires if any filter condition is not met

## Slide 14: Inverted Filtering Example
Notes: Inverted filters provide the ability to write more concise and efficient filters. With an inverted filter, all static NATs can be performed with a single filter. If you wanted to use standard filtering, you would have to use two filters for every static NAT instance. If you have multiple filters, this could take a toll on switch operations.

## Slide 15: Inverted Filter Example
Non Inverted Filters
Filter 1
  SIP 10.10.10.0/24
  DIP 10.10.10.0/24
  Action Allow
Filter 2
  SIP 10.10.10.0/24
  DIP Any
  Action NAT
  NAT Source
  Inverted Filter
  Filter 1
    Invert ena
    SIP any
    DIP 10.10.10.0
    Action NAT
    NAT Source
Notes:   Two examples of filters: one inverted, one non-inverted.
  The non-inverted filters require two filters: one to allow the 10.10.10.0 network traffic to flow to other 10.10.10.0 network devices and one to NAT any traffic that isn’t destined for the 10.10.10.0 network.
  The inverted filter processes those two requirements at the same time. With invert enables, the filter will fire if any of the conditions are NOT met. This means if the destination is a 10.10.10.0 network, the condition is met and the filter will not fire, as in non-inverted filter 1. If the destination is not a 10.10.10.0, the condition is not met and the filter will fire, as in non-inverted filter 2. In both cases, the result is the source IP is NAT’d from a private IP address to a public IP address.

## Slide 16: Denial of Service
Attempt by attackers to prevent legitimate users from using a service
Types of attacks
  Syn floods---most frequent
  Machine against machine
  Bandwidth consumption
Prevention against attacks
  Routers slowed by ACLs
  Put filters on better device, relieving router of filtering
Notes: Syn floods
This is probably the most common type of attack. Your attacker’s goal is to prevent hosts or networks from communicating on your network. This is accomplished by establishing a connection between the attacker and the victim machine, but it does this in such a way as to prevent the ultimate completion of the connection. In the meantime, the victim machine has reserved one of a limited number of data structure requests (a session request) to complete the impending connection. The attacker continues to request sessions, never completing them. The result is that legitimate connections are denied while the victim machine is waiting to complete bogus “half-open” connections.
Machine against machine
In this attack, the intruder uses forged UDP packets to connect the elected service on one machine to the service on another machine. The result is that the two services consume all available network bandwidth between them. Additionally, while the connectivity between the two targeted machines are ultimately affected, the network connectivity for all machines on the same networks may be affected as well.
Bandwidth consumption
An intruder may be able to consume all the available bandwidth on your network by generating a large numbe rof packets directed to your network. Typically, thses packets are ICMP Echo packets, but in principle they may be anything.

## Slide 17: DOS Prevention
First, set filters
  Router
  Wire speed device
Alteon is able to:
  Deny IP ranges
  Deny protocols
  Deny ports

## Slide 18: Configuring Filters
Create an appropriate set of global filters and enable them
  E.g., /cfg/slb/filt 100/sip any/dip any/proto tcp/sport any/dport 80/act deny/ena
Apply the filter(s) to the appropriate port(s)
Enable filtering on the port(s)
SLB must be turned on!
Apply, save and you’re done!
Notes: Steps to configure a filter
Configure Rules
  Addresses, Masks, Protocols, TCP/UDP Ports
  Set Action
  Logging
  Enable
Configure Default Rule
Configure Port for Filtering on/off
Add Filters to Port

## Slide 19: Filtering Summary
Filter adds in network protection and application redirection
Alteon switches are optimally engineered in order to perform packet filtering at wire speeds
Filter parameters
  IP ranges
  Protocols
  Ports (HTTP, Telnet, FTP, etc.)
  TCP Flags
  MAC address
Default Filters
  Implicit Allow vs. Implicit Deny