## Slide 1: Direct Access Mode & Proxy IP Addresses
Notes: 1

## Slide 2: DAM & PIP Objectives
Upon completion of this module, the user shall be able to:
  Understand immediate binding persistence
  Understand delayed binding persistence
  Understand Direct Access Mode (DAM) and its benefits
  Understand Proxy IP’s (PIP) and its benefits
  Configure DAM
  Configure PIP

## Slide 3: Review of Alteon’s Server Binding Mechanisms
Two types of binding mechanisms for Alteon Switches
  Immediate binding
    Decision about which real server to send the request to is made upon arrival of the TCP SYN packet
  Delayed binding
    Decision about which real server to send the request to is made after the TCP 3-way handshake is completed by the switch
Notes: Immediate bindings allow you to make L4 switching decisions based only on the information that comes in on the TCP SYN Packet that arrives. This basically allows the switch to make L4 decisions only on the VIP and VPORT that comes in with the original SYN.
With delayed bindings, L4 decisions can be made on the VIP/VPORT but also information from the client that resides further in the TCP frames, such as URL, SSL session ID, session cookie, permanent cookie or specific application-related information.

## Slide 4: The Life of an HTTP Request
IPDA 192.168.13.10: SYN ACK-ACK, TCP Port 80
Client
Client Site DNS Server
DNS Lookup for: www.alteon.com
DNS response with: 192.168.13.10
Client
Alteon’s Web Server
IPDA 192.168.13.10: TCP SYN, Dest TCP Port 80
IPDA (client) : TCP SYN-ACK
IPDA 192.168.13.10: HTTP GET (url), TCP Port 80
IPDA (client) : GET RESPONSE (data)
IPDA 192.168.13.10:TCP FIN, Dest TCP Port 80
IPDA (client) : TCP FIN-ACK
Notes: A Review of the HTTP Frame Flow
In Immediate Bindings, every frame will contain:
IP Source Address (IPSA)
IP Destination Address (IPDA)
Source TCP Port (sPort)
Destination TCP Port (dPort)
Delayed Bindings will contain the same information, but Alteon switches can parse information in the 1st HTTP GET frame and make switching decisions based on information contained in it. This includes URLs, SSL session IDs, session cookie, permanent cookie or specific application-related information.

## Slide 5: Immediate Bindings
Client
Load Balancer
Real Server
“Best Available Server” selection
TCP SYN request
TCP SYN request
Three-way handshake completion
1
2
3
4

## Slide 6: Delayed Bindings
Client
Load Balancer
Real Server
“Best Available Server” selection
TCP 3-way handshake
LB records sequence #
Client sends 1st GET
TCP 3-way handshake
LB records sequence #
Forwards the client’s GET
Sequence # adjustment and connection splicing
1
2
3
4

## Slide 7: Advantages of Delayed Binding
Allows a load balancer to observe client’s request and bind to the appropriate server
Enables advanced load balancing options
  URL Based Web Server Load Balancing
  URL Based Web Cache Redirection
  SSL Session ID Based Binding for session persistence
  Cookies Based Binding for session persistence

## Slide 8: Direct Access Mode

## Slide 9: Why Do We Need Direct Access Mode?
Without DAM, switch assumes flows from a RIP using a load balanced service are load balanced
Server-to-client traffic flow
  Sometimes, flows from a RIP that use a load balanced service should not be load balanced
  Switch must discriminate between load balanced and non-load balanced flows
Notes: Review of SLB server-to-client traffic flow
  Server to client frames use DIP = client IP, SIP = RIP
  Client expects to see frames coming from VIP, not RIP
  Translation done at server port but binding information stored at client port
  Server port translates SIP from RIP to VIP for all frames using load balanced services when SIP = RIP

## Slide 10: When Is Flow Discrimination Needed?
When providing direct access to real servers
  Load balanced, L4 frame flows
  Non-load balanced, native, L2/L3 frame flows
When a single RIP supports multiple VIPs
When delayed bindings are used
Notes: In server-to-client direction, switch must translate SIP if load balanced flow
Must not translate SIP if not load balanced flow
  Otherwise, client will receive SYN-ACK from VIP instead of RIP and will send a TCP-RST
When one RIP supports more than one VIP
  In server-to-client direction, switch must determine which VIP to substitute as the SIP
When delayed bindings are used
  Switch must terminate client-to-switch and switch-to-server connections and adjust sequence numbers

## Slide 11: DAM Configuration and Operation
Configure SLB as usual and enable DAM
  /cfg/slb/adv/direct ena
  Enables DAM for all VIPs and services
All server-to-client processing occurs at the client port
Notes: Restrictions when using DAM
  Network topology must force all server-to-client frames to exit the switch on the same physical port where the client-to-server frames entered
  Redirection filters cannot be run on the server ports
  Port mapping is not supported
  Default gateway load balancing is not supported

## Slide 12: Restrictions when using DAM
Network topology must force all server-to-client frames to exit the switch on the same physical port where the client-to-server frames entered
Redirection filters cannot be run on the server ports
Port mapping is not supported
Default gateway load balancing is not supported
Must use VMA to combine DAM with SLB and FWLB

## Slide 13: Valid and Invalid DAM Topologies

## Slide 14: Proxy IP Addresses

## Slide 15: Why Do We Need Proxy IP Addresses?
Need server-to-client frames explicitly addressed to the switch
  Diverse network topologies
  Direct server access
  Delayed bindings
Notes: When used with SLB, proxy IP addresses cause the switch to rewrite both the IP DA and IP SA for all load balanced frames in both directions
PIP addresses are also used with application redirection -- be careful not to confuse the two!

## Slide 16: What is a Proxy IP?
A Proxy IP (PIP) address is an IP address that is associated with a physical port on the switch
The PIP is substituted for the Client IP address as the frame flows through the switch
All frames received at the Destination IP address appear to have come from the PIP

## Slide 17: How is PIP Used?
In SLB, PIP addresses cause the switch to rewrite both the IP DA and IP SA for all load balanced frames in both directions
In application redirection, PIP addresses are used to redirect frames to alternate sites

## Slide 18: Session ID Substitution without PIP:Client to Server
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Vmac
Cmac
B62A
CIP
VIP
037A
2155
80
Client
Vmac
Cmac
B62A
CIP
VIP
037A
2155
80
Alteon Switch
Rmac
Cmac
48A0
CIP
RIP
C107
2155
80
Rmac
Cmac
48A0
CIP
RIP
C107
2155
80
Real Server

## Slide 19: Session ID Substitution with PIP:Client to Server
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Vmac
Cmac
644B
CIP
VIP
A786
2155
80
Client
Vmac
Cmac
644B
CIP
VIP
A786
2155
80
Alteon Switch
Rmac
Pmac
823F
PIP
RIP
02C5
10420
80
Rmac
Pmac
823F
PIP
RIP
02C5
10420
80
Server

## Slide 20: Session ID Substitution without PIP:Server-to-Client
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Client
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Alteon Switch
Cmac
Rmac
823F
RIP
CIP
0A15
80
2155
Cmac
Rmac
823F
RIP
CIP
0A15
80
2155
Real Server

## Slide 21: Session ID Substitution with PIP:Server-to-Client
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Client
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Alteon Switch
Pmac
Rmac
823F
RIP
PIP
0A15
80
10420
Pmac
Rmac
823F
RIP
PIP
0A15
80
10420
Server

## Slide 22: SLB PIP Configuration
Configure SLB as usual except server processing should not be enabled on server-side ports
Configure a PIP address on each client side port
  /cfg/slb/port n
  pip x.x.x.x
  Each port must have a unique PIP address if using VMA
With VMA enabled, all ports must be configured with a PIP
  PIPs may be invalid (Per RFC 1918)

## Slide 23: SLB PIP Notes
All server-to-client processing occurs at the client port
  PIP Binding Table
Restrictions when using PIP addresses
  Redirection filters should not be run on the server ports
  Real server cannot collect valid user statistics
  Network troubleshooting will be difficult

## Slide 24: DAM & PIP Examples

## Slide 25: Direct Real Server Access: Ease Migration from Round Robin DNS to SLB
Client
HTTP Servers for a.com
Before Picture
205.178.13.2
205.178.13.3
205.178.13.4
Internet
Upstream DNS Server
a.com = 205.178.13.2 a.com = 205.178.13.3 a.com = 205.178.13.4
Local Network
Local DNS Server
a.com = 205.178.13.3
Notes: New SLB customers must often migrate from a current load balancing infrastructure that uses round robin DNS. An example round robin DNS configuration is shown in this slide. The upstream DNS server responds to requests for a.com’s address with one (or more, if the requester can handle a list) of the addresses on an ordered list. Note that, in this example, the local DNS server has cached only one address for a.com.

## Slide 26: Direct Real Server Access: Ease Migration from Round Robin DNS to SLB
Client
HTTP Servers for a.com
After Picture
205.178.13.5
205.178.13.3
205.178.13.4
Internet
Upstream DNS Server
a.com = 205.178.13.2
Local Network
Local DNS Server
a.com = 205.178.13.3
VIP = 205.178.13.2
Can implement using DAM or proxy IP
Notes: In this example, the customer has followed our advice to move the address (205.178.13.2) of one of the servers supporting a.com to be the VIP for a.com and to reconfigure DNS to advertise only that address. Unfortunately, the client’s local DNS server still has 205.178.13.3 in it’s cache. Without direct RIP access, the client would not be able to reach a.com until this entry was flushed from the local DNS server’s cache. With direct RIP access, the client can reach a.com even though it’s local DNS server has a stale address cached.

## Slide 27: Direct Real Server Access: More Management Topology Options
Management Station
HTTP Servers for a.com
205.178.13.5
205.178.13.3
205.178.13.4
VIP = 205.178.13.2
Goal: Allow management station to execute scripts that test responsiveness of each real server in server farm by retrieving a Web page.
Can implement using DAM or proxy IP

## Slide 28: Web Hosting: Complicated IP Addressing
In hosting sites, supporting multiple domains on the same set of servers requires complicated IP addressing or port mapping.
Client
205.178.13.5 205.178.14.5 205.178.15.5
VIP = 205.178.13.2 205.178.14.2 205.178.15.2
DNS Server
a.com = 205.178.13.2 b.com = 205.178.14.2 c.com = 205.178.15.2
205.178.13.3 205.178.14.3 205.178.15.3
205.178.13.4 205.178.14.4 205.178.15.4

## Slide 29: Web Hosting: Simplified IP Addressing
With multiple VIPs per RIP, IP addressing is simplified without requiring port mapping.
Client
205.178.13.5
VIP = 205.178.13.2 205.178.14.2 205.178.15.2
DNS Server
a.com = 205.178.13.2 b.com = 205.178.14.2 c.com = 205.178.15.2
205.178.13.3
205.178.13.4
Implement using DAM

## Slide 30: Enforcing Frame Flow with Proxy IP
Ensure proper frame flow proxy IP
  When performing proxy IP load balancing, IP source addresses are replaced with a configured proxy IP address at the client port
  Ensures that response frames from the servers with come back to the switch.
Local and Remote Load Balancing
  Allow customers to flexibly deploy servers across routed networks
VIP1
RIP Group1
Clients
Notes: By combining IP routing and Full Network Address Translation, where the IPSA and IPDA are translated on every SLB frame, the Real Servers can exist anywhere in a routed network.
User’s will want to be prudent in how these configurations are deployed, but there is no reason that VIPs and RIPs cannot be separated by a WAN connection.
This setup REQUIRES two connections from the Alteon switch to the backbone network - one to act as a SLB Network connection ; one to act as an SLB Server connection. When connecting in this manner to a backbone switch, proper VLAN and Spanning Tree design guidelines must be followed.

## Slide 31: Content Switching HTTP Content Based Load Balancing
GET/www.foo.com/event/reg.bin
GET /www.foo.com/images/abc.gif
GET /www.foo.com/product/abc.html
Load distributed within group via any standard metric or URL hashing
Sub-string matching for:
  “.cgi”
  “.bin”
  “.exe”
Sub-string matching for:
  “.html”
Inspect request content including URL, HTTP headers, cookie and SSL Session ID.
Support multiple frames inspection, up to 4,500 bytes
Sub-string matching for:
  “images”
  “.gif”
  “.jpg”

## Slide 32: Cookie Cutting
Preferential services
  Redirect higher priority users to a higher capacity server or server group
  Identify a user group and redirect them to a particular server
  Serve content based on user identity
  Prioritize access to scarce resources on a web site
  Provide better services to repeat customers, based on access count
Notes: Users can be identified by one of the following methods:
1. Individual User
Specific individual user distinguished by IP address, login authentication or permanent HTTP cookie.
2. User Communities
Some set of users, such as “Premium Users” for service providers who pay higher membership fee than “Normal Users”., may be identified by source address range, login authentication or permanent HTTP cookie.
Cookies can be used to provide preferential services for customers. An example is a web server could authenticate a user via a password and then set cookies to identify them as “Gold”, “Silver” or “Bronze” customers. “Gold” customers may get redirected to better resources and receive better service than all other users.

## Slide 33: Preferential Services
GET/www.foo.com/event/cookie=“Silver”
GET /www.foo.com/images/cookie=“Gold”
GET /www.foo.com/product/cookie=“Bronze”
“Gold” Server Group
“Bronze” Server
Differentiate users and place them into groups or communities
Provides preferential service for customers based on some form of ID, e.g. HTTP cookie
“Silver” Server Group
Gold
Customer
Silver
Customer
Bronze
Customer

## Slide 34: Content-Intelligent Load Balancing
Virtual Hosting
  Single VIP to represent multiple domains for hosting customers
Preferential Service Policy
  Hoster can provide differentiated service, e.g. Gold, Silver or Bronze customers
  Based on HTTP cookie information
Server Selection based on browser type
  Direct requests to different servers based on browser types

## Slide 35: Why Virtual Hosting?
http://www.isp.com
Client #1
http://www.isp.com/~client1
Client #2
http://www.isp.com/~client2
Client #3
http://www.isp.com/~client3

## Slide 36: Virtual Hosting on Web Server
http://www.isp.com
172.16.0.1
Client #1
http://www.client1.com
IP Address = 172.16.0.2
Client #2
http://www.client2.com
IP Address = 172.16.0.3
Client #3
http://www.client3.com
IP Address = 172.16.0.4
IP Aliases
172.16.0.2
172.16.0.3
172.16.0.4

## Slide 37: Virtual Hosting with WebOS
Client #1
http://www.alteon.com
VIP = 172.16.0.1
Client #2
http://www.nortel.com
VIP = 172.16.0.1
Client #3 & #4
http://www.shasta.com
VIP = 172.16.0.1
http://www.neato.com
VIP = 172.16.0.1
IP_1: alteon.com
IP_2: nortel.com
IP_3: shasta.com
IP_4: neato.com
www.neato.com
www.alteon.com
www.nortel.com
www.shasta.com
VIP = 172.16.0.1

## Slide 38: DAM/PIP Summary
DAM & PIP are used to support delayed binding applications
DAM allows direct access to servers
PIP rewrites both the SMAC and IPSA for all load balanced frames
  PIP on each port must be unique if using VMA