## Slide 1: Persistency
Notes: 1

## Slide 2: Persistency Objectives
Upon completion of this module, the user shall be able to:
  Understand immediate binding persistence
    IP load balancing, hash, minmisses
  Understand delayed binding persistence
    SSL ID, cookie parsing, cookie search
  Configure immediate binding persistence
  Configure delayed binding persistence

## Slide 3: Persistence Mechanisms Using Immediate Bindings
Hash and Minmiss algorithms
IP load balancing
Pbind – Timer Based Persistence

## Slide 4: Persistence Mechanisms Using Delayed Bindings
SSL session ID
Cookie-based

## Slide 5: Introduction to SSL
  Multi-layered protocol
  Sources that create SSL messages – Handshake, Change Cipher, Alert, Applications – HTTP
  Handshake protocol - SSL Hello to negotiate encryption algorithm
  Record Layer – Formats, Encrypts message, Message Authentication
  SSL Hello Handshake done in clear text
  Normal data encrypted using encryption algorithm exchanged after handshake

## Slide 6: SSL Protocol Overview
1. Establish SSL Session ID
2. Exchange security certificates
3. Negotiate an encryption and
compression method
SSL
Handshake

## Slide 7: SSL Protocol Messages
Protocol Messages | Important fields
Client Hello | SSL Version , Random number, Session ID, List of Ciphers
Server Hello | SSL Version, Random Number, Session ID, Cipher suite
ServerKeyExchange | iSD-SSL’s RSA Public Key. (Sent in clear)
ClientKeyExchange | Key to be used for symmetric encryption
ChangeCipherSpec | Symmetric encryption algorithm ( DES, 3DES,..), Message Integrity algorithm ( MD5..) & keys for session
Certificate | Authenticate iSD-SSL (proxy for server) Authenticate Client (Not supported by Alteon)

## Slide 8: SSL Handshake Protocol – New SSL Session
Client Connects to SSL using a Client Hello
1
SSL responds to Server Hello selecting the SSL options
2
Server Hello Done
4
Client Key Exchange
5
Client sends Change Cipher Spec
6
Finished
7
Change Cipher Spec
8
Finished
9
10
Secure Session
Public Key in ServerKeyExchange message
3
Certificate

## Slide 9: SSL Handshake Protocol – Session ID reuse
Server Hello (SSL ID)
Client SSL Hello (SSL ID)
Client Change Cipher
Finished
Finished
Change Cipher Spec
Notes: Frequency of SSL connections – Depends on Design of Web server, client base and HTTPs use of SSL sessions.
SSL provides session ID caching- allows a client to request a previously established secure session to be resumed for a new HTTP transaction. Ideally each user visit only corresponds to a single session.
According to Rainbow on the Intranet a limited number of clients engage in substantial communication . So Session ID caching.
On the Internet, many of the requests are small requests. The benefits of sesion id caching diminishes. Also, session id information affects the host CPU on the servers.

## Slide 10: SSL Session ID Persistence
Web
Server
Farm
Client #1
Client #2
Internet
Proxy Firewall
RIP_1
RIP_3
RIP_2
Proxy Firewalls break persistency by IP Source Address
Many individual users coming from a proxy firewall will be directed to a single server
Traffic concentrated on a single server instead of load balancing
Notes: Client #1 requests new SSL session
Switch recognizes the session is new and selects server RIP_1 based on configured load balancing algorithm
TCP Connection Spliced
SSL Hello Handshake between client #1 and RIP_1 via the switch
SSL Session ID assigned to client #1
Switch records the SSL Session ID
Subsequent connections from client #1 to VIP with the same SSL Session ID get directed to RIP_1
Client #2 appears to the switch as the same source IP address and requests a new SSL session
Switch recognizes that client #2 does not have an established SSL session and WILL NOT direct client #2 to RIP_1
Switch performs steps described above and spliced connection from client #2 to RIP_3
Subsequent connections from client #2 to VIP with the same SSL Session ID get directed to RIP_3

## Slide 11: Configuring SSL Session ID Persistence
Configure as you would for SLB without persistence
Enable DAM or specify PIP address(es) on the client port(s)
  If PIP addresses are used, make sure server processing is disabled on the server port
SSL session ID persistence is on a per VIP basis
Enable persistent bindings for TCP port 443 to be type “sessid”
  /cfg/slb/virt 1/service <tcp port #>
  pbind sslid

## Slide 12: Cookie-Based Persistence
Cookie based persistence causes requests with the same cookie to be sent to the same real server
  Cookie can contain IP address to load balance to or arbitrary data used to generate hash key
Best HTTP persistence mechanism, useful only for HTTP
Two modes of cookie based persistence
  Passive Cookie Mode
    Admin configures in the real server the cookie and value that the switch looks for
  Cookie Rewrite Mode
    Server is configured to return a special cookie with a null value
    Switch intercepts the special cookie and rewrites the value to include specific server information
Support for cookie-assignment servers

## Slide 13
Web
Server
Farm
Client #1
Client #2
Internet
Proxy Firewall
RIP_1
RIP_3
RIP_2
Same Proxy IP address for all clients
All connections from clients behind the proxy firewall will get redirected to R_IP 1
Why Source IP Persistence Mode Does Not Work
Many individual users coming from a proxy firewall will be directed to a single server
Traffic concentrated on a single server instead of load balancing
Notes: Every element of a Web Page (GIF, JPG images, HTML text, buttons, toolbars, sounds, etc all require a separate TCP connection/session with HTTP 1.0, the most common version of HTTP.

## Slide 14
Web
Server
Farm
Client #1
Client #2
Internet
Proxy Firewall
RIP_1
RIP_3
Second connection from client #1 get redirected to RIP_3 based on Proxy IP address #2
Persistence based on Source IP address is broken when there is more than one proxy address used by the proxy firewall
RIP_2
First connection from client #1 get redirected to RIP_1 based on Proxy IP address #1
A pool of Proxy IP addresses for all clients
Connections from the same client may use different Proxy IP Address
Why Source IP Persistence Mode Does Not Work?
Notes: Every element of a Web Page (GIF, JPG images, HTML text, buttons, toolbars, sounds, etc all require a separate TCP connection/session with HTTP 1.0, the most common version of HTTP.

## Slide 15: Passive Cookie Mode
Administrator configures the server defined cookie to be used for maintaining persistency
Web
Server
Farm
Client #1
Client #2
Internet
Proxy Firewall
RIP_1
RIP_2
Server responds with a cookie value in the server defined cookie
Switch records the cookie value and the server that provides the respond
Subsequent requests from client #1 with the same cookie value will be sent to the same server, RIP_1 in this example.
Client #1 first visit to the web site with an HTTP request, without the configured cookie
Switch chooses a server and sends the request through

## Slide 16: Cookie Rewrite Mode
Web
Server
Farm
Client #1
Client #2
Internet
Proxy Firewall
RIP_1
RIP_2
Client #1 first visit to the web site with an HTTP request without the cookie “Alteon Persistence”
Switch chooses a server and sends the request through
HTTP response from the server now contains the cookie “Alteon Persistence” with an empty value
Switch rewrites the value of the cookie “Alteon Persistence”
The cookie value represents a server, e.g. the value can be used for hashing into a server ID or it can be the server IP address or server ID
Subsequent requests from client #1 with the same cookie value will be sent to the same server, RIP_1 in this example.

## Slide 17: Cookie Assignment Servers
Web
Server
Farm
Client #1
Client #2
Internet
Proxy Firewall
RIP_1
RIP_3
First request without cookie can optionally be redirected to a group of cookie assignment servers
Cookie assigned to client #1 by server RIP_1
Switch uses cookie value in subsequent requests to hash to server RIP_3
RIP_2
Cookie Assignment Servers
RIP_4

## Slide 18: Cookie Cutting
Applications requiring intelligent session tracking
  Associate user information with server
  Server has unique data associated with a user
  Increases server efficiency by taking advantage of memory caching
  Forms that span multiple pages
  “Shopping cart” sessions
Notes: Users can be identified by one of the following methods:
1. Individual User
  Specific individual user distinguished by IP address, login authentication or permanent HTTP cookie.
2. User Communities
  Some set of users, such as “Premium Users” for service providers who pay higher membership fee than “Normal Users”., may be identified by source address range, login authentication or permanent HTTP cookie.
Cookies can be used to provide preferential services for customers. An example is a web server could authenticate a user via a password and then set cookies to identify them as “Gold”, “Silver” or “Bronze” customers. “Gold” customers may get redirected to better resources and receive better service than all other users.

## Slide 19: Cookie based persistence How it works?
1 User visits the website the first time
2 Switch completes 3-way handshake with client
- Selects the appropriate server
- Forwards the HTTP request to the server
3 Web server provides the page information along with the cookie information
4 Switch “records” or “rewrites” cookie information depending on configuration
5 Cookie stored on client computer
6 Subsequent requests from the same user with the same cookie value visit the website
7 Based on cookie information, switch redirects request back to the same server
Notes: Cookies are a general mechanism for maintaining state between clients and servers. They allow the server to issue a “token” to the client, which the client will send to the server on all subsequent requests. This way the server does not need to use authentication, the client IP address, or any other time –consuming or failure-prone mechanism to determine that the user is the same certain user as before.
In the simplest case, the cookie may be just a “customer ID” assigned to the user. It may be a token of trust, allowing the user to ship authentication while his or her cookie is valid. It may also be a key that associates the user additional state data that is kept on the server, such as a shopping basket and its contents. In a more complex application, the cookie may be encoded so that it actually contains more data than just a single key or an identification number. The cookie may contain the user’s preferences for a site that allow their pages to be customized.
A cookie is defined as an HTTP header based on RFC2109. The format of the cookie header is “Name”=Value” pair in addition to other parameters. Cookies can be permanent, i.e. it gets stored on the client’s browser or cookies can be temporary, i.e. the cookie is only valid for the browser session. Based on the RFC2109, cookie without an expiration date is a temporary cookie. Examples of cookies are:
Cookie:ASP_SESSIONID=POIUHKJHLKHD
Cookie: name=john_smith
The first example represents an Active Server Pages (ASP) session ID and the second example represents an application specific cookie that records the name of the client.

## Slide 20
Cookie-based Persistence Passive Cookie Mode
1. Admin configures server or application to send cookie
Web
Server
Farm
Client #1
Client #2
Proxy Firewall
RIP_1
RIP_2
3. Client visits web site
4. Switch selects “most available” server and sends request.
5. Server responds with a value in the server defined cookie
6. Switch registers the cookie value
Internet
2. Admin configures switch to record cookie value
Notes: Passive mode
  No definition of any special persistence cookie on the server
  Admin configures an existing cookie that the switch uses
  Switch monitors cookie information in HTTP response
The sequence of steps that occur in this case are
Client sends a HTTP request without the server defined cookie to the switch
Switch selects the real server based on load balancing algorithm to redirect the client HTTP request
HTTP response from the real server,with the cookie value, is intercepted by the switch
Switch registers the cookie value before it returns the HTTP response back to the client
The cookie value is used to maintain persistency

## Slide 21
Cookie-based Persistence Cookie Rewrite Mode
Web
Server
Farm
Client #1
Proxy Firewall
RIP_1
RIP_2
3. Client visits web site
4. HTTP response from server contains cookie with empty value.
5. Switch rewrites the value of the cookie
6. The cookie value identifies a server - the value can be used for hashing into a server ID
2. Admin configures switch to perform cookie rewrite
Internet
1. Admin configures server or application to send a specific persistence cookie
4. Switch selects “most available” server and sends request.
Notes: Cookie rewrite mode
The Web switch uses a specific cookie, “Alteon Persistence” cookie defined by the server
The server persistence cookie is a permanent cookie
Server reserves the space for the cookie
Switch rewrites the cookie value with the IP address of server or server identifier
The sequence of steps that happen in this case are
Client sends a HTTP request to the load balancer, without the Server Persistence Cookie
Switch selects the best real server based on load balancing algorithm to redirect the HTTP request
HTTP response from real server to the load balancer with the Server persistence cookie with empty value
Load balancer inserts the value that represents the real server in the Server Persistence Cookie before it returns the response back to the client.
The value of this Server Persistence Cookie is used to maintain persistence to the real server for future requests

## Slide 22: Configuration Components
Configure as you would for SLB without persistence
  Select hash as the metric if NOT embedding IP address in cookie (use with cookie assignment server)
  If embedding IP address in cookie, select round-robin or leastconns as metric
Enable DAM or specify PIP address(es) on the client port(s)
  If PIP addresses are used, make sure server processing is disabled on the server port
Configure cookie-specific parameters

## Slide 23: Configuring Cookie-based Persistence
Enable cookie load balancing on the VIP
  /cfg/slb/virt #/service <tcp port #>/httpslb e/cookie
Configure a cookie name, offset, and length
  Choice of hashing vs. embedding real server IP address implicit in this assignment
Optionally assign a server specifically to serve cookies when client requests do not contain the specified cookie
  /cfg/slb/real #/layer7/nocook e
  Connection requests without cookies are load balanced across real servers with this enabled within the group
  Requests with cookies are load balanced across other real servers in the group

## Slide 24: Server-Side Multi-Response Cookie Search
Enables web switch to look beyond first HTTP response for persistence cookie
  Configurable from 1 to 16 responses
  /cfg/slb/virt #/service <tcp port #>/rcount

## Slide 25: Delayed Binding Considerations
Subject memory limitations
Enabling delayed bindings will result in tradeoff performance
Persistence versus even distribution
  Persistence take precedence over load balancing

## Slide 26: Persistency Summary
Persistency allows successive sessions to go back to the same server for:
  Forms
  Shopping carts
  Search engines
  Credit card transactions
Persistency is available for both immediate bindings and delayed bindings
Configurations of delayed bindings requires the configuration of DAM or PIP