## Slide 1: Advanced Firewall Load Balancing

## Slide 2: Advanced FWLB Objectives
Upon completion of this module, the user shall be able to:
  Understand the advantages of 4 switch FWLB
  Understand and configure 4 switch FWLB with STP and VLANs to block broadcast loops
  Understand and configure 4 switch direct connect FWLB (Bucher Box)
  Understand 4 switch FWLB with SLB and URL SLB
  Understand FWLB with DMZs
  Understand FWLB with NAT
  Understand FWLB with HTTP health checks

## Slide 3: Application Redirection Example: Firewall Load Balancing
Redirect incoming and outgoing traffic to group of firewalls
Automatic load balancing across multiple firewalls
Filter packets at ingress port so firewalls see only relevant packets
Benefits:
  Increase firewall performance
  Reduce response time
  Redundant firewalls ensures internet access
Campus LAN
Load-sharing, redundant firewalls
External servers

## Slide 4: A Review of Basic FWLB Concepts
FWLB is an extension of Application Redirection
Uses hash metric for persistency
ICMP or HTTP for health checks
Static routes for health checks
Load balance opposite interfaces
FW 1
Redir
Filter
Redir
Filter
FW 2

## Slide 5: Two-Switch FWLB Data Flow
Internet,
Web Servers
Secured Network
Clients
Alteon Switch
Firewalls
Alteon Switch
Client data enters clean side switch
Data is redirected by
the entry port to the firewalls
Client data exits dirty side switch
Traffic hits redirection filter at ingress to firewall sandwich
Hash metric ensures that clean-to-dirty and dirty-to-clean traffic between IP address pairs traverses the same firewall in both directions

## Slide 6: Two-Switch FWLB Health Check Flow
Internet,
Web Servers
Secured Network
Clients
Alteon Switch
Firewalls
Alteon Switch
ICMP health checks pass through the firewalls to the opposing switch to detect if firewall is up
Notes: 2 switch FWLB rarely used in production
Provides for firewall failover
Switch becomes single point of failure
Main use is for learning purposes

## Slide 7: Two Switch FWLB Configuration
Configure firewalls
  Interfaces
  Static routes
Configure interfaces on both switches
  3 interfaces
    1 exterior
    2 interior
Enable default gateways
Configure static routes on switches

## Slide 8: Two Switch FWLB Configuration
Configure real servers on each switch
  Set opposite switch interfaces as real servers
Turn on SLB on each switch
Configure groups
  Place interfaces in groups
Configure redirection filters
Configure ports with filters
  Assign redirection filters to ports not connected to firewalls
Check connectivity

## Slide 9: Concepts of Advanced FWLB
Same concepts from basic FWLB used in Advanced FWLB
  Redirection filters on outside ports
  Health check opposite interfaces through firewalls
  Hashing for persistency
  Static routes facilitate health checks
More options/more complexity
  Multiple switch configurations
  Additional health checks

## Slide 10: Advanced FWLB Configurations
4 switch FWLB with STP
4 switch FWLB with VLANs
4 switch direct connect FWLB
FWLB with SLB/URL SLB
FWLB with DMZ
FWLB with NAT
FWLB with HTTP health check

## Slide 11: Four Switch FWLB
Most widely implemented FWLB
4 switch FWLB provides full fault tolerance
Uses VRRP routers as failover gateways
  Define VRs as RIP interfaces
L2 switches used for link redundancy
4 switch FWLB introduces L2 bridge loops into network configuration
Requirement to block bridge loops for operation
  STP
  VLANs

## Slide 12: Four Switch FWLB with STP
Four switch FWLB introduces loops into network due to provide L2 link redundancy
STP blocks redundant links
  STP blocks redundant links on a L2 level
    Source of broadcast storms
  STP must be enabled on all switches
Configure switch’s bridge root priorities to ensure proper switch failover
  Switch with highest priority (lowest value) is bridge root
  Main Alteon highest, backup switch second highest priority

## Slide 13: Four Switch FWLB Diagram
Client
Switch 2
Switch 1
Switch 3
Switch 4
Server
200.1.1.X
200.1.2.X
192.168.X.X
.1.2
.3.2
.1.3
.3.3
.2.2
.4.2
.2.3
.4.3
.2
.3
.2
.3
VR Routers
192.168.1.1
192.168.3.1
200.1.1.1
VR Routers
192.168.2.1
192.168.4.1
200.1.2.1

## Slide 14: Four Switch FWLB with STP
Higher Bridge Priority
Client
Switch 2
Switch 1
Switch 3
Switch 4
Lower Bridge Priority
Higher Bridge Priority
Lower Bridge Priority
Broadcast Domain 1
Broadcast Domain 2
X
X
X
X
Notes: With STP, the bridge root priority will forward on all ports. The other switches that participate in spanning tree protocol will be responsible for blocking L2 (MAC level) redundant links. If switch 1 is the bridge root, switch 2 will be responsible for listening to all ports, learning which ports have duplicate MAC addresses and blocking the ports that have duplicate MAC addresses, forwarding on only one of those duplicate ports.
In the diagram above, you see two broad cast domains, each with with loops. Since switch 2 is the lower priority, it is responsible for blocking its ports. Switch 2 listens on all ports and learns that it can hear switch 1’s MAC address on two ports, which can lead to a broadcast loop. Switch 2 blocks one (or more) of the duplicate ports, eliminating the broadcast loops.
Since there are two separate broadcast domains, similar STP configurations can be placed on the second pair of switches, also eliminating broadcast loops in the 2nd broadcast domain.

## Slide 15: Four Switch FWLB with STP Configuration
Configure firewalls
  Interfaces
  Static routes
Configure STP on Alteon switches
  Highest priority on main switch
  Lower priority on secondary switch
Configure interfaces on all four Alteon switches
  3 interfaces---1exterior, 2 interior
Configure VRRP routers on each switch
Enable IP forwarding
Enable default gateways
Configure static routes on switches
  Ensure RIP is turned off

## Slide 16: Four Switch FWLB with STP Configuration
Configure real servers on each switch
  Set opposite switch virtual interfaces as real servers
Turn On SLB on each switch
Configure groups
  Place interfaces in groups
Configure filters
  Local access filters
  Redirection filters
  VRRP exception filters
Configure ports with filters
  Assign filters to ports
Check connectivity

## Slide 17: Four Switch FWLB with VLANs
Four switch FWLB introduces loops into network due to provide L2 link redundancy
Similar to STP, VLANs can be used to block L2 broadcast loops
Offers faster VRRP interface failover than STP

## Slide 18: Four Switch FWLB with VLANs
Client
Switch 2
Switch 1
Switch 3
Switch 4
Server
VLAN 1
VLAN 2
VLAN 3
VLAN 1
VLAN 2
VLAN 3

## Slide 19: Four Switch FWLB with VLAN Configuration
Configure firewalls
  Interfaces
  Static routes
Configure VLANs on Alteon switches
  Place each switch port in a separate VLAN
Configure interfaces on all four Alteon switches
  3 interfaces---1 exterior, 2 interior
Configure VRRP routers on each switch
Enable IP forwarding
Enable default gateways
Configure static routes on switches
  Ensure RIP is turned off

## Slide 20: Four Switch FWLB with VLAN Configuration
Configure real servers on each switch
  Set opposite switch virtual interfaces as real servers
Turn On SLB on each switch
Configure groups
  Place interfaces in groups
Configure filters
  Local access filters
  Redirection filters
  VRRP exception filters
Configure ports with filters
  Assign filters to ports
Check connectivity

## Slide 21: Four Switch Direct Connect FWLB (Bucher Box)
Variation of 4 switch FWLB with STP
  Similar configuration
  Different network topology
Each firewall port is directly connect to an Alteon Switch
  One to dirty side, one to clean side
No hub or L2 switches used in network topology
Simpler configuration to manage
Decreased fault tolerance
  Loss of a switch will lead to loss of firewall

## Slide 22: Direct Connect FWLB (Bucher Box)
Client
Switch 2
Switch 1
Switch 3
Switch 4
Server

## Slide 23: Four Switch Direct Connect Configuration
Configuration is similar to 4 switch STP configuration
Configure firewalls
  Interfaces
  Static routes
Configure STP on Alteon switches
  Highest priority on main switch
  Lower priority on secondary switch
Configure interfaces on all four Alteon switches
  3 interfaces
    1 exterior
    2 interior
Configure VRRP routers on each switch

## Slide 24: Four Switch Direct Connect Configuration
Enable IP forwarding
Enable default gateways
Configure static routes on switches
  Ensure RIP is turned off
Configure real servers on each switch
  Set opposite switch virtual interfaces as real servers
Turn On SLB on each switch
Configure groups
  Place interfaces in groups

## Slide 25: Four Switch Direct Connect Configuration (cont’d)
Configure filters
  Local access filters
  Redirection filters
  VRRP exception filters
Configure ports with filters
  Assign filters to ports
Check connectivity

## Slide 26: Four Switch FWLB with SLB
FWLB + SLB
  Add VIP and servers to load balance to clean side switch
  Requires no additional hardware
FWLB + URL SLB
  Requires PIP configured on the client port
    Uplinks from the clean side to the firewalls
    Each PIP must be unique
  FWLB and DAM do not work together without VMA enabled

## Slide 27: FWLB with DMZ
Untrusted hosts
Router
Firewall
DMZ
Internal Network
DMZ is a segment of the network where external clients can have access to internal servers
Untrusted hosts only have access to services for which they are cleared Three types of DMZ
  Dirty side DMZ
  Firewall DMZ
  Clean side DMZ

## Slide 28: Dirty Side DMZ FWLB
No traffic travels through firewalls
  Filter set to redirect to servers,not firewalls
Switch is responsible for all access control
No logging or monitoring of traffic possible
Untrusted hosts
DMZ
Internal Network

## Slide 29: Firewall DMZ
Provides internal network security, as with traditional DMZ
Normal FW DMZ results in loss of fault tolerance
Additional L4 switches add fault tolerance and security
Untrusted hosts
DMZ
Internal
Network

## Slide 30: Clean Side DMZ
DMZ connected to clean side switch
All inbound and outbound traffic must pass through firewall before being routed to its final destination
No internal connections allowed without clearance from firewalls
Untrusted hosts
DMZ
Internal Network

## Slide 31: FWLB with NAT
Used with networks that have private IP’s internally but need access to public networks
Dynamic NAT --- many-to-one NAT
  Firewalls carry many-to-one NAT address for outbound traffic
  Dirty side switches require an additional NAT exception filter to allow NAT traffic to flow to and from switches
Static NAT --- one-to-one NAT
  No exception filters required
  Both firewalls must carry the same inbound and outbound static NAT configuration

## Slide 32: FWLB with HTTP Health Checks
Used instead of ICMP to eliminate ICMP ping concerns
Health HTTP instead of ICMP
Content required to be HEALTH.HTML in real server group
Create a high-numbered dummy filter for HTTP processing
  Filter 223: Default Filter (to limit access to filter 224)
  Filter 224: SIP ANY, DIP ANY, PROTO ANY, SPORT HTTP, DPORT HTTP, RPORT HTTP, ACTIO REDIR, GROUP 1 (HTTP Triggering Filter)
Add dummy filter to any port you are using or after the final allow/redir filter on a port you are using
HTTP health checks do not work with FWLB where VRs are used as RIPs
  Per VR Spec, HTTP connections directed to VRs are not passed to master interfaces

## Slide 33: FWLB Troubleshooting Concepts
Do L2 first
  Make sure it works
  STP
  VLANs
Do L3 next
  Make sure it works
  Pinging limitations
Do L4 next
  Make sure it works
Turn on firewall policies LAST
Most common mistake
  Static routes on switches or firewalls

## Slide 34: Advanced FWLB Summary
Four switch firewall load balancing allows for full fault tolerance with increased firewall throughput
Advanced features provide for multiple configuration options:
  4 switch FWLB with STP
  4 switch FWLB with VLANs
  4 switch direct connect FWLB
  FWLB with DMZ
  FWLB with NAT
  FWLB with SLB/URL SLB
  FWLB with HTTP health check