## Slide 1: URL Parsing
Notes: 1

## Slide 2: URL Parsing Objectives
Upon completion of this module, the user shall be able to:
  Understand the advantages of URL based SLB
  Understand the advantages of URL based WCR
  Understand URL parsing parameters
  Configure URL Server Load Balancing
  Configure URL Web Cache Redirection

## Slide 3: A Review of Server Binding Mechanisms
Immediate Binding
  Decision about which real server to send the request to is made upon arrival of the TCP SYN packet
Delayed Binding
  Decision about which real server to send the request to is made after the TCP 3-way handshake is complete
  Decision is based on the information from the client, such as URL, SSL session ID, session cookie, permanent cookie or specific application-related information

## Slide 4: DAM & PIP
Direct Access Mode and Proxy IP’s are used to support delayed bindings
Delayed bindings enabled by moving server processing to the client port
Enables TCP connection splicing

## Slide 5: URL-Based Parsing

## Slide 6: URL Parsing for Web Servers
Optimize resource access and server tuning by separating static and dynamic content requests
Sends requests with specific URLs or URL “sub-string matches” to designated web servers
For instance:
  cgi --> Real servers #1, 2, 3
  jpg and gif --> Real servers #4, 5, 6
Requires TCP connection termination, URL inspection and pattern matching, and session fix-up
Supports HTTP 1.0 and HTTP 1.1

## Slide 7: Summary of URL based SLB
Up to 128 strings of 40 bytes long for URL sub-string matching
Examples of “sub-strings”
  “/product”, matches URL that starts with “/product”
  “product”, matches URL that has the string “product” anywhere in the entire URL

## Slide 8: Challenges in HTTP 1.1
In HTTP 1.0, each request is made over a new connection
HTTP 1.1 allows persistent connections
Open Connection
Send 1st request
Read request
Send response
Receive 1st response
Send 2nd request
Read request
Send response
Receive 2nd response
…etc...
Close connection
Client
Server

## Slide 9: URL Based SLB for HTTP 1.1
“.cgi”
“.bin”
“.exe”
“images”
“.gif”
.jpg”
“/product
“/company”
“/information”
1st Request: GET /www.alteon.com/images/ACEswitch180.gif
forwards request to RIP_1
2nd Request: GET/www.alteon.com/switch/A180.bin
inspects URL and selects RIP_3
terminates connection to RIP_1
establishes connection to RIP_3
forwards request to RIP_3
RIP_1
RIP_2
RIP_3
RIP_4
GET /www.alteon.com/images/ACEswitch180.gif
GET/www.alteon.com/switch/A180.bin
X
Notes: URL Based Web Server Load Balancing
  Selection of server is based on the first HTTP GET URL
  URL of subsequent GETs from the same connection need to be inspected
  Terminates the original connection to the selected real server if subsequent URLs need to be forwarded to other server

## Slide 10: Configuring SLB URL Parsing
Configure as you would for SLB without URL parsing
Enable DAM or specify PIP address(es) on the client port(s)
  If PIP addresses are used, make sure server processing is disabled on the server port
Configure match string, assign to real server and enable

## Slide 11: Configuring URL-Based LB
Define the “sub-string” for matching
  /cfg/slb/url/lb
  add, add sub-string or a path
  rem, removed sub-string or a path
Assign a defined sub-string to the real server
  /cfg/slb/real 1
  addlb, url ID of sub-string defined above
  remlb, url ID of sub-string defined above
Enable URL based LB for Virtual Server:vport
  /cfg/slb/virt #/service <tcp port #>/httpslb e/urlslb

## Slide 12: URL Based Web Server LB
“.cgi”
“.bin”
“.exe”
“images”
“.gif”
.jpg”
“/product
“/company”
“/information”
GET/www.alteon.com/switch/A180.bin
GET /www.alteon.com/images/ACEswitch180.gif
GET /www.alteon.com/product/ACEswitch180.html
Implicit
Load balancing
within the group

## Slide 13: URL Based Web Cache Redirection

## Slide 14: URL Parsing for Caches
Optionally offload overhead from caches by sending only appropriate requests to the caches
  Examine request to see if it is a non-GET request like HEAD, POST, or PUT -- if yes, don't send to cache
  Examine request to see if it is an ASP or CGI request, or a dynamically generated page -- if yes, don't send to cache
  Examine request for cookies -- if present, don't send to cache
Allow tuning by sending requests with specific URLs or sub-string matches to designated caches
Supports HTTP 1.0 and HTTP 1.1

## Slide 15: URL Based WCR
Host B
Host C
Host A
GET /company/images/swiitch.gif
Internet
“/product”
“information”
“images”
GET /product/ACEswirch180.html
Web Cache Redirector
GET /www.hostc.com/cgi-bin/script.bin
Non HTTP GET
GET /company/information.html
GET /http://finance.yahoo.com/q?s=hwp%2C+ibm%d=v1
Implicit
Load Balancing
within the group

## Slide 16: Summary of URL based WCR
Up to 32 URL expressions, each 8 bytes long for non-cacheable content types
Up to 128 “strings” of 40 bytes long for URL “sub-string” matching
Possible actions for each Web request are
  Forward to origin server for non-cacheable items
  Redirect to appropriate cache server (group) based on a “sub-string” matching
Examples of “sub-string” are
  “/product”, matches URL that starts with “/product”
  “product”, matches URL that has the string “product” anywhere in the entire URL

## Slide 17: Content-Intelligent Load Balancing Customer applications
Ability to define cacheable domains
  Configure domain pages that should not be cached
Cache redirection based on domain names
  Redirection based on domain name, e.g.: “.com” redirect to server group 1 and all others to server group 2
URL Hashing
  Requests for each unique URL be sent to the same server
  Takes advantage of server memory and caching to optimize server efficiency

## Slide 18: Non-Cacheable Content Types
Switch pre-configured with 13 non-cacheable items
Pre-configured non-cacheable items are dynamic content file extensions or dynamic URL parameters
Examples of pre-configured non-cacheable items
  Dynamic content: cgi, .cfm, .asp, bin, cgi-bin, shtml, .htx, .exe
  Dynamic URL parameters: +, !, %, =, &
Pre-configured non-cacheable items can be modified/deleted

## Slide 19: HTTP Content Based WCR
Host B
Host C
Host A
Internet
“.org”
“.net”
“.com”
Web Cache Redirector
.sg
.jp
.hk
Notes: UURL Based Web Cache Redirection
SSelection of cache for cacheable content or forwarding to origin server for non-cacheable content in based on the first HTTP GET URL
TTerminates the original connection to the selected cache server or the origin server, if subsequent URLs need to be forwarded to other caches or directly to the origin server
Adding Web cache redirection to a transparent proxy cache solution eliminates the drawbacks of transparent proxy without redirection. Much of this is due to the fact that the cache is moved out of the data path and network functions such as examining each packet to determine which are for HTTP and performing network address translation are offloaded from the cache to the redirector.
Web cache redirection is generally run on a networking device such as a LAN switch or router. Because the packet examination is by a device optimized for examining packets and can therefore do it very fast, there is minimal impact on non-Web traffic. The cache redirector can also remove the network address translation function from the cache. Moving these two functions to the web cache redirector frees up CPU cycles on the cache server for serving web pages -- the job the cache is really supposed to do. Also, removing the network address translation function from the cache means that the cache doesn’t have to be configured with network address translation software. Since transparent proxy already eliminated the browser configuration, adding the redirector brings caching as close to zero administration as possible.
Using a cache redirector that is separate from the cache server allows the client load to be spread over multiple caches, while directing requests for content to the cache holding that content. This increases hit rate which, in turn, decreases WAN traffic and user response time. Also, because the cache redirector is aware of the different physical caches, if multiple caches have been deployed, it can perform health checks on the caches and direct requests for web pages only to healthy caches. Further, redundant redirectors can be deployed, eliminating any single point of failure and yielding the ultimate in uptime.
The biggest negative to web cache redirection is that the redirector must be purchased and deployed, increasing modestly the expense of the solution and incurring some additional administration because of the need to configure the redirector.

## Slide 20: URL Based WCR for HTTP 1.1
Host B
Host C
Host A
GET /company/images/switch.gif
Internet
“/product”
“information”
“images”
GET /product/ACEswitch180.html
Web Cache Redirector
X

## Slide 21: WCR without URL Hashing
Host B
Host C
Host A
Internet
The rest of the
requests
All www.yahoo.com
requests
Web Cache Redirector
.sg
.jp
.hk
All www.excite.com
requests

## Slide 22: WCR with URL Hashing
Host B
Host C
Host A
Internet
www.yahoo.com/weather
www.excite.com/map
www.excite.com/weather
www.alteon.com/product
Www.hp.com/product
www.yahoo.com/finance
www.excite.com/voice
www.alteon.com/company
Web Cache Redirector
.sg
.jp
.hk
www.excite.com/mail
www.yahoo.com/map
Notes: Adding Web cache redirection to a transparent proxy cache solution eliminates the drawbacks of transparent proxy without redirection. Much of this is due to the fact that the cache is moved out of the data path and network functions such as examining each packet to determine which are for HTTP and performing network address translation are offloaded from the cache to the redirector.
Web cache redirection is generally run on a networking device such as a LAN switch or router. Because the packet examination is by a device optimized for examining packets and can therefore do it very fast, there is minimal impact on non-Web traffic. The cache redirector can also remove the network address translation function from the cache. Moving these two functions to the web cache redirector frees up CPU cycles on the cache server for serving web pages -- the job the cache is really supposed to do. Also, removing the network address translation function from the cache means that the cache doesn’t have to be configured with network address translation software. Since transparent proxy already eliminated the browser configuration, adding the redirector brings caching as close to zero administration as possible.
Using a cache redirector that is separate from the cache server allows the client load to be spread over multiple caches, while directing requests for content to the cache holding that content. This increases hit rate which, in turn, decreases WAN traffic and user response time. Also, because the cache redirector is aware of the different physical caches, if multiple caches have been deployed, it can perform health checks on the caches and direct requests for web pages only to healthy caches. Further, redundant redirectors can be deployed, eliminating any single point of failure and yielding the ultimate in uptime.
The biggest negative to web cache redirection is that the redirector must be purchased and deployed, increasing modestly the expense of the solution and incurring some additional administration because of the need to configure the redirector.

## Slide 23: Configuring WCR with URL Parsing
Optionally configure proxying
Configure URL parsing

## Slide 24: Configuration of URL Based WCR
Configure application redirection as usual
Enable URL parsing for the redirection filter
  /cfg/slb/filt #/adv/urlp
  Enable or disable
Add/delete/modify non-cacheable content types (option)
  /cfg/slb/url/redir
  add or rem
Define sub-string matching (option)
  /cfg/slb/url/lb
  add, add sub-string or a path
  rem, remove sub-string or a path

## Slide 25: Configuration of URL Based WCR
Assign sub-string to real servers (option)
  /cfg/slb/real 1
  addlb, url ID of sub-string defined before
  remlb, url ID of sub-string defined before
Non-GET Requests (option)
  By default non-GET requests will be forwarded directly to origin server
  Admin can disable it
  /cfg/slb/url/redir/urlal, enable or disable
Cookie in URL (option)
  By default, URLs with cookies sent directly to origin server
  Admin can disable it
  /cfg/slb/url/redir/cookie, enable or disable

## Slide 26: SLB & WCR URL Parsing Summary
URL based parsing allows the user to optimize resources
  Separate static content from dynamic content
  Resources used only where they can be properly processed
Provides URL parsing, Cookie Based Parsing and SSLID parsing