## Slide 1: Global Server Load Balancing

## Slide 2: Advanced GSLB Objectives
Upon completion of the GSLB module, the user shall:
  Understand the advantages of distributed site redundancy
  Understand Alteon’s Global Server Load Balancing approach and advantages
  Understand how DNS supports Alteon’s GSLB approach
  Understand how GSLB selects the best server
  Understand GSLB site failover
  Be able to configure GSLB sites

## Slide 3: Most Distributed Content Sites Today
www1.company.com
www2.company.com
www3.company.com
Internet
Mostly static content on Web, FTP servers
Load and site distribution performed through round robin DNS
  No Site Health Awareness
  No Site Performance Awareness
  No Geographic Awareness
  Cached DNS requests for servers that are down produces “failure to connect” messages

## Slide 4: Alteon Global Load Balancing Users mapped to Closest, Best Performing Servers
B
Content server
Web Servers
3-in-1 switching
Simple configuration
Dynamic site health and performance knowledge on every switch
No added latency
Notes: 3-in-1
  Switching, local and global server load balancing in one device
Simple configuration
  Only switch and DNS configuration required
  No router change, no network reconfiguration
Dynamic site health and performance knowledge on every switch
No added latency
  User origination is determined instantly by DNS request
  Instant handed-off decision making at each site

## Slide 5: A Very Brief DNS Tutorial
User request www.alteon.com results in DNS lookup
Request travels up DNS
  A DNS site returns list of IP addresses to local DNS
Client’s local DNS server sends address for www.alteon.com to client and caches address or list of addresses
www.alteon.com
1
2
3
4
1
2
3
4
5
5
Notes: User types in “www.alteon.com” - browser makes a DNS lookup request to client’s local DNS
Client’s local DNS looks in cache - not there? Request goes up to a root DNS server, and then down to domain owners (“.com” owner --> “.alteon.com” owner)
alteon.com owner receives the request and return an address or list of addresses for www.alteon.com owner
www.alteon.com owner returns an address or list of addresses for www.alteon.com
Client’s local DNS server sends address for www.alteon.com to client and caches address or list of addresses
Note on Local DNS Server Behavior
If the local DNS server has an address for www.alteon.com in cache, it will return that address in response to client queries.
If the local DNS server has a list of addresses for www.alteon.com in cache, it will cycle through addresses in round robin fashion when responding to client queries, if configured to do so.
If the local DNS server does not have an address for www.alteon.com in cache but has an address for the www.alteon.com owner, it will query the owner.
If the local DNS server does not have an address for www.alteon.com in cache but has list of addresses for the www.alteon.com owner, it will query the owner with the shortest response time.
Initially, all response times are set to zero
  If two or more response times are the same, server picks at random
  Each time an address is used, response times of other addresses are decremented slightly

## Slide 6: Global SLB Processes Lots of Things Happening at the Same Time
Each GSLB site generates a global view of health and responsiveness of all GSLB sites
Each GSLB site acts as a DNS server for sub-domain being load balanced
Each GSLB site performs local server load balancing if more than one server is present at the site
Sites redirect traffic if all local servers are down or at maxconns
Notes: Each GSLB site generates a global view of health and responsiveness of all GSLB sites
  Test each other for health and responsiveness
  Exchange information about health and responsiveness
  Determine which sites are healthy and providing best global responsiveness
Each GSLB site acts as a DNS server for sub-domain being load balanced
  Uses global view of site health and responsiveness to determine where to send user requests
Each GSLB site performs local server load balancing if more than one server is present at the site
Sites redirect traffic if all local servers are down or at maxconns

## Slide 7: Technology Keys for Global SLB
Receive DNS request from client’s DNS server
Determine best site/server (one or more)
  Server/service availability
  Geographic location of client vs. server
  Site/server measured responsiveness
  Client response time to server(s)
DNS response directs client request to best site/server
Receive client’s TCP connection request
Redirect client’s TCP connection request if no server available
  HTTP Redirect
  IP Proxy

## Slide 8: Receive DNS Request
User makes browser request
DNS query—from local cache to root DNS server to domain owner
Domain’s DNS server receives the request and hands it off to the DNS server in an Alteon switch
DNS server in an Alteon switch acts as a DNS name server for a particular subdomain - www.alteon.com
Valid DNS responses are cached by the client’s local DNS server
www.alteon.com
Notes: User types in “www.alteon.com” - browser makes a DNS lookup request to client’s local DNS
Client’s local DNS looks in cache - not there? Request goes up to a root DNS server, and then down to domain owners (“.com” owner --> “.alteon.com” owner)
Domin’s DNS server receives the request and hands it off to the DNS server in an Alteon switch
DNS server in an Alteon switch acts as a DNS name server for a particular subdomain - www.alteon.com
  Returns one or more IP addresses as the appropriate place to send the user
  How does it figure out where to send the user? We’ll talk about that next.
Valid DNS responses are cached by the client’s local DNS server

## Slide 9: Determine Best Server: Geographic Evaluation
Rough geographic determination to ensure that requests stay in continental domains if possible
World split up into geographies according to IANA, ARIN and RIPE published IP address allocation lists
GSLB makes first set of decisions based on the region the IP address resides
Notes: Why did we do it this way? Large amounts of memory are needed to store huge user/site preference lists over long periods of time.
So, the first question answered by the switch is “What continent is the user coming from?”

## Slide 10: Determine Best Server: Site/Server Availability and Measured Responsiveness
Each site knows the health and performance of other sites
Allows instant decision-making on client handoff
Notes: Each site executes health and performance checks on each other site, building a matrix of measured response times.
Takes into account server, SLB, router, WAN, etc., performance to ensure that the best performing sites are always picked but not overwhelmed.
Allows instant decision-making to determine where to send the client.
Performance measurement “granularity” will be poor with less than three sites.
Periodic Updates
  Peer site performance behavior
  Local site status information
  Ordered Handoff Table based on periodic updates
Triggered Updates
  Unresponsive site
  Local site unable to respond

## Slide 11: Fair Site Selection
Best performing sites get priority, but are not overwhelmed
Even distributions of requests
Weighted Site Handoff Table
Site Performance Table

## Slide 12: User / Site Decision Flow
1. Client’s DNS request for www.foo.com sent to local DNS
2. Local DNS queries upstream DNS
3. Switch at site C receives DNS request and determines that site B is the best site. Acting as Authoritative Name Server, switch returns site B’s IP to client’s local DNS
4. Local DNS server responds to client with site B’s VIP
5. Client opens application session to 172.168.13.10 (site B)
www.foo.com
205.178.2.2
www.foo.com
172.168.13.10
www.foo.com
162.113.25.20
Site health, response time and throughput
exchanged between
switches on a periodic
or event-driven basis using encoded DSSP
B
A
C
DSSP
Updates
1
4
5
Rank Site %Traffic
1 B 70
2 C 20
3 A 10
DNS
3
2

## Slide 13: Send Request/Client to Best Server: DNS Response
Client makes a DNS request for www.alteon.com
Request from the client’s local DNS eventually gets to switch at a GSLB site
Received on one of the switch’s IP interfaces, not a VIP
Switch evaluates geography and site health and responsiveness and formulates DNS response
The DNS response includes:
  A list of IP addresses
  A configurable TTL value (default of 1)
Client opens TCP connection to that IP address
www.alteon.com
1
2
1
2
3
3
4
4

## Slide 14: Local Site Preference
User requests site
DNS resolves to local GSLB switch
If local site is able to answer request, GSLB site returns local IP address
If local site isn’t able to answer request, GSLB site returns peer IP address
www.alteon.com
1
2
3
4
5
Notes: GSLB relies on DNS servers running in switches at some or all distributed sites
User types in www.alteon.com and hits enter
Browser makes a DNS lookup request to client’s local DNS
Local DNS checks cache -- if not there, request goes to a root DNS server, then to domain (e.g., alteon.com)
Site’s DNS Server receives request and hands off to switch
Switch acts as a DNS Name Server for a particular subdomain - www.alteon.com
  Returns VIP running on switch as address to use as long as the site has at least one healthy server not at max conns
Local DNS server caches address and sends to client
Client sends TCP SYN request to VIP

## Slide 15: Global Server Load Balancing (GSLB) Client Proximity Tables
Challenges with current GSLB implementation
  IANA data is not granular for site selection
  Large ISP partners cannot use their own geographic data to determine GSLB site selection based on client location
Static Client/Site Database
  Allows customization per user environment
  Up to 128 static entries stored on the switch
  Configurable Source Network <--> Site Preference Tables
  E.g
    205.178.13.* prefers Site 1, Site 2
    204.165.*.* prefers site 4, site 2

## Slide 16: GSLB Proximity Tables How it works
1. Client sends request to
local DNS server
2. DNS request sent
to switch
DATABASE FIELDS
<IP ADDRESS> <NETMASK> <VIP_1> <VIP_2>
3.Switch looks at database
and responds
4.Client request forwarded
to nearest location

## Slide 17: Servers down or overloaded? Use HTTP Redirect
www.alteon.com
1
2
Load Balancer allows the TCP connection to complete, and then sends an “HTTP REDIRECT 30x to SITE
Client closes first TCP connection, and opens a new TCP connection to new site
Notes: Client already has the IP address for a site hosting www.alteon.com
Client opens TCP connection to that IP address
Load Balancer at chosen site/server determines that it is not the best server to handle the request
Load Balancer allows the TCP connection to complete, and then sends an “HTTP REDIRECT 30x to SITE xxx.xxx.xxx.xxx” message back to client
Client closes first TCP connection, and opens a new TCP connection to new site
Browser will probably continue to make requests to the original site (its stupid..)

## Slide 18: Servers down or overloaded? Use IP Proxy
1. Client makes request to overloaded site
2. Switch accepts request ; forwards to next best site
3, 4. Switch at site #2 load balanced request to local servers
5. Switch returns data to switch at site #1
6. Switch at site #1 returns data to client.
Internet
Web, POP3 Servers
POP3 Request fulfilled via IP-Proxy
Web, POP3 Servers
1
2
3
4
5
6
Site 1
Site 2
Redirects non-HTTP requests when all servers in a site fail health checks or are at max conns
Notes: This is not triangulation, our GSLB function provides a distributed load balancing approach that is superior to triangulation. IP proxy is a mechanism to increase availability in the event that all servers at GSLB site fail or are saturated.

## Slide 19: Configuration Overview
Configure Alteon switches as Peer Sites
Configure Domain Name Services
  Switch becomes a DNS server for virtual domains being hosted
Peer VIPs (in other switches) become Remote Servers
Switches exchange configuration information through DSSP
  What domains are being hosted by what VIPs, response times, server health, etc
Adding another site …
  Add new Peer Site to existing switches’ configs
  Add new Peer Sites VIP as Remote RIPs on existing switches
Peer Site #1
VIP-1 for www.company.com
Remote Server to Site #2
Peer Site #2
VIP-2 for www.company.com
Remote Server to Site #1
Internet

## Slide 20: Configuring GSLB
Assuming two distributed sites
Configure each switch as you would with local SLB
Activate GSLB with a SWKey obtained from Alteon
  /oper/swkey
Determine a hostname/domain-name to distribute to at least two sites
  www.alteon.com
Configure all appropriate DNS servers for alteon.com to use SW1 and SW2 as name servers for www.alteon.com
  Configure the DNS servers to recognize SW1 (100.5) and SW2 (113.5) as NS records / authoritative name servers for www.alteon.com

## Slide 21: GSLB Configuration (cont’d)
Now, configure GSLB
  In switch 1, config switch 2’s IP-if address as a primary remote switch
  In switch 2, config switch 1’s IP-if address as a primary remote switch; enable
    /cfg/glsb/site #
  /cfg/gslb/on - turn on GSLB
Create Remote Servers, add them to VIPs
  In Switch 1, config the VIP of SW2 as a remote server:
    /cfg/slb/real #/ rip 172.176.113.10 ; remote enable ; enable
    /cfg/slb/group (same as before) /add #
  In Switch 2, config the VIP of SW1 as a remote server:
    /cfg/slb/real #/ rip 192.168.100.10 ; remote enable ; enable
    /cfg/slb/group (same as before) /add #
  In both switches, configure each VIP with the same distributed domain name, and hostname per service
    /cfg/slb/virt/dname alteon.com
    /cfg/slb/virt/service port #/hname www
    (and any additional services like ftp, etc)

## Slide 22: Test GSLB
Execute a browser request to www.alteon.com
Check the stats on each switch to determine which switch handled the request
  /stats/slb/gslb virt
  /stats/slb/gslb group
  /stats/slb/maint
  /stats/slb/virt
  /info/slb
Disable the local real servers on the switch that handled the request
  The switch should HTTP Redirect the request to the other VIP on the other switch

## Slide 23: GSLB Configuration Notes
DSSP runs over HTTP using port 80
  If you want to manage the switch using the Web UI, you must configure the Web UI to use a port other than 80
HTTP redirects can use either the IP address or service name and domain name of the remote site
  Using IP address easier to configure
  Using service name and domain name more cookie-friendly
  Configure using /cfg/slb/gslb/usern e|d command

## Slide 24: GSLB Summary
GSLB provides the user with a distributed site architecture that supports redundancy and increases processing
GSLB configuration
  Set up SLB as usual at redundant sites
  Set up the opposite site as a real server
  Enable the opposite site’s real server as a remote site
  Enable GSLB software key