## Slide 1: Advanced Topics Appendix

## Slide 2: Configuring Large Numbers of VIPs/RIPs
For Web hosting environments, many thousands of web sites may be hosted.
Each web site is assigned its own IP address (to correspond with their own IP domain’s web server name)
Configuring thousands of IP addresses to represent these environments is easy with Alteon’s Web switching products

## Slide 3: Using Address Masking to Increase Virtual Address Space
An imask may be applied to V_IPs and the R_IPs configured in the switch.
This will increase the range of IP addresses that each V_IP, R_IP responds to.
Default mask is 255.255.255.255, which represents a single IP address
For instance, a mask of 255.255.255.0 corresponds to 255 IP Addresses per configured V_IP, R_IP.
Many ISPs use entire subnet address ranges when configuring web servers (I.E. xxx.2 through xxx.254)

## Slide 4: Topology Using Virtual Masking
imask: 255.255.255.128
V_IP #1 : 204.165.121.129 (represents .128-.255)
V_IP #2 : 204.165.130.2 (represents .0-.127)
multi-netted / logical-IF servers
R_IP #1 : 10.10.1.129 (represents .128-.255)
R_IP #2 : 10.10.2.129 (represents .128-.255)
R_IP #3 : 10.10.3.2 (represents .1-.127)
R_IP #4 : 10.10.4.2 (represents .1-.127)
Router interface(s) to the ‘Net
Supporting all the subnets for all V_IPs,
Notes: PING and ARP behavior
Routing using the Switch

## Slide 5: Virtual Masking Rules/Notes
When using masking, contiguous ranges of IP addresses are used based on configured VIPs and RIPs
There is a one-to-one correspondence of VIP IP addresses to RIP IP addresses
The defined IP address for each Real Server is the ONLY IP address which is health checked -- we do not health check the entire range of addresses.
The last octets of the VIP map directly to the last octets of the RIP (based on mask)
  Assume a mask of 255.255.255.0
  V1:192.168.20.125 maps to
    R1:10.230.11.125
    R2:10.88.55.125
VIPs are the IP addresses advertised via DNS
Works best with IP routing or static NAT running in the switch -- servers are usually on a private subnet (10.x) with each server having at least one reachable admin address

## Slide 6: VIPs with Many Services
Useful to be able to configure many TCP/UDP services associated with a single virtual IP address
You can now configure multiple virtual servers (/cfg/slb/virt nnn) with the SAME IP address. So, (virt 1 .. virt nnn ) can be configured with the same IP addresses, and (8) unique services apiece.

## Slide 7: Default Gateway Load Balancing
Works with SLB at the same time. All egress traffic is statistically load balanced among up to four default gateway routers.
Similar to how we do it with Redirection, we ensure IP Flows are properly maintained between unique IP Sources and Destinations
Required to ensure no out-of-order frames are transmitted out the WAN or LAN backbone
We don’t care (nor can we control) how frames ingress from the WAN to the switch
All Routers must have the ability the get to all destinations. Out-of-balance routing tables between the routers (from different network providers, for instance) will create problems.