## Slide 1: VPN Load Balancing

## Slide 2: VPN Load Balancing Objectives
Upon completion of this module, the user shall be able to:
  Understand what a VPN is
  Understand how VPN load balancing works
  Understand VPN load balancing configurations supported in WebOS 8.3
  Understand how VPN load balancing effects other applications

## Slide 3: What is a VPN?
Provides secure communication over a shared link
  A virtual tunnel is created between the client and the network
  Data traversing the shared link is encrypted
  VPNs can provide firewall features
    NAT
    Encryption
    Authentication

## Slide 4: How Does VPNLB Work?
Like FWLB, ingress and egress traffic must travel through same device
Hashing on SIP and DIP is not always possible
  DIP is encrypted in incoming datagrams
  SIP and DIP may change as data traverses from clean side to dirty side and back
Session state is used to support VPNLB
  State is recorded on frames entering and exiting the switches in the Alteon VPNLB configuration
Notes: Web OS 8.3 supports load balancing on up to 255 VPN devices.

## Slide 5: Load balancing basics…
Primarily two ways to load balance traffic through an Alteon switch
  Sessions load balanced via a VIP and virtual service
  Session load balanced via a redirection filter
  Session entries created by the “client” port (SLB) or by the filtered port (FWLB, WCR)
    Session entries actually live on the “Designated Port” when using VMA.
Any packets entering a L4 port are checked against the cached session table.
  If a session entry exists, perform the cached action.
    SLB -> NAT to/ from RIP
    Filters -> NAT/ Redirect to RIP/ Allow/ Drop…

## Slide 6: Load balancing basics… - Sessions load balanced via a VIP and Virtual Service
Virtual IPs (VIPs)
  represent the web site
  live on the Alteon switch
Virtual Services (ie HTTP)
  associated with a VIP
  mapped to Real Servers (RIPs) via Server Groups
Session entries
  Created by client processing
  Indexed by SrcIP/ Src Port
  Cached on VMA “Designated Port”
Client
Real Servers (RIPs)
VIP
Client Processing
Server Group

## Slide 7: Load balancing basics… - Sessions load balanced via Redirection Filters
Many different “transparent redirection” applications
  Web cache redirection
  Firewall Load Balancing
  Gateway Load Balancing
  Many others…
Redirection Filters
  Define match/ selection criteria
  Traffic redirected to a “server” group
    Usually not actual “servers”
  One or more devices such as caches accept traffic forwarded to them
Session entries
  Created by filter processing
  Cached on VMA “Designated Port”
  Indexed by Src IP/ Src Port or Src/ Dest IP depending on the application.
Caches, etc
Redirection Filter
Server Group
Network
Network

## Slide 8: Load balancing basics… - Firewall LB – a variation on Redirection Filters
Creative use of redirection filters
  Traffic load balanced across multiple FWs
  Health checks for all paths between switches.
  Bi-directional transparent traffic redirection.
Same LB algorithm runs on both clean and dirty switches
  Must use a Src/ Dest IP hash.
  Needed to maintain “stateful” session forwarding in both directions.
Session entries
  Created by filter processing
  Cached on VMA “Designated Port”
  Must be indexed by Src/ Dest IP.
Redirection Filters
Load Balanced Paths
Clean Network
Dirty Network
Load Balanced Paths
Firewalls

## Slide 9: IPsec Tunnel Mode Packet Format
User IP header is embedded within the packet payload
  Usually encrypted.
Outer IP header is used to transmit packets to/ from the VPN client and VPN gateway
The VPN gateway validates the headers/ payload and strips outer headers off the packet to leave the original IP frame.
New IP
Header
IPSec
Header
Data
IP Header
Data
Original IP
Header
Optional Encryption
User Packet
IPsec Packet
encapsulated into

## Slide 10: VPNs Break FWLB!
FWLB must use HASH metric on clean and dirty switches to maintain session state!
But VPN inside and outside addresses are different!
Session state cannot be maintained where the addresses change through the FW/ VPN gateways!
Redir Filter
Clean Network
Dirty Network
VPN/ Firewalls
Redir Filter
VPN/ IPsec packets using “outside” addresses
Decrypted packets using “inside” addresses

## Slide 11: What is VPN Load Balancing?
Introduced in WebOS 8.3
Creates a reverse session entry in the session table
  VPN LB performs a lookup into the session table (just like any other L4 feature) but with the Src/ Dest IP addresses/ ports reversed.
    If an entry exists, no additional action.
    If no entry exists, the "reverse" session entry is created.
Sessions returning to the switch are checked against the session table, and if they match an existing session entry they are forwarded to the original source
Requires that filtering be enabled on the server/ VPN gateway port(s) of the switch to force the session to be checked against the session table.

## Slide 12: How does it work?
Inbound sessions hits redirection filter on dirty switch and are LB’d to one of the VPN GW based on some metric
  Normally HASH but it is only important that a session entry is created which will match future inbound sessions and will forward to the same VPN GW.
VPN GW strips outer headers.
Clean switch VPN LB port creates a reverse session entry in the session table using the “inside” headers.
Returning session hits port filter on clean switch. Session table checked and existing entry found from step 3.
Session forwarded to originating VPN device.
VPN headers added and session forwarded to client.
Session hits VPN LB port on dirty switch. The session table is checked but as an entry already exists no action is needed.
Redir Filter
Clean Network
Dirty Network
VPN/ Firewalls
Redir Filter
vpn ena
vpn ena
vpn ena
vpn ena
1
2
3
4
5
6
7

## Slide 13: What is needed to set it up?
Enabled VPN load balancing on ports connected to the VPN device(s).
  /cfg/sl/port x/vpn ena
Enable filter processing on the clean/ dirty side of the switches
  i.e the non-VPN ports to force a session table lookup.
  /cfg/sl/port y/filt ena
VMA must be enabled.
  Needed to find the cached reverse session entries.

## Slide 14: How VPN LB effects other applications
Returning outbound traffic to the same router which delivered the sessions inbound.
  Symmetric session flows
NATing Firewalls
Allows metrics other than HASH for FWLB
Allows metrics other than HASH for iSD-SSL
Supports client IP spoofing for cache redirection.

## Slide 15: Symmetric Session Flows
Inbound flows will be returned via the same router
  Great for dual ISP scenarios
Outbound sessions forwarded normally
  Based on default GW configs including health checking of remote ISP router/ WAN link.
filt ena
vpn ena
vpn ena

## Slide 16: NATing Firewalls
Customers often use private address space within their networks and then NAT their internal addresses to one or more public addresses.
FWLB uses HASH metric on clean and dirty switches to maintain session state!
But NAT’d inside and outside addresses are different!
Session state cannot be maintained where the addresses change through NAT!
Redir Filter
Clean Network
Dirty Network
NATing Firewalls
Redir Filter
Public addresses
Private internal addresses
VPN LB fixes NATing Firewalls!
vpn ena
vpn ena
vpn ena
vpn ena

## Slide 17: FWLB with metrics other than HASH
FWLB normally uses the HASH metric on clean and dirty switches to maintain session state!
Session distribution not always ideal using HASH
Redir Filter
Clean Network
Dirty Network
VPN/ Firewalls
Redir Filter
vpn ena
vpn ena
vpn ena
vpn ena
Leastconns
Leastconns
VPN LB allows LEASTCONNS or ROUND ROBIN while maintaining session state !

## Slide 18: Leastconns for iSD-SSL
iSD-SSL server group
Redir SSL to iSD group
Redir pseudo-SSL to iSD group
Must use HASH Metric
Can use LEASTCONNS metric with VPN LB
vpn ena
iSD-SSL requires the use of the HASH metric on the iSD server group to ensure that sessions are consistently mapped to and from the same iSD
  Inbound SSL from the client
  Server traffic to the iSD to be re-encrypted
Can use VPN LB on iSD server group and simply enable filtering on the server ports to map traffic back to the correct iSD

## Slide 19: Cache Client IP Spoofing
Caches normally use own IP address when requesting content on behalf of client
  Can break IP based authentication schemes – MSN
Most commercial caches support the ability to spoof the client IP address
  Previously not possible to identify spoofed client sessions and return them to the cache.
To Content
Client
1 - Client request redirected to cache
2 - Cache retrieves object from source
3 – Cache forwards object to client
VPN LB provides a way to identify spoofed sessions from the cache and return them correctly to the cache without impacting other client traffic.
  Needs filter enabled on host side of switch.
  VPN enabled on cache port(s)
vpn ena
filt ena

## Slide 20: Caveats
Must enable VMA (on by default)
Ports with VPN LB enabled cannot have filters enabled
Will not support Active-Active configurations.
  Inbound/ outbound sessions must transit the same switch.
Cannot use NAT filters on the same switch
DAM cannot be used where VPN LB enabled on a client port.
  Creates designated port mismatch for real server and VIP sessions.
Cannot use VPN LB with iSD-SSL on clean side of an FWLB switch
  Conflict between VPN LB and FWLB filters on same ports.

## Slide 21: VPNLB Configuration
Two configurations supported
  Client to VPN
    Remote user to corporate network
  VPN to VPN
    Secure link between corporate offices
CLI menu
  /cfg/slb/port #/vpn e|d
    Enable or disable VPN processing on the port
    Ensure that filtering is enabled on a port that is not VPN LB enabled

## Slide 22: Summary
VPN LB adds another powerful feature to WebOS
Provides much needed support for VPN LB and NATing firewalls.
Beware that not all VPNs are created equal.
  A number of different flavors.
  VPN LB works well with solutions using a cluster or virtual IP address to represent a load sharing group of VPN gateways.
Alteon has tested with Checkpoint VPN/ FW-1
Alteon has tested with Contivity
  Need to create secondary addresses via Contivity CLI.

## Slide 23: VPNLB Summary (con’t)
VPNs provide secure communications over a shared link
200+ VPN devices can be load balanced
Configuration is similar to FWLB