## Slide 1: Bandwidth Management

## Slide 2: Bandwidth Management (BWM) Objectives
Upon completion of this module, the student should be able to:
Discuss Alteon’s implementation of BWM and specific BWM applications
Configure BWM on Alteon switches to include:
  Defining policies
  Setting up contracts
  Setting SLA limits

## Slide 3: Bandwidth Management Why Should I Care?
Website managers can allocate a portion of bandwidth to specific users or applications.
This enables numerous applications:
  Usage-based services for Hosters and ISPs
  Allows Hosters/ISPs to “cut off” heavy bursters
  Preferential services for portals and eCommerce sites
  QoS for different content types with different jitter/loss requirements
  Security management

## Slide 4: What’s Unique About Alteon’s Bandwidth Management?
Different from IP-based QoS/CoS
  Most QoS/CoS systems use IP TOS to prioritize delivery
Alternatives used before Alteon’s BWM
  Settle for IP TOS-based QoS
  Use Committed Access Rate (CAR) on Cisco 75xx routers
  Use bandwidth management appliances that have performance limitations
Notes: How is this different from IP-based QoS/CoS?
  Most QoS/CoS systems use IP TOS to prioritize delivery
    No precise bandwidth metering and control per traffic class
    Hardware-based queuing limits support to less than a dozen queues
What did customers do before Alteon bandwidth management?
  Settle for IP TOS-based QoS
  Use CAR on Cisco 75xx routers
  Use bandwidth management appliances that have performance limitations

## Slide 5: BWM Terms
Class of Service - Typically either 802.1p or TOS, best effort
Quality of Service - ATM is the only thing that REALLY does this
Bandwidth Management - Controlling the actual bandwidth used by enforcing a least rate/peak rate/both rates
Rate Shaping - TCP frame rate manipulation (i.e. Packeteer)
Class-Based Queuing - Basically bandwidth management

## Slide 6: BWM Terms (cont’d)
Policy
  Set of rules that determine the limits and packet precedence
Contract
  Amount of bandwidth allocated or assigned to user
  256 (AD3/180e) or 1024 (AD4/184) contracts per switch
Precedence
  Each contract has a precedence number
  Default precedence(VIP, filter, VLAN, source port) used if no multiple classification precedence is specified
Filter based
  Any filter parameter can be used for bandwidth management - IP source address, IP destination address, port numbers

## Slide 7: Key Concepts in Class-Based Queuing (CBQ)
Classification of incoming packets
Selection of packets to remove from queue
Overlimit Action related to burst traffic
Estimation of packet flow
Notes: Classification of incoming packets
  Rules determine which queue to direct packet
  Alteon classifies on anything used for filtering
Selection of packets to remove from queue
  Alteon uses a virtual clock to select packets from one of multiple queues to place on the wire
Overlimit Action
  Queue overflow
Estimation is the process of calculating the current rate of the packet flow on the outbound port and the MP. This feeds back into the selection algorithm

## Slide 8: Key Concepts in BWM Implementation
Contract creation includes classification and bandwidth policies
  256 contracts per AD3/180e, 1024 contracts per AD4/184
Classification policies
  Limit the traffic from the server farm
  Classification policy that groups frames
Bandwidth policies
  Committed Information Rate (or Reserved Rate), Soft Limit, Hard Limit
Notes: One or more Contracts created per switch. Each contract includes:
  Bandwidth policy that specifies usage limits
  256 contracts per AD3/180e, 1024 contracts per AD4/184
Classification policies
  Purpose: limit the traffic outbound from the server farm
Bandwidth policies: Committed Information Rate (or Reserved Rate), Soft Limit, Hard Limit
  64 Bandwidth policies per switch. Often based upon a hoster’s or co-location provider’s rate structure

## Slide 9: BWM Implementation Class-Based Queuing (CBQ)
No direct competitors, though the following have products which may be used in some of the same applications
  Cisco CAR
    Committed Access Rate --- traffic shaping
  Lucent Xedia
    QoS VPN routers
  Packeteer
    PacketShaper BWM products
  Extreme
    L1-4 “QoS”

## Slide 10: Introduction to BWM Framework
CLASSIFICATION
POLICY
USER IDENTITY
  Cookies, IP address
APPLICATION TYPE
VIRTUAL SERVER
REAL SERVER
URL
RESERVED RATE
SOFT LIMIT
HARD LIMIT
BANDWIDTH ALLOCATION
Notes: This is a graphical representation of the key elements of BWM:
Classification of frames, policy creation and bandwidth allocation.

## Slide 11: Bandwidth Management How Does It Work?
Bandwidth management based on traffic classes and bandwidth policies:
  Multiple levels of bandwidth per traffic class
  Traffic queuing
  Theoretical Departure Times (TDT)
Server Link
VIP A
RIP 2
RIP 1
VIP B
Notes: Bandwidth management based on traffic classes and bandwidth policies:
  Multiple levels of bandwidth per traffic class
    Guaranteed bandwidth,soft ceiling,hard ceiling
  Traffic is queue’d up
    Each frame placed in a managed buffer and placed in the queue for its contract
  Transmit pacing based on Theoretical Departure Times (TDT)/queue
    TDT adjusted between CIR/HL based on queue fullness and available outbound bandwidth

## Slide 12: Frame Classification
Layer 2/3 attributes
  Physical Port
  VLAN
  IP source address
  IP destination address
Layer 4 attributes
  VIP
  Group of VIPs
Application attributes
  TCP Port number
  Protocol type
  Content based using URL
  User based using cookies (TBD)
Combinations
  Group VIPs
Notes: Frames can be classified on ingress on any of the following parameters:
Layer 2/3 attributes
  Physical Port
  VLAN
  IP source address
  IP destination address
Layer 4 attributes
  VIP
  Group of VIPs
Application attributes
  TCP Port number
  Protocol type
  Content based using URL
  User based using cookies (TBD)
Combinations
  Group VIPs

## Slide 13: Bandwidth Policies and Contracts
  Bandwidth policies
    Policies based on ports, L2/3/4 filter rules
    Cookie and URL strings classification
    Nesting of rules allowed
  Bandwidth contract per traffic class
    Committed Rate/Soft Ceiling/Hard Ceiling (CIR/SL/HL)
    Optional queue depth and IP TOS setting
Server Link
VIP A
RIP 2
RIP 1
VIP B

## Slide 14: Bandwidth Policies – A Trio of Limits
Committed Information Rate or Reserved Rate
  Guaranteed rate
  Sum of CIRs must not exceed link capacity
Soft Limit
  Paid for rate
  If bandwidth available, this rate is used
  IP TOS bits are changed when soft limit is reached
Hard Limit
  “Never exceed” rate
  Drop frames when hard limit is reached
  Charge for any amount above soft limit
Committed Rate
Soft Limit
Hard Limit

## Slide 15: Frame Flow
Classification
AceSwitch
SP
SP
SP
Backplane
BW Mgt Queues

## Slide 16: Virtual Clocks and TDT
Queue 1
Queue 2
Queue 3
Queue 4
Time

## Slide 17: Bandwidth Management Other Features
Queue Sizing
  Adjust queue sizes for delay sensitive vs. drop sensitive traffic
Accounting per traffic class
  PULL (SNMP) and PUSH (SMTP)
IP TOS setting above SL rate
  Enables end-to-end QoS
IP TOS bit filtering and rewrite based on L2/3/4 attributes
  Traffic redirection based on IP TOS field
Server Link
VIP A
RIP 2
RIP 1
VIP B
Notes: TOS byte:
Uses IP precedence field (3 bits) for drop preference.
Uses TOS field (4 bits) for delay indication.
Defines diff-serv semantics *only* -- leaves implementation details to implementors (both vendors & users).
How drop preference might be used:
Packet marking can either be done by end-system (ingress passive) or policed by first-hop router (ingress active).
Preferential drop mechanism might be an “enhanced” RED, or Weighted RED, or similar mechanism (more thought required for non-adaptive flows -- shaping may be required).
How delay indication might be used:
Packet marking can either be done by end-system (ingress passive) or policed by first-hop router (ingress active).
Packets designated as belonging to a specific delay class could be mapped to a particular CBQ queue for transmission priority.
Delay indication provides *NO* a prior knowledge of end-to-end delay, jitter, etc.

## Slide 18: Bandwidth Management For Security
Broadcast/ Multicast
CIR = 10 SL = 30 HL = 50
Internet
Intranet
SYN & IP Options
CIR = 2 SL = 2 HL = 5
NAT
TCP flag filtering
Unknown Socket #’s
CIR = 2 SL = 10 HL = 10
BW Contracts:
Prevent DOS attacks by flooding of “necessary evil” packets
Prevent potential outgoing DOS attacks
Augmented by other Web switch security features (i.e., ACL, NAT, FWLB)
Notes: Prevent DOS attacks by flooding of “necessary evil” packets
  Rate limit TCP SYN, Ping and other disruptive packets
  Alert/log network manager when Soft Limits exceeded
Prevent potential outgoing DOS attacks
  Rate limit applications using unknown port numbers
Augmented by other Web switch security features
  Combine with ACL to prevent undesirable packets, e.g.: IP options, certain ICMP message types, etc
  Combine with NAT to hide internal addresses
  Combine with firewall load balancing for most robust security enforcement

## Slide 19: Bandwidth Management For Fairness
Internet
Dialup Customers
Dial up:
CIR = 5 SL = 20 HL = 20
Prevent heavy bursters from locking out other users
  DSL
  Flash crowds
  FTP
  Napster
Improve customer satisfaction
Broadband Customers
Video Download:
CIR = 30 SL = 60 HL = 60
Notes: Prevent heavy bursters from locking out other users
  Customers using broadband access (e.g., DSL) from blocking dialup customers
  Customers from same hosting facility locking out each other due to flash crowd
  FTP from locking out Telnet
  Rate limit Napster and similar applications
Improve customer satisfaction
  Minimize help desk calls
  Help enforce SLAs

## Slide 20: Bandwidth Management For Preferential Services
A.com
Preferential services - based on source IP blocks, applications, URL types and cookies
Usage-based services - Usage charges based on CIR, SL and HL agreements in SLAs
B.com
VIP 100.2.16.3
CIR = 10 SL = 30 HL = 50
VIP 100.2.16.2
CIR = 5 SL = 15 HL = 30
Notes: Preferential services
  Based on source IP blocks, applications, URL types and cookies
  Augment with IP TOS marking
  Useful for eCommerce sites
Usage-based services
  Flat charges by CIR or SL
  Usage-based charges between SL and HL
    Billable based on burst size
  Useful for NSPs, shared hosting and managed services hosting

## Slide 21: Key Steps in Configuring BWM
BANDWIDTH ALLOCATION
2. ADMIN CONFIGURES POLICY AND CONTRACT
1. USER BUYS A
CONTRACT (e.g. a
VIP)
3. CLASSIFICATION IS DONE ON INGRESS PORT
4. BANDWIDTH MANAGEMENT ON EGRESS PORT
- OVER SOFT, SET TOS=OTOS
- UNDER SOFT, SET TOS =UTOS
5. TOS VALUE AFFECTS ROUTER BANDWIDTH

## Slide 22: Configuring BWM
Configure SLB as usual
On the switch, select a BWM contract and name (optional)
  /cfg/bwm/contract 1
  BW Contract 1# name <name>
Set the precedence for the BWM contract
  BW Contract 1# prec <1-255>
Select BWM policy
  /cfg/bwm# policy <1-64>
Set hard, soft and reserve limits (Mbs)
  Policy 1# hard 6
  Policy 1# soft 5
  Policy 1# resv 4

## Slide 23: Configuring BWM (cont’d)
Set the buffer limit for the policy
  Set as a multiple of packet size
  /cfg/bwm/policy 1# buffer <8192-128000> <32640>
Set the classification policy
  /cfg/slb/virt 1/service <2-65538>/cont 1 (Assign contract 1 to virtual server 1)
  /cfg/slb/filt 1/adv/cont 1 (Assign contract 1 to filter 1)
Enable BWM
  /cfg/bwm/on
Apply and save

## Slide 24: Classification Configuration
Source port
  /cfg/port <port #>/cont<contract#>
  /cfg/trunk <1-4>/cont<contract#>
VLAN
  /cfg/vlan <1-4096>/cont<contract#>
Filters
  /cfg/slb/filt <1-224>/adv/cont<contract#>
Virtual services
  /cfg/slb/virt<1-256>/service <2-65536>/cont<contrac#>

## Slide 25: URL-Based BWM What it gives you
The ability to allocate bandwidth based on type of request
The ability to prioritize transactions or applications
The ability to allocate bandwidth for WCR

## Slide 26: Configuring URL-Based BWM
Define load balancing path or string
  /cfg/slb/url/lb/add path or string
Allocate bandwidth for each path
  /cfg/slb/url/lb/cont URL pathID “ANY” is #1 Contract #
Configure a real server to handle the request
  /cfg/slb/real #/layer7/addlb # - “ANY” is #1
Enable DAM or use proxy IPs
  /cfg/slb/adv/direct e
Turn on URL-based load balancing on virtual server
  /cfg/slb/virt #/service <tcp port #>/httpslb e/urlslb
Turn on SLB

## Slide 27: HTTP Header-Based BWM
Gives the administrator the ability to allocate bandwidth based on header value
  Browser type
  Cookie value
Notes: HTTP header-based BWM allows website managers to allocate bandwidth based on header value. Thus, they can allocate bandwidth based on browser type, cookie value, etc.

## Slide 28: Cookie-Based BWM
Prevents network abuse by bandwidth hogging users
Allows for the creation of tiered service levels
Requires DAM or use of proxy IPs

## Slide 29: BWM Summary
Alteon’s bandwidth management allows the administrator to allocate a portion of bandwidth to specific users or applications.
BWM applications include:
  Usage-based services
  Controlling heavy bursters
  Preferential services for portals and eCommerce sites
  Security management
Reviewed BWM configurations
  Contract
  Policy
  Limits
  Classification