## Slide 1: Advanced VRRP

## Slide 2: Advanced VRRP Objectives
Upon completion of the Advanced VRRP module, the user shall:
  Understand VRRP interfaces
  Understand priorities and preemption
  Understand interface sharing
  Understand flow restrictions with sharing
  Understand tracking
  Understand broadcast loops from fully meshed VRRP networks
    VLAN solution
    STP solution
  Understand stateful failover

## Slide 3: High Availability in Web OS
Alteon Switch Redundancy
  Supports hot standby, active-standby and active-active configurations
  Supports Virtual Router Redundancy Protocol (VRRP – RFC 2338)
  Supports Alteon extensions to VRRP
VRRP
  Allows multiple routers to be active at the same time
  Supports layer 3 redundancy only
Alteon extensions to VRRP
  Virtual Server Routers (VSRs) for VIP (L4) redundancy
Stateful Failover of L4 and L7 Persistent Sessions
  If active switch fails during transaction, stateful information is preserved, and action is transparent to users

## Slide 4: Layer 3 Active-Active Redundancy (Virtual Default Gateway)
Physical L3 Interfaces
if #1 = 10.10.10.11
if #2 = 10.10.20.11
Internet
Server 3
IP #3 = 10.10.20.3
IP #4 = 10.10.20.13
DefGW = 10.10.20.100
Physical L3 Interfaces
if #1 = 10.10.10.10
if #2 = 10.10.20.10
Server 1
IP #1 = 10.10.10.1
IP #2 = 10.10.10.11
DefGW = 10.10.10.100
Active “Virtual” L3 Interfaces
10.10.10.100
10.10.20.100
Server 2
IP #1 = 10.10.10.2
IP #2 = 10.10.10.12
DefGW = 10.10.10.100
VIR=L3 Interface
Notes: L3 Active Active Redundancy provides a survivable default gateway that can forward packets. Note the server’s default gateway configurations. Because the servers are configured to use the virtual default gateways instead of an individual switch interface, if there is a casualty on the master switch, the backup switch will be able to forward packets without loss of service

## Slide 5: Layer 4 Active-Active Redundancy (Virtual VIP)
Active VIP #1
VIP = 205.178.13.100
Active VIP #2
VIP = 205.178.13.200
…….
Internet
Active VIP #1
VIP = 205.178.13.100
Active VIP #2
VIP = 205.178.13.200
VIPs on both switches
are active at the same
time
VSR=VIP
Notes: Due to sharing the L4 interface, both switches are able to process VIP packets that arrive at the switch. If the master switch becomes inactive, the backup switch will continue to process packets, ensuring the L4 packets continue to flow to the servers.

## Slide 6
Master Switch Selection
VRIP = 226.13.254.2
L3 Interface = 226.13.254.2
Priority = 255
VRIP = 226.13.254.2
L3 Interface = 226.13.254.1
Priority = 105
VRIP = 226.13.254.2
L3 Interface = 226.13.254.3
Priority =100
VRIP = 226.13.254.2
L3 Interface = 226.13.254.4
Priority =100
1
2
3
4
First in line for master
Second in line for master
Third in line for master
Fourth in line for master
Notes: Priority
  Used to determine which is the master router
  Ranges from 1-254 for renters
  Per standard, owner’s priority is 255
  Default setting is 100
  VRRP router with highest priority will be the master
Preemption
  Allows a switch to assume master router responsibilities if its priority rises above the current master router’s priority
Based on the VRRP parameters set above, the switches would negotiate between themselves to see which switch would become master at any point.
As you remember from the basic VRRP configuration class, only the master switch sends out VRRP advertisements.
In the above example, the switches would negotiate between themselves and switch 2 would become master due to the fact that it has the highest priority. Switch two obtains the highest priority based on the fact that its L3 interface is equal to the VRIP address, making it the IP address owner. Since it’s the IP address owner, the switch’s priority is automatically set to 255.
If switch 2 fails, the remaining three switches would negotiate with each other. At that point, switch 1 would become master due to it having the next highest priority of 105. This priority was set by the switch administrator.
If switch 2 should fail, switch 4 would become master become master. Even though switch 3 and switch 4 have the same default priority of 100, switch 4 has the higher L3 interface address, which is used as the tie breaker.
With preemption enabled, if any of the higher priority switches come back on line, that switch reacquires the master status.
If preemption is not enabled on the switch, it will only relinquish master if it fails.

## Slide 7: What is Sharing Interfaces?
Active Active is the sharing of the same Virtual Interface Router and the same Virtual Server Router interfaces on two or more switches
  A VSR is defined as a L4 interface
Allows L4 redundancy in the case of switch failure
Allows for simultaneous processing of L4 frames on two or more switches supporting the same VSR
  Backup switch processes L4 frames that are sent to it
What Does Sharing Get You?
  Increased processing for peak session requests
  Confidence in backup networks

## Slide 8: How Does Active-Active Work?
VIP = VSR 216.134.44.8
Active Master
VIP = VSR 216.134.44.8
Active Backup
4 hops to VIP
5 hops to VIP
1 hop to VIP
1 hop to VIP
Sharing enabled on both switches
Notes: Based on the router protocols, individual routers will have different hops to the two VRRP interfaces.
Since the Master VR ARPs for VIP 216.134.44.8 requests, all attached network devices will know what they have to do to get to the VRRP.
In the example, each router in the separate Autonomous Systems will have different ways of getting to the VIPs. Router AS1 will have two routes to the VIP: 1 hop directly connected or 5 hops through router AS 39. Router AS39 will also have two ways: 2 hops through the backup switch and 4 hops through router AS1.

## Slide 9: How Does Active-Active Work?
AS 1
AS 39
VIP = VSR 216.134.44.8
Active Master
VIP = VSR 216.134.44.8
Active Backup
Client 1 HTTP Request to VIP
1 hop
5 hops
Sharing enabled on both switches
Notes: If a client that is connected to router AS1 makes an HTTP request to the 216.134.44.8, the router will forward the request to the VIP by the smallest number of routers. In this case, that would be the route directly connected. The Master would see the L4 request and process the frames, making the best server decision and forwarding it to the appropriate server.

## Slide 10: How Does Active-Active Work?
AS 1
AS 39
VIP = VSR 216.134.44.8
Active Master
VIP = VSR 216.134.44.8
Active Backup
Client 2 HTTP Request to VIP
1 hops
4 hops
Sharing enabled on both switches
Notes: If a client that is directly connected to the router AS39 makes a HTTP request to the VIP, the router would decide which route was the closest. It would select the hop through the backup switch and forward the VIP request to the switch to forward to the Master switch. The backup switch would recognize that it was capable of processing the L4 frames and would make a best server switching decision, forwarding the packets to a real server versus forwarding it to the master switch for processing.

## Slide 11: Flow Restrictions with Sharing
When using sharing, you must ensure that frames reach a maximum of one switch
  Frames that reach switches simultaneously will cause over processing of L4 frames
Use STP or VLANs to stop simultaneous processing of L4 frames

## Slide 12: Sharing Interfaces Simultaneous Frame Processing
VIP = VSR 216.134.44.8
Active Master
VIP = VSR 216.134.44.8
Active Backup
Hub
Hub
Single Client HTTP Request
Notes: If the user does not ensure that frames do not reach the switches simultaneously, there is the possibility that frames may be processed more than once.
In the above example, a single client request reaches the hub above the Alteon switches running Active Active VRRP. The hub will broadcast the VIP request out all its ports. Both switches will receive the VIP requests simultaneously and process them simultaneously. They will then be sent to servers that will process the HTTP request and return multiple responses to the client.
Obviously, this is an undesireable situation. Simultaneous frame processing can be eliminated with Spanning Tree Protocol or with VLANs.

## Slide 13: Sharing Interfaces Frame Flow Restrictions with STP
VIP = VSR 216.134.44.8
Active Master
VIP = VSR 216.134.44.8
Active Backup
Single Client HTTP Request
X
Block Correct Link
Notes: In order to prevent simultaneous processing of frame, the user can apply Spanning Tree Protocol to ensure that frames only reach the master switch to be processed. The user would set the bridge route priorities of the switch links such that the link to the upper link on the backup switch is block, stopping it from processing any VIP frames.
In the event of a Master switch failure, STP would reconverge and open the blocked link, allowing VIP frame processing on the backup switch.

## Slide 14: Sharing Interfaces Frame Flow Restrictions with VLANs
VIP = VSR 216.134.44.8
Active Master
Track on L4 ports
VIP = VSR 216.134.44.8
Active Backup
Single Client HTTP Request
VLAN 1
VLAN 2
VLANs eliminate L2 broadcast storms
Notes: Another option to ensuring that frames are not processed simultaneously is to set up two VLANs, putting one port on each switch in separate VLANs. By definition, a VLAN provides broadcast domain segmentation. This means that any broadcast traffic arriving on one port will not be broadcast across VLAN1 to the port in VLAN2. This eliminates bridging loops.
An important note. In order to do this, you must track on L4 port. L4 port tracking cuts across VLANs, where as physical port tracking will not.
Additionally, if you want to ping from one side of the VLAN to another, you must run a VIR in the top and bottom VLANs. This will allow you to cross the VLANs with your pings.

## Slide 15: Tracking
Tracking dynamically modifies a VRRP router’s priority based on the configuration of the switch
  The objective is to have as much processing of layer 3 and VIP on the same switch as possible
A backup VRRP router becomes master when its priority level rises above that of the current master

## Slide 16: Tracked Parameters
Track on L3 parameters or L4 parameters
Parameters you can track on:
  L3 parameters
    Virtual routers in master mode on the switch
    Active IP interfaces on the switch
    Active ports on the same VLAN
  L4 parameters
    Physical ports that have active layer 4 processing
    Healthy real servers behind the VIP
    In HSRP networks, the number of layer 4 client-only ports that receive HSRP advertisements
Each tracked parameter has a user configurable weight associated with it

## Slide 17: How Does Tracking Work?
Tracking criteria continuously update switch’s priority when tracking is enabled
For each tracking criteria met, the priority of the switch is incremented by the parameter weighting
Switches exchange priority information during VRRP advertisements
PREEMPTION allows a switch to assume master if its priority becomes the highest

## Slide 18: L3 Tracking – Virtual Routers
Switch tracks on the L3 Virtual Routers (VRs) in master mode on the switch
Ensures that the switch with the most client-server pairings are handled the same switch
Increase routing and load balancing efficiency

## Slide 19: Virtual Router Tracking Example
Master
VR priorities set to 101
Backup
VR priorities set to 100
VR1 Master
Pri 107
VR2 Master
Pri 107
VR3 Master
Pri 107
VR1 Backup
Pri 100
VR2 Backup
Pri 100
VR3 Backup
Pri 100

## Slide 20: Virtual Router Tracking Example
Backup
VR priorities set to 101
Master
VR priorities set to 100
VR1 Off
VR2 Master
Pri 105
VR3 Master
Pri 105
VR1 Master
Pri 102
VR2 Backup
Pri 102
VR3 Backup
Pri 102

## Slide 21: Virtual Router Tracking Example
Master
VR priorities set to 101
Backup
VR priorities set to 100
VR1 Off
VR2 Off
VR3 Backup
Pri 101
VR1 Master
Pri 106
VR2 Master
Pri 106
VR3 Master
Pri 106

## Slide 22: L3 Tracking - Interfaces
Switch tracks the number of L3 IP interfaces (other than itself) that are active on the switch
  An IP interface is considered active if at least one physical port in the VLAN is active, i.e., has a link associated with it
The VIR with the most active IP interfaces becomes master
Ensures that the switch with the most available routes in/out of the local network becomes master

## Slide 23: Interface Tracking Example
Master
VR1 priority set to 101
VR1 using L3 IF1
Backup
VR1 priority set to 100
VR1 using L3 IF1
IF1 Active
IF2 Active
IF3 Active
VR1 Pri =107
IF1 Active
IF2 Active
VR1 Pri =104

## Slide 24: Interface Tracking Example
Master
VR1 priority set to 101
VR1 using L3 IF1
Backup
VR1 priority set to 100
VR1 using L3 IF1
IF1 Active
IF2 Active
IF3 Active
VR1 Pri =105
IF1 Active
IF2 Active
VR1 Pri =104

## Slide 25: Interface Tracking Example
Backup
VR1 priority set to 101
VR1 using L3 IF1
Master
VR1 priority set to 100
VR1 using L3 IF1
IF1 Active
IF2 Active
IF3 Active
VR1 Pri =103
IF1 Active
IF2 Active
VR1 Pri =104

## Slide 26: L3 Tracking - Ports
The switch tracks the number of active physical ports
The VIR with the highest number of active physical ports will become master
Ensures that the switch with the most available active ports is master

## Slide 27: Port Tracking Example
Master
VR1 priority set to 101
Backup
VR1 priority set to 100
5 Active Ports
VR1 Pri = 111
4 Active Ports
VR1 Pri = 108

## Slide 28: Port Tracking Example
Master
VR1 priority set to 101
Backup
VR1 priority set to 100
4 Active Ports
VR1 Pri = 109
4 Active Ports
VR1 Pri = 108
X

## Slide 29: Port Tracking Example
Backup
VR1 priority set to 101
Master
VR1 priority set to 100
3 Active Ports
VR1 Pri = 107
4 Active Ports
VR1 Pri = 108
X
X

## Slide 30: L4 Tracking – Layer 4 Ports
The switch tracks the number of active physical ports
If L4 processing is active, the VSR with the highest number of active physical ports will become master
Ensures that the main L4 switch becomes master

## Slide 31: L4 Port Tracking Example
Master
VR1 priority set to 101
VR1 using L3 IF1
Backup
VR1 priority set to 100
VR1 using L3 IF1
Port 1 (Client) Active
Port 6 (Server) Active
Port 7 (Server) Active
VR1 Pri =107
Port 1 (Client) Active
Port 7 (Server) Active
VR1 Pri =104

## Slide 32: L4 Tracking – Real Servers
The switch tracks the number of healthy servers on the switch that are associated with the VSR
The VSR with the highest number of locally attached, healthy real server will become master
Ensures that the switch with the largest available server pool will become master
VIRs and corresponding VSRs must be the same on all the switches
Increases L4 efficiency

## Slide 33: Real Server Tracking Example
Master
VR1 priority set to 101
Backup
VR1 priority set to 100
R_IP1 Up
R_IP2 Up
R_IP3 Up
VR1 Pri =107
R_IP1 Up
R_IP2 Up
VR1 Pri =104

## Slide 34: Real Server Tracking Example
Master
VR1 priority set to 101
Backup
VR1 priority set to 100
R_IP1 Down
R_IP2 Up
R_IP3 Up
VR1 Pri =105
R_IP1 Up
R_IP2 Up
VR1 Pri =104
X

## Slide 35: Real Server Tracking Example
Backup
VR1 priority set to 101
Master
VR1 priority set to 100
R_IP1 Down
R_IP2 Down
R_IP3 Up
VR1 Pri =103
R_IP1 Up
R_IP2 Up
VR1 Pri =104
X
X

## Slide 36: L4 Tracking - HSRP
Switch tracks on the number of client-only ports that receive HSRP advertisements
The VSR with the highest number of HSRP associated ports becomes master
Elects the switch closest to the master HSRP router as master
Optimizes routing efficiency

## Slide 37: HSRP Tracking Example
Master
VR1 priority set to 101
Backup
VR1 priority set to 100
1 Client Only HSRP Port
VR1 Pri = 111
0 Client Only HSRP Ports
VR1 Pri = 100
HSRP Master

## Slide 38: HSRP Tracking Example
Backup
VR1 priority set to 101
Master
VR1 priority set to 100
No Client Only HSRP Ports
VR1 Pri = 101
1 Client Only HSRP Port
VR1 Pri = 110
X
HSRP Master

## Slide 39: Bridging Loops
Fully meshed VRRP configurations will result in bridging loops
Use STP or 3 VLANs to eliminate broadcast storms

## Slide 40: VRRP Loops with STP
Internet
X
X

## Slide 41: VRRP Loops with 3 VLANs
Internet
VLAN 1
VLAN 2
VLAN 3

## Slide 42: Reminder on Configuring Active-Active Redundancy
Configure L2 and L3 parameters on all VRRP routers
Turn VRRP and SLB on
Setup Layer 4 parameters on the master switch
Define all filters needed
Setup the VRRP parameters on the master switch
Synchronize layer 4 and VRRP configurations
  Need to explicitly “push” configurations to other VRRP capable switches
  Set up the peer switches on both VRRP switches
Modify configurations if necessary
  Change priority
Notes: Use the synchronize command with caution:
synchronization will cause the switches to have exactly the same layer 4 configurations
This may or may not be the desirable behavior
Each VRRP router does not necessary have the same layer 4 configurations

## Slide 43: Stateful Failover
State of session and connection table is shared between switches on port 9
Stateful failover is only supported in active-standby mode with VMA enabled
All URL and cookie parsing information is stored in the session table on port 9
  Sharing this information ensures that persistent sessions are sent to the same server in a failover situation
Notes: Shared persistency information includes SSL session state, HTTP cookie state, and Layer 4 persistent and FTP session state.

## Slide 44: Stateful Failover
What happens when a switch fails?
Notes: The backup switch (switch 2) becomes active.
The incoming request is redirected to switch 2.
When the user clicks Submit again, the request is forwarded to the correct server.

## Slide 45: Advanced VRRP Summary
Alteon supports VRRP configuration, allowing for full L3 & L4 redundancy
Active Active provides additional L4 processing power to the user’s network
Sharing enables Active Active processing
Tracking dynamically selects master switch in a VRRP network
VRRP configuration
  Define L3 parameters
  Define L4 (SLB and VRRP) parameters on master switch
  Push configuration from master to backup