## Slide 1: Alteon Switch Administration

## Slide 2: Switch Administration Objectives
Login to switch and change defaults
Upgrade and downgrade code
Perform serial downloads
Set switch software images
Set switch configurations
Set switch timeout
Set switch date and time
Run the switch setup script
Enable/disable Telnet
Setting the switch banner
Setting the management network
Configure port parameters
Set up a Syslog
Set SNMP parameters
Store system configurations
Set switch software key
Upon completion of the module, the student should be able to:

## Slide 3: Establishing a Console Connection
Requires standard DB9 cable with male connection
Standard connection
  9600 baud
  8 data bits
  No parity bit
  1 stop bit
  No flow control
Hyperterminal or any other terminal emulator

## Slide 4: Switch Administration Security Protection
user
  Generic switch access to view switch statistics and status information
  Default - user
slboper
  Operator that manages web servers and other Internet services and their loads
l4oper
  Operator that manages traffic on the lines leading to the Internet services.
oper
  Operator that manages all functions of the switch and is permitted to reset ports or the entire switch
Notes: By default, only user and admin accounts are active.

## Slide 5: Switch Administration Security Protection (cont’d)
slbadmin
  Administrator that configures and manages web servers and other Internet services and their loads
l4admin
  Administrator that configures and manages the traffic on the lines leading to the shares Internet services
  Default - l4admin
admin
  The Superuser Administrator that has access to all of the switch's management and configuration features
  Default - admin
Password determines user level
Notes: By default, only user and admin accounts are active.

## Slide 6: Changing Password
To change a user level password
  Administrator access to switch with admin password
  /cfg/sys menu
    admpw
    l4apw
    usrpw
    sopw
    l4opw
    opw
    sapw

## Slide 7: Security Administration with the CLI

## Slide 8: Upgrading Switch Code
Two software images plus boot image
Upgrading procedure
  Load new image to tftp server
  Download image from tftp server to switch
  Reset switch with new image
/boot menu
  gtimg – downloads new image via TFTP
    Where to put image <image 1/image 2/boot>
    TFTP server IP address
    Image file name
      _mp vs. _boot
      180 vs. 180e vs. 184
Reset switch with /boot/reset command
  Select image1 or image2 for reboot
/boot menu
  ptimg – transfers image to a TFTP server
Notes: /boot/ptimg and /boot/gtimg are new commands in the 8.3 code. They replace the /boot/tftp command, which is still available but hidden. Previously, you could not upload an image via tftp.

## Slide 9: Downgrading Image
Software image specific
Cannot downgrade two major revision levels
Follow release notes instructions exactly
BACKUP, BACKUP, BACKUP!!!
  Use /boot/ptimg to save current image
Serial download option

## Slide 10: Serial Download of Switch Image
Image transfer of last resort
  Corrupt firmware
  Corrupt configuration
Software image transfer through serial port
  Slower…56K tops
Serial download procedures
  Hard cycle switch
  Shift-D for 33.6K or shift-F for 56K
  Set Hyperterminal for 33.6 or 56
  File transfer using Xmodem
  Wait for the “Done”
  Hard cycle switch and reset hyperterminal to 9600
Notes: /boot/reset hard is equivalent to power cycling the switch.

## Slide 11: Setting Switch Images
Two software image banks
/boot/image <image>
  Select image1, image2 or boot
  Rebooting of the switch required - /b/r
Notes: Other general items to know are the switch:
Uses TFTP to load new software images to FLASH
Has two (2) FLASH banks - each can be independently controlled, overwritten, booted
Has a maintenance kernel for booting an image of last resort
Has two (2) CONFIG banks - One Primary, one Backup. Each indepdendently bootable
Has a FACTORY DEFAULT flash bank for booting a clean config
Real Time clock should be set at switch setup time.
The IP address should be set via BOOTP or via Console. Thereafter, Telnet and the WebUI are also available.
IT IS NECESSARY TO SET THE BOOT CONFIGURATION TO FACTORY DEFAULT WHEN DOWNREV’ING THE SWITCH IMAGE DURING BOOT.

## Slide 12: Setting the Switch Configuration Block
Two user configuration blocks or a factory configuration
/boot/conf command
  active
  backup
  factory

## Slide 13: Switch Image Administration with the CLI

## Slide 14: Setting Telnet
Telnet capabilities
Enable/disable telnet
  /cfg/sys/tnet <e|d>
  From console port only
  Telnet timeout default set to 5 minutes

## Slide 15: Setting Telnet with the CLI

## Slide 16: Switch Timeout
Switch CLI session timeout
  1 to 60 minutes
  Default set to 5 minutes
/cfg/sys/idle <idle time>
  Set time from 1 to 60 minutes

## Slide 17: Setting Idle Timeout with the CLI

## Slide 18: Setting Switch Date and Time
/cfg/sys/date <date>
/cfg/sys/time <24 hour time>

## Slide 19: Setting Switch Date and Time with the CLI

## Slide 20: Using the Setup Utility
Setup script allows for basic switch configuration
  Upon bootup of an unconfigured switch
  /cfg/setup
  <esc> to exit setup utility

## Slide 21: Setting the Switch Banner
Login banner up to 80 characters
Banner enabled for console/telnet user/admin logins
/cfg/sys/bannr <banner>

## Slide 22: Setting the Banner with the CLI

## Slide 23: Setting the Switch Management Network
Allows the administrator to set a workstation or range of workstations that are allowed to have management access to the switch
/cfg/sys/mnet <IP Address>
/cfg/sys/mmask <Subnet Mask>
Limits internal stack access
Notes: Limits internal stack access. The switch will only respond to internal TCP stack requests from source addresses in the mnet/mmask range.

## Slide 24: Setting mnet and mmask with the CLI

## Slide 25: Port Configurations
Configure individual physical switch ports
  /cfg/port <port number> fast menu
    Link speed - speed <any/10/100>
    Duplex mode - mode <any/full/half>
    Flow control - fctl <auto/rcv/trns/both/none>
    Autonegotiation enable/disable - auto <e|d>
Enable/disable a switch port
  /cfg/port <port number> menu
    ena/dis (or shorter term e/d)

## Slide 26: Port Configuration with the CLI

## Slide 27: Setting Up a Syslog
Configure up to two hosts to capture syslog messages
/cfg/ip/log(2) <ip address>
Eight different types of syslog messages
  EMERG: system is unusable
  ALERT: immediate action required
  CRIT: critical condition
  ERR: error condition/operation
  WARNING: warning condition
  NOTICE: normal but significant condition
  INFO: information message
  DEBUG: debug level message

## Slide 28: Configuring Syslogs with the CLI

## Slide 29: Setting Up SNMP
Allows for the switch to support SNMP network management
  /cfg/snmp menu
    System name, system location, contact information (64 characters each)
    Read/write community strings (32 characters)
    IP address of up to 2 hosts to receive system traps (allows for community string access)

## Slide 30: Configuring SNMP with the CLI

## Slide 31: Storing and Retrieving Switch Configurations
Two options to store and retrieve switch configurations
  TFTP -- use the switch’s TFTP feature
    /cfg/ptcfg <server IP, filename> to store a configuration
    /cfg/gtcfg <server IP, filename> to get a configuration
  Text capture
    Use the capture text capabilities of hyperterm
      Transfer pull down menu: capture text option
      Send to a file to store
      Set switch to verbose 0
      Cut and/or paste text from the configuration file
      Set the switch to verbose 2 to return to switch menu
Notes: There are three levels of verbosity: 0, 1, and 2.
  0 – no prompts, no messages
  1 – prompts, but no messages
  2 – prompts and messages. This is the default setting.

## Slide 32: Storing and Retrieving Configurations with the CLI

## Slide 33: Upgrading Switch Software Key
SLB and WCR software come with the switch
GSLB and BWM are optional
If you want to run GSLB or BWM
  Call Alteon to obtain license certificate (key)
    License is MAC specific
  /oper/swkey
    Enter swkey

## Slide 34: Upgrading Software Keys with the CLI

## Slide 35: Switch Administration Summary
Alteon switches are fully configurable by the network administrator
Alteon switches can be managed from a variety of security levels (e.g., user to admin)
Reviewed CLI administration commands