## Slide 1: Switch Product Line

## Slide 2: The Problem – Scaling Web Servers
Moore’s Law - processor speed doubles every 18 months
Internet doubles every 3 months: 64x every 18 months
So - - - a single processor can’t keep up!

## Slide 3: The Web System Solution
Web server clusters are the solution
There are few textbooks or courses for designing large web sites containing clusters of complex web servers, caches, firewalls . . .

## Slide 4: Web Data Centers Today
Server network built in piecemeal
Multi-vendor integration and debugging left to customer
Slowest device creates bottleneck
Redundant devices are idle
Application Servers
Database
Web Servers
Internet
Backup Storage
Local load balancer
Cache
VPN Server
Global load balancer
Bandwidth manager
Firewall

## Slide 5: The New Web Data Center
Web server cluster
Inter/Intranet
LAN
Cache server cluster
Application
server cluster
Backup/Storage
Load balancing mirrored or cache sites
Architecture provides
  No bottlenecks
  No idle components
  Predictable behavior and scalability
  Single point of control
Internet
Firewall cluster
Router cluster
Web switch provides
  Switching, IP routing
  Clustering (with health checking)
  Traffic redirection
  Bandwidth management
  Server protection
Web Switch

## Slide 6: Web Switch Requirements
Session-based traffic management
Speed, speed, and more speed
Availability
Scalability
Flexibility/control
Notes: Session-based traffic management
  Each session must be statefully tracked, processed and forwarded
  Definition of a “session” is application dependent
Speed, speed, and more speed
  “Session bindings” per second, not just packets per second
  Session binding latency is key to reducing web wait
Availability
  Resilience against application, server, link, switch and site failures
  Ensure integrity of critical sessions
Scalability
  Performance and capacity for millions of sessions per second
  Room for adding new traffic management services
Flexibility/control
  Single policy drives all integrated services
  Customization for differentiation and flexibility
  Support service level agreements (SLAs)

## Slide 7: Alteon Product Lines
ACEdirector
  Fast Ethernet Web Switches
Alteon 180 Series
  Gigabit Ethernet Web Switches
Alteon 700 Series
  The 708 is a Modular, Web Data Center Switch
  The 780 is a High-density Content Switch
Integrated Service Director (iSD) Platform
  SSL Accelerator
  PCD – Personal Content Director
  PCC – Personal Content Cache

## Slide 8: ACEdirector 2, 3, 4
8 x 10/100Base-TX Autosensing Ethernet ports -
RJ45 connectors
ACEdirector 2 has (8) 10/100 ports and 1 MB memory per port
ACEdirector 3 adds a gigabit port and has 2 MB memory per port
ACEdirector 4 has a gigabit port and has 4 MB memory per port

## Slide 9: Alteon 180+, 180e, 184
Single-MAC
Dual-PHY Ethernet port
SC connector for 1000-SX
RJ45 connector for 10/100Base-TX
Console port
8 x selectable 10/100/1000 Mbps Ethernet ports
1 Gigabit Ethernet uplink
Alteon 180 Plus: 1 MB memory per port
Alteon 180e: 2 MB memory per port
Alteon 184: 4 MB memory per port

## Slide 10: Alteon 180 Series and ACEdirector Architecture
Distributed processing architecture - 18 or 20 processors
  Per port ASIC integrates dual RISC processors and hardware-assisted forwarding engine
  Distributed software environment
Scalable performance across all ports
Room for on-going feature enhancements
1 or 2MB
RISC
Fwd Engine
RISC
ASIC
1 or 2MB
RISC
Fwd Engine
RISC
ASIC
1 or 2MB
RISC
Fwd Engine
RISC
ASIC
...
Multi-Gigabit switch backplane
Management Module
4MB SRAM
2MB Flash
Switch Modules
RISC
RISC
1 or 2MB
RISC
Fwd Engine
RISC
ASIC

## Slide 11: The Alteon 708 Series
Ultra high performance at all layers
  Wire-speed L2/3 switching
  3.0 million pps per port on all ports (full duplex)
  Wire-speed session switching
  372K sessions per second per port; 12 million per switch
Total system resilience
  Support for active-active redundancy configurations
Built-in content, application and network-intelligence
  Example: Content parsing in hardware
Notes: Ultra high performance at all layers
  In addition, the 700 series has the lowest session binding latency compared to other products in the marketplace.
Total system resilience also includes:
  All modules work in both systems, hot swappable; redundant power/fan/fabric/management modules
  Maintain active sessions during failover
Built-in content, application and network-intelligence
  Content parsing hardware minimizes session setup latency
  Comprehensive and customizable application health monitoring

## Slide 12: The Alteon 780
Uses a distributed Application Specific Integrated Circuit (ASIC)-based architecture
Wirespeed Layer 2 and Layer 3 forwarding for the network core
Supports 10 Mbps, 100 Mbps, and Gigabit Ethernet interfaces
Wirespeed Layer 2, 3 and 4 “application-based” classification, and filtering
Consistent low latency for time-critical applications like voice and video, even under a heavy load
Distributed, Redundant MLT (MultiLink Trunking)
CPU, switch fabric, and power supply redundancy available
VRRP support

## Slide 13: Integrated Service Director SSL (iSD SSL)
Allows for Content switching on HTTPS sessions
Improves server performance processing SSL traffic
Scalable
iSD-SSL health checking, load balancing and failover accomplished by Alteon Web Switch.
Notes: Allows for Content switching on HTTPS sessions
  Solves the mega-proxy “stickiness” problem by providing cookie based persistence for both HTTP and HTTPS
  Allows HTTPS load balancing based on HTTP content such as cookie, browser type, language, etc.
Scalable
  Simply connect additional iSD-SSL’s to the switch to increase capacity

## Slide 14: Integrate Service Director PCD (iSD-PCD)
Personal content director
Performs true client proximity and Global Server Load Balancing (GSLB)
Enhances web experience for users by determining best server for each client

## Slide 15: Web OS Highlights
Core
Features
Advanced
Features
Virtual
Matrix
Architecture
(VMA)
Scripted
Health
Check
Content
Switching
Cookie Cutting
Secured
Switch
Management
Application
Redirection/
SLB
SSL Session ID based persistence
High
Availability/
VRRP
Bandwidth
Management
Wire-speed
Packet Filtering
Usability
-CLI
-SNMP
-SYSLOG
GSLB – Global Server Load Balancing

## Slide 16: Web OS: Server Load Balancing
Low latency server load balancing
Highest performance content-aware SLB
TCP connection termination at the switch
Clients
Site 1
Site 2
Notes: Low server load balancing latency
  SLB session almost entirely hardware switched
Highest performance content-aware SLB
  Switch terminates TCP connection from client
  Hardware-assisted content-parsing (URL, cookie, etc)
  Switch opens TCP connection to server
  Hardware splices client and server TCP connections

## Slide 17: Web OS: High Availability
Active-active redundant mode:
  Load split between peer switches
  Switch/switch port detects peer failures and assumes entire load
  Supported for L3 and SLB configs
Session maintenance during failover
  Automatic per-port failover with no session loss
  Ensure transaction integrity for business-critical sessions (e-shopping)
GSLB provides site failure protection
VRRP
Active Switch B
Active Switch A
In the event of a switch or switch port failure, redundant switch assumes load balancing responsibility for its peer
Primary - A
Backup - B
Primary - B
Backup - A

## Slide 18: Web OS: Global Server Load Balancing
Content server
Web Servers
3-in-1 integration
  Switching, local and global server load balancing in ONE
Traffic directed to best performing sites without overloading site
Simple configuration
  Requires only switch and DNS changes
  No router, server or network reconfiguration
No added latency
  Instant request handed-off decision
GSLB proximity table

## Slide 19: Web OS: Bandwidth Management
Granular bandwidth allocation
  CoS based on web site (VIP), user class, application, content-type, or IP TOS
  Hardware queue management and scheduling based on strict priority, weighted fair queuing or deadline de-queuing
Per-session traffic shaping
  Committed Information Rate (CIR) support enables service differentiation
  Congestion management: End-point flow control or intelligent packet drop
Hardware-assisted logging for accounting and SLA reporting
AD3, AD4
180e, 184

## Slide 20: Web OS: Server Security
Prevents Denial of Service (DoS) attacks without blocking legitimate traffic
Network address translation (NAT)
Wire-speed access list filtering
Secure switch administration
Secure switch management
Notes: Prevents Denial of Service (DoS) attacks without blocking legitimate traffic
  Terminates all incoming connections at switch
  Only completed connections are let through
  Thwarts SYN attacks without blocking legitimate session requests
Enhanced packet filtering capabilities
  non-IP packets filtering
  IP options
  ICMP message types
    Echo, Echo reply, Source quench, Redirect
  TCP flags
    Syn, Ack, Rst, Fin, Psh, Urg
Increased switch administration security protection
7 levels of administrator access
Secure switch management
  Secured shell (ssh) and secured copy (scp)
  Radius and Secure ID authentication for management access

## Slide 21: The Power of VMA
Realize full advantage of distributed processing without its limitations
Optimized for both asymmetric and symmetric topologies
Software upgrade; no new hardware
Most scalable architecture; long-term investment protection
Notes: Realizes full advantage of distributed processing without its limitations
  Maximum parallel processing with minimum memory search latency
Optimized for both asymmetric and symmetric topologies
  Up to 8-fold increase in session performance at all load levels
  Memory at all 8 ports pooled to increase storage capacity
    256,000 session table entries even when all traffic enters at a single port
    Increased packet buffering capacity

## Slide 22: Web OS: Virtual Matrix Architecture
DA_Z, SA_3, RIP_A
CPU
CPU
Each received packet is hashed to a designated port’s CPUs for L4-7 processing, regardless of where it ingresses
  Hashing algorithm ensures even distribution of traffic
  Packets in same session always hashed to the same CPUs
Session entry kept in memory local to designated CPUs
  Global session table kept for all persistent sessions
  All ports store all filtering/redirection policies
Layer 2/3 processing unchanged
CPUs at all ports actively processing load at all times
Memory at all ports pooled and utilized at all times
...
CPU
CPU
SA_1
DA_X
...
SA_2
DA_Y
...
SA_1
DA_X
...
Global persistent session table
SA_3
DA_Z
...
client port
unattached port
server port
server port
CPU
CPU
CPU
CPU
DA_X, SA_1, RIP_A
DA_Y, SA_2, RIP_B
DA_X, SA_1, RIP_A
DA_Z, SA_3, RIP_A
AD2, AD3, AD4
180, 180e, 184
Notes: The approach assigns a port, called the designated port, to each client. The designated port performs all processing on the L4 frames to and from the client. L4 frames include client, server, and filtered frames. Frames that only require L2 or L3 processing are not affected.
A client is assigned to a designated port based upon it's IP address. The IP address is folded and xor'd until a 4 bit quantity remains. This quantity is divided by the number of ports (masked with 0x7?) to determine the designated port. This method provides the best distribution since all 32 bits are significant.

## Slide 23: User Scriptable Health Checks
Example of script
  open port 80
  send GET /script.cgi /HTTP1.1\n\rHost:www.alteon.com\n\r
  expect HTTP/1.0 200*
  send GET /index.html HTTP1.1\n\rHOST:www.alteon1.com\n\r
  expect HTTP/1.0 200*
  …
  close
  open port 443
  …
  close
Benefit
Dynamically execute a series of
tests to check for application and
content availability
Features
Ability to send multiple commands
Check for any return string
Test availability of different applications
AD2, AD3, AD4
180, 180e, 184
Notes: This feature allows the user to configure the switch to send a series of requests to real servers and monitor the responses.
The advantages of this method:
More complex tests, to check the availability of various web applications
Monitor responses to detect sever or application failure

## Slide 24: New Features in Web OS 8.3
VPN Load Balancing
Stateful failover
Port mapping enhancement
Enhanced bandwidth management
Server-side Multi-response cookie search
CPU and session table information
List ICMP filter types
Increased static route capacity
New TFTP commands
WSP health checks
Enhanced URL web-cache redirection
Notes: VPN Load Balancing
8.3 has the ability to load balance VPN traffic in much the same way that FWLB works.
Stateful Failover of L4 and L7 Persistent Sessions
Stateful failover provides session failover in high availability configurations.
Port Mapping Enhancement
The ability to map a single vport to multiple rports has been enhanced. A lab exercise has been added to the advanced class on this topic.
Enhanced Bandwidth Management
URL-based BWM allow the network administrator to control bandwidth based on URLs, HTTP headers, or cookies.
Server-Side Multi-Response Cookie Search
Allows the switch to look at up to 16 server responses for a persistence cookie. CPU and Session Table Information
New ways to monitor CPU and Session table information have been added to the CLI menu.
Option to List ICMP Filtering Types
When configuring filters, the user can now list the available ICMP message types.
Increased Static Route Capacity
Static route capacity has doubled to 128 routes.
New TFTP Commands
The gtimg and ptimg commands have been added to the Boot menu. The ptimg command lets the user put the Web OS image to the TFTP server from the switch.
WSP Health Checks
WSP health checks allow for the health checking of wireless gateways. Look for more wireless features to be added in the future.
Enhanced URL Web-Cache Redirection
This feature now supports transparent caches.

## Slide 25: Summary
Alteon WebSystems’ sole focus is to enable scalable, high-performance, high availability web-centric data centers and large customer web sites to perform as efficiently as possible.
The Alteon web switches have a hardware-assisted, distributed processor architecture that is needed to scale web switching performance