## Slide 1: Basic Filtering
Notes: 1

## Slide 2: Filtering Objectives
Upon completion of this module, the user shall
  Understand Alteon filtering capabilities
  Understand the advantages of wire speed filtering
  State the filtering parameters and actions
  Understand filter usage
  Configure an Alteon switch for filtering

## Slide 3: Why Do We Want to Filter?
Allow/deny traffic
Support Web Cache Redirection (WCR)
  In-depth discussion in Application Redirection module
Support iSD-Platform
Increase security through network address translation (NAT)
  In-depth discussion in Alteon Certified Engineer course

## Slide 4: Advantages of Alteon Filtering
Speed
  Wirespeed access lists
Control who uses your network and how your network is used
  Layer 3 and Layer 4 filtering capabilities
Off load network devices to take advantage of their strengths

## Slide 5: Alteon Filtering
Alteon allows filtering on the following parameters
  Source IP address/range of addresses
  Source port/range of ports
  Destination IP address/range of addresses
  Destination port/range of ports
  Protocols
  TCP flags (ACK and RST {reset})
Notes: List of Well Known Ports
1 ICMP
2 IGMP
6 TCP
17 UDP
89 OSPF
112 VRRP

## Slide 6: Alteon’s Policy Based Filtering Engine
Frame Ingress
Frame /Session Inspection Engine
Source MAC
Destination MAC
IP Source Addr /Range
IP Dest Addr / Range
Protocol Type
TCP/UDP Source Port
TCP/UDP Dest Port
TCP Flags
Allow Frame / Express Forward
Drop
Redirect to Server Group
Action
Iterate per Unmatched Frame / Session

## Slide 7: Filter Usage
Configure filters globally, assign them locally
224 filters per switch
Filter number determines order of precedence
Filter numbering
Once filter fires, packet is passed out of switch
Default filters

## Slide 8: Configuring Filters
Create filters under /cfg/slb/filt # and enable it
  Set filter parameters and action
    filt 224/sip any/dip any/proto tcp/sport any/dport 80/act redir/rport 80/group 1/ena
Under /cfg/slb/port #, select the port you wish to apply the filter to.
Enable port filtering under /cfg/slb/port #/filt e
Add filter port with /cfg/slb/port #/add #
Turn SLB on - /cfg/slb/on
Apply and save
Notes:   Note that client and server processing do not have to be enabled for application redirection. By default, if no group is specifically chosen by the user, redirection selects group one.

## Slide 9: Configuring Filters with the CLI

## Slide 10: Configuring Filters with the CLI

## Slide 11: Filtering by ICMP Type
Notes: /cfg/slb/filt X/adv/icmp list gives a list of the available ICMP types upon which filtering can be performed.

## Slide 12: A Brief Note On Filters
Normal filters perform a logical AND on all filter parameters
  Filter fires IF all filter conditions are met
Inverted filters perform a logical OR on the inverse of all filter parameters
  Filter fires if any filter condition is not met

## Slide 13: Process Static Filters Before Dynamic Filters
Process exclusion/inclusion filters first
Process high use filters next
Process default allow and deny filters last

## Slide 14: Filtering Summary
Filtering enable the administrator to allow and deny traffic, provides application redirection and increase network security
Reviewed filtering configuration and operation
  Allow
  Deny
  Redirect
  NAT