## Slide 1
Basic L2/L3 Operations:
VLANs, Jumbo Frames,
and Trunking

## Slide 2: Objectives
Upon completion of this module, the student will be able to:
  Understand Alteon’s L2 capabilities
  Understand Alteon’s L3 capabilities
  Understand Alteon’s VLAN capabilities
  Understand Alteon’s Port Trunking capabilities

## Slide 3: Alteon Layer-3 Solutions: IP Routing
Why does Alteon perform routing?
  SLB enhanced with routing
  Inter-VLAN routing
  Jumbo frames through routing
  Implement security policies through routing

## Slide 4: Where Does Alteon’s Routing Fit In?
At the edge of the network, near the servers, where you need line-rate IP communication between servers, server networks and the LAN backbone
WAN Backbone Switch
Internet Desktop
LAN/WAN Boundary Router
L2/L3 LAN Backbone Switch
Notes: Please note that the Alteon switch is not a router. It is a Layer 4-7 switch that has L2 and L3 capabilities. It does not fill the function of a full fledged border router.

## Slide 5: Enhanced SLB with Routing
RIP Group1
RIP Group2
Internet
10.23.54.5
10.23.54.6
10.23.54.7
10.40.31.11
10.40.31.12
10.40.31.13
VIP1
192.168.100.13
IP Routing Interfaces
192.168.100.3
10.23.54.1
10.40.31.1
IP Routing Interfaces
192.168.100.1
WAN I/F addr
Notes: Configure SLB on the switch (ports, general config)
Configure RIPs on private subnets. The switch is the RIP’s default gateway
Configure VIPs on public subnet, advertised via DNS
Config VLANs if desired
Frames coming from the Internet Router will be sent to the VIP of the switch (via the VIPs virtual MAC and IP)
Frames will be address translated as appropriate, and sent directly to the RIPs. No need to use the IP routing function, yet…
Frames coming back from the servers will be sent to their configured default gateway, because their destination is off the local subnet.
These frames will have the switch’s IP routing MAC address as the MAC destination address. The switch will receive them via the IP routing process, and then perform L4 SIDS afterwards.
The Real Servers can now be located on their own private subnets with the Alteon switch acting as their gateway. With the combo of L3/L4 - their addresses are completely hidden from the rest of the world. The “world” talks to the VIPs and the servers talk to the Alteon switch. This is especially useful with many real servers with many addresses (using I-masking on the switch, for instance).
The real servers will have their default gateways set to subnet interface addresses configured in the switch. When the servers transmit frames destined for another subnet than their own, they will use the switch as the default gateway (DefGW) to get frames to those networks.
The most common configuration deployed have with some number of subnets routed via the switch (servers on those subnets), and two (2) default gateways from the switch to the routed backbone. The switch will health check between the default gateways, and fail between as necessary.
The Alteon switch can provide a level of network security by allowing the servers to have non-routable IP addresses on the network. This ensures that no one can directly address the servers or no server can directly forward information with its non-routable IP address.

## Slide 6: Routing Protocols
RIPv1, 1K route table entries
RIPv2 only on the Alteon 700 series
BGP4 subset supported (on AD4 and Alteon 184)
Static routes (up to 128)
Multiple default routes
  Up to 4 per switch
  Each default gateway is health checked using ICMP Echos

## Slide 7: Configuring IP Routing with the CLI

## Slide 8: Configuring IP Routing with the CLI (con’t)

## Slide 9: VLAN Terminology
VLANs
  Separation of broadcast domains
    On a single networking device or multiple networking devices
VLAN ID
  Identifier of a specific broadcast domain
  Can be “named” any number 1-4095 (per IEEE 802.1Q standard)
PVID
  Port VLAN Identifier
  Used to associate a physical switch port with a specific VLAN
Tagged Ports
  Field in Ethernet frame used to identify a VLAN
  Required if multiple VLANs are running over an single port
Trunk Ports
  Ports that carry more than one VLAN

## Slide 10: VLANs
2
2
3
3
4
4
1
1
1, 2, 3, 4, 5:
VLAN IDs
...
1, 2, 5
3, 4, 5
1, 2, 3, 4, 5
1, 2, 3, 4, 5
Notes: VLANs define Layer 2 broadcast domains.
All broadcast, multicast, and unknown destination address (DA) unicast frames are flooded to all ports associated with a VLAN.
Often, addresses are allocated so that all members of an IP subnet are on the same VLAN. Cross-VLAN routing is then needed to communicate between subnets.
Both the Alteon ACEnics and ACEswitches support VLANs.
The method for one device to indicate to another device which VLAN a frame is associated with is called VLAN "tagging". IEEE 802.1Q, which is heading towards standardization, defines the fields into which tags are inserted. This portion of the standard has been stable for about a year and is the approach Alteon uses on both NICs and switches.

## Slide 11: VLAN Tagging Terminology
1,2,3,4,5:
VLAN IDs
1,2,5
3
1, 2, 3, 4, 5
1,2,3,4,5
2
2
3
3
4
4
1
1
Tagged Ports
Untagged Ports;
PVIDs
Untagged Ports – A single VLAN
Tagged Ports – Multiple VLANS
Notes: Alteon supports port-based VLANs.
Every port is configured as an “untagged port” or a “tagged port.” All ports which are to support more than one VLAN must be configured to be tagged ports.
The default is “untagged port.” An untagged port can support only one VLAN. The identity of that VLAN (and, hence, the association of frames transmitted and received on that port to a VLAN) is determined by the port VLAN ID (PVID) configured on that untagged port.
Untagged ports can be configured for a default PVID. The default for all ports is PVID 1.
Each ACEswitch port and ACEnic can be configured to be tagged and support up to 64 identified VIDs. These VIDs can be any number in a range of 1 through 4095 as defined by the 802.1Q standard. The set of VIDs configured is referred to as the internal VLANs. For tagged ports, the frame-to-VLAN association is determined by the tag in the frame.

## Slide 12: VLAN Operation
1,2,3
2
1,5
Tag Insertion
1
A Broadcast
Tag Insertion
Tag Removal
Notes: Tagged and untagged switch ports differ in operation both in ingress and egress rules.
  Tagged ports:
    Ingress:
      Drop frames received with no tags and frames received with VIDs different from the set the port has been configured for.
      Strip the VLAN tag off of all frames received with a VID that matches what the port has been configured for.
    Egress:
      Insert VLAN tag (the VID is remembered from input port)
  Untagged ports:
    Forward untagged frames received. If broadcasts, multicasts, or unicast frames with unknown destination addresses (DA), flood to all ports in the switch configured for the same VID (could be both untagged and tagged ports).
    Drop any received frames which are already tagged.
NICs which support VLANs operate very much like switch tagged ports.
  VIDs are configured to be associated with logical interfaces. The logical interfaces correspond to different IP addresses in different subnets.
  Tags are added going out the NIC, based on the logical interface the frame was passed to the NIC.
  Tags are removed coming into the NIC, and frames are passed up through the logical interface corresponding to the tag.

## Slide 13: Inter-VLAN IP Routing
Flexible networking
256 VLANs per switch
  10 VLANs for management
  246 VLANs for use
Up to 256 IP interfaces per VLAN
Jumbo frame support
2
2
3
3
4
4
1
1
1,2,3,4,5:
VLAN IDs /
IP subnets
...
1
5
1,2,3,4,5
1,2,3,4,5
Notes: IP Routing allows flexible network topologies
Support 246 network-wide VLANs per switch
Each VLAN may have between 1-256 IP routing interfaces configured
Inter-VLAN communication takes place within the switch instead of burdening a router
Allows flexibility in configuring which servers support VLAN tagging and which do not
Servers with AceNICs easily support jumbo frames, with or without VLANs
IP fragmentation in the switch will fragment jumbo frames from server to standard Ethernet frame sizes

## Slide 14: VLAN Implementation Guidelines
802.1Q standard interoperable
Configure trunk ports to support all active VIDs
  Both ends must be consistent
  Jumbo frame exception
Notes: Many vendors support a compatible method of tagging VLANs based upon pending 802.1Q specifications. This portion of the standard has been stable for quite some time. One still must take care to make sure that the same VIDs are used across all the vendors products for all ports that are in the same VLAN.
Although not absolutely required, trunk ports should generally be configured for all VLANs in the Spanning Tree domain. This makes on-going network maintenance easier. As new ports are configured for VLANs or the VLAN configuration changes, it won’t matter to the trunks because they ensure a presence of each VLAN is available on each switch. Otherwise, VLANs could be configured on a switch which are islands, unable to trunk to ports on the same VLAN on a different switch.
An exception to this guideline is that VLANs that carry jumbo frames should not be configured on any trunk port that does not have a jumbo-capable switch on the other end of the link. The reason is that reception of jumbo frames by non-jumbo-capable systems may have an unpredictable (negative) impact on the non-jumbo-capable systems. If VLANs that carry jumbo frames are configured on a trunk, it is inevitable that some jumbo frames will traverse the trunk because of things like frames destined for unknown DAs.
Conversely, for tagged ports connected directly to NICs, the port should be configured to support only the same VLANs as is configured on the NIC. This reduces the amount of spurious broadcast traffic sent to the NIC.
Configure trunk ports to support all active VIDs; both ends must be consistent
  Exception: do not configure VLANs that carry jumbo frames on any trunks port that does not have a jumbo-capable switch on the other end of the link

## Slide 15: VLAN Configurations
When running VLANs, there are two areas you need to configure VLAN identifiers:
  on the IP interface configuration
  on the switch port
To configure VLANs on the IP interface
  /cfg/ip/if <if number>
  vlan <vlan number> (1-4096)
To configure VLANs on the port
  /cfg/port <port number> menu
  pvid <vlan number (1-4096)>
To configure a port for multiple VLANs
  /cfg/port <port number>/tag e
  pvid <vlan number (1-4096)>

## Slide 16: Configuring VLANs

## Slide 17: Configuring VLANs

## Slide 18: Jumbo Frame Guidelines
A complete Alteon supported path is required to support 9K jumbo frames
If there are any third party devices connected to the Spanning Tree domain at all, VLANs must be configured
  The AceNIC is configured to use jumbo frames on the selected VLAN and not on others
Notes: For jumbo frames to pass from server A to server B, each server must have an AceNIC, and the path must be through Alteon switches.
Generally, VLANs must be configured to make jumbo frames work while at the same time allowing connectivity to devices which cannot be reached through an all Alteon path.
Even if the only non-Alteon device connected to the Spanning Tree domain is a router, VLANs must be configured, one for communication within the Spanning Tree domain and one for communication to the router.

## Slide 19: IP Routing: Enhances Jumbo Frames
Physical Partitioning
VLAN 1
VLAN 2
VLAN Partitioning
IP Fragmentation
Standard
Jumbo
Standard
Jumbo
Standard
Jumbo
LAN
LAN
Notes: Servers are attached to one VLAN, which has jumbo frames enabled on it. These servers are on one subnet.
All other non-jumbo frames devices are on other VLANs (1 or more). These VLANs are different subnets.
IP routing interfaces are configured in the switch and are attached to appropriate VLANs - one per subnet.
When servers communicate with each other, they do so using Jumbo frames.
When clients communicate with the servers:
  Using TCP, part of the TCP setup process is called MSS Negotiation, or Maximum Segment Size negotiation. This exchange process between the two endpoints of the TCP session sets the maximum frame size/TCP payload size that can be exchanged. All of the frames between client/server will be standard Ethernet frames.
  Using UDP, frames will be IP fragmented by the switch when transmitting from server (jumbo frames) to client (non-jumbo frames).

## Slide 20: Port Trunking
Port trunking is combining multiple physical ports together to act as one single “Super Bandwidth” port
  Aggregate bandwidth
  Statistical load balancing over ports
    L2 and L3 inspections used to determine load balancing
  Built in fault tolerance
  Increase session tables
Notes: Statistical load balancing – Network traffic is statistically load balanced between the ports in a trunk group. WebOS uses both L2 MAC and L3 IP address information to determine load distribution.
Statistical load balancing depends on the devices feeding the trunks. With L2 only distribution algorithms, only L2 devices attached to the trunks are eligible for trunk distribution. This may be limiting as far as port trunking is concerned. With the addition of L3 distribution algorithms, the switch can take advantage of the wider address combinations seen, thereby taking advantage of more even port distribution.
Increased session tables – With the Alteon 5.2 and 6.0 WebOS, there is a limit of 64,000 concurrent sessions per port (2MB products: AD3/180e). With normal and heavy internet traffic, this is more than adequate to handle L4 traffic processing. With delayed binding options enabled, the concurrent session table space is reduced to 32,000 concurrent sessions per port. In the event that concurrent session table space becomes limited, it is possible to extend the concurrent session space by using Alteon’s port trunking capability. By trunking ports, the user not only aggregates bandwidth but also aggregates the concurrent session table space. Concurrent session tables can be increased to 364K concurrent sessions with the AD3/180e platforms.

## Slide 21: Alteon’s Port Trunking Capabilities
Up to four trunk groups consisting of 2 to 4 ports each
Up to six 10/100 MHz ports per group
Up to four 1000 MHz ports per group
IEEE 802.1P compatible
Nortel Multilink Trunking (MLT) compatible
Cisco Etherchannel compatible
SUN Quad Fast Ethernet Adapter compatible

## Slide 22: Configuring Trunk Ports

## Slide 23: Switch Access with Routing/Multi-IFs
The switch will be accessible from any subnet interface configured in the switch
To minimize or prevent access to one or more switch IP addresses, configure filtering on one or more physical ports to allow/disallow switch IP address access

## Slide 24: L2 and L3 Applications

## Slide 25: Single VLAN IP Routing Configuration
IP Routing Interfaces
204.165.121.1
192.168.12.1
203.10.45.1
All servers are members of same broadcast domain
All ports are configured for same VLAN (1)
Multiple IP interfaces are defined in the switch to route between servers on the network
Allows any server to be plugged into any port on the switch with no IP address changes
204.165.121.5
203.10.45.21
192.168.12.10
204.165.121.2

## Slide 26: Multi-VLAN IP Routing Configuration
Partial allocation of servers into different broadcast domains
(3) VLANs (Green, Red, Blue) with multiple switch ports as members
Each IP interface is directly associated with a specific VLAN (and therefore, ports too)
If a Red Server is attached to a Blue VLAN port, it will not be able to communicate with the rest of the network.
Multiple IP interfaces may be associated with the same VLAN
204.165.121.5
203.10.45.21
192.168.12.10
204.165.121.2
IP Routing Interfaces
204.165.121.1 : vlan1
192.168.12.1 : vlan200
203.10.45.1 : vlan 300

## Slide 27: “Classic Router” IP Routing Configuration
Top Alteon switch is acting as a “classic router”, with each switch port configured for one VLAN. Each VLAN is configured with a single IP routing interface
Communication between Red Servers and Green Servers involves L2 switching at the edges and IP routing in Alteon switch
All server subnet to subnet communication does not require going through the router
Communication to network backbone (Black subnet) involves the router as the next-hop
Router

## Slide 28: L2, L3, VLAN Trunking Summary
Alteon switches provide Layer 2 and Layer 3 functionality to include routing, VLANs, jumbo frames and port trunking
Reviewed configuration of
  L3 switching
  VLANs
  Port trunking