## Slide 1: Basic Server Load Balancing
Notes: 1

## Slide 2: Server Load Balancing (SLB) Objectives
Upon completion of this module, the student should be able to:
  Understand L4 bindings
  L4 frame flow
  Client and server processing
  Server health checks
  SLB configurations

## Slide 3: Server Load Balancing Provides Performance, Scalability and Availability
Clients
Site 1
Site 2
Site 3
Clients
Site 3
Site 2
Site 1
Site 2
Site 1
Site 2
Site 2
Site 1
Site 2
Site 2
Site 2
Server Load Balancer
Outage!
Congestion!
Wasted Capacity!
Site 1
Site 2
Site 3
Site 1
Site 2
Site 3

## Slide 4: HTTP Server Load-Balancing
Alteon Site Virtual Service
TCP Session Requests
1000 Mbps
100 Mbps
Web Farm
ACEswitch load-balances and redirects session requests to servers
ACEswitch forwards non-session traffic via L-2 switching
Reduced internet access response time
Increased service reliability
Increased server efficiency
Increased application scalability
Notes: Every element of a Web Page (GIF, JPG images, HTML text, buttons, toolbars, sounds, etc.) all require a separate TCP connection/session with HTTP 1.0, the most common version of HTTP.

## Slide 5: Review: IP Communications
IP Header
  IP Source Address
  IP Destination Address
  IP Checksum
TCP Header
  Source Port
  Destination Port
  Checksum
Notes: IP source address (IPSA) – 32 byte address in the sender’s ethernet frame
IP destination address (IP DA) – 32 byte address that is the ultimate receiver of the ethernet frame
IP Checksum – a 4 byte value used in error checking IP transmissions
Source Port – the virtual port the server will use for communications to the client
Destination Port – the virtual port the client will use for communications to the server
TCP Checksum – a 4 byte value used in error checking in TCP communications

## Slide 6: The Life of an HTTP Request
IPDA 192.168.13.10: SYN ACK-ACK, TCP Port 80
Client
Client Site DNS Server
DNS Lookup for: www.alteon.com
DNS response with: 192.168.13.10
Client
Alteon’s Web Server
IPDA 192.168.13.10: TCP SYN, Dest TCP Port 80
IPDA (client) : TCP SYN-ACK
IPDA 192.168.13.10: HTTP GET (url), TCP Port 80
IPDA (client) : GET RESPONSE (data)
IPDA 192.168.13.10:TCP FIN, Dest TCP Port 80
IPDA (client) : TCP FIN-ACK
Notes: Every Frame will contain:
IP Source Address (IPSA)
IP Destination Address (IPDA)
Source TCP Port (sPort)
Destination TCP Port (dPort)
When the Client transmits frames, the IPSA will be its own IP address corresponding to the configuration of the workstation by the administrator. The sPort will be dynamically generated by the client at TCP session “start time.” Whenever the client transmits frames for this particular TCP session, it will always use the same IPSA and TCP sPort. The IPDA will be the server’s IP address, and the dPort will be the well-known TCP port number for HTTP: TCP Port 80.
When the Server transmits frames back to the client, everything is reversed: the IPSA will be the server’s, the sPort will be the well-known TCP port number for HTTP (port 80), the IPDA will be the client’s, and the dPort will be the dynamically generated by the client at TCP session “start time.”
Any deviation from any of these expectations this will result in the Client or Server issuing a TCP Reset for the session (effectively closing it).

## Slide 7: Web Switch Operation (aka What a Web Switch needs to be able to do)
1. Address Substitution
2. Selective Forwarding
3. Monitoring Health
4. Layer 2 Switching
Notes: Web switches provide a “Virtual Service Interface” to clients. Virtual services are a combination of Virtual IP addresses (VIP) and (optionally) actual TCP destination ports. Web switches perform “session switching”. While they do perform packet-by-packer forwarding, they do so in the context of understanding the beginning and completion of active sessions.
Virtual services present a single address/port for a group of real servers and load-balance service requests between the real servers at a site. Real servers are actual host machines with unique IP addresses that provide TCP/IP services to the network. The Virtual service IP address is published to the user community (via DNS), but the real IP address can remain unpublished, allowing customers to hide actual site implementation details and provide single points of contact for users.
The basic functions of Alteon Web switches are:
Session address substitution to support the flow of traffic from client-to-server and server-to-client related to the vrtual services.
Selective forwarding of service requests associated with a virtual service to real servers to balance the load among those real servers.
Monitoring the health of real servers to bring them transparently in and out of service.
Monitoring the closure of non-persistent sessions so that new sessions can be recognized and sent to the best available server to achieve granular load balancing.
Monitoring the traffic activity of persistent sessions to time them out after a predetermined period of inactivity.
(In Hot Standby) Monitoring of link and redundant switch health to ensure continual availability of virtual services to clients and servers.
Layer 2 switching for traffic not associated with virtual services.

## Slide 8: Basic Frame Flow
DNS
(1) DEFINES POLICY
Network Manager
(3) SWITCH SELECTS BEST
SERVER BASED ON POLICY
(4) RESPONSE SENT TO
CLIENT VIA SWITCH
(2) DNS RESOLVES
INCOMING
REQUEST TO SWITCH
VIP 192.100.45.10
Port 80
10.10.10.1
10.10.10.2
10.10.10.3
Notes: Basic Frame Flow is:
Step 1. Network manager defines the policy
Step 2. Incoming request is resolved by DNS to web switch
Step 3. Web switch forwards request to server based on policy
Step 4. Response sent to client directly or via switch
BUT…..It’s important to understand the specifics of the frame flow between the client, the switch and the servers.
Client to switch (via VIP) communications:
User types in www.alteon.com in browser. Client resolves the IP address via normal DNS operation to 192.100.45.10.
Browser/stack issues a TCP SYN to 192.100.45.10 at TCP Port 80.
192.100.45.10 is really VIP running in an Alteon web switch.
Switch to server communications
The VIP receives the TCP SYN request for TCP Port 80, and inspects the frame.
The frame is valid: it is destined for a VIP configured in the switch, and for a TCP service the switch provides.
The switch “inspects” the number of current connections to each RIP in the group for this VIP, and picks the server best able to respond to the customer’s request, based on the switches configuration.
It translates the IP and MAC address destination fields of the frame to that of the chosen server, recomputes checksums, and forwards the frame using normal L2 forwarding techniques. In this case, the switch selects RIP 3, 10.10.10.3.
Server to client (via VIP) communications
The RIP server receives the TCP SYN frame which came from the client.
The frame looks like a normal client request, so it responds back with a SYN ACK connection establishment frame.
The switch intercepts the SYN ACK frame as it is being sent to the client, and translates the RIP address and server’s MAC address back into the VIP address and switch’s MAC address, so that the client thinks that it established a connection to the VIP.

## Slide 9: The Key to SLB: The Session ID
Key information recorded in the switch during SLB operations.
Notes: The combination of client IP address and the randomly generated source port will constitute an unique value. Since the same source port is required for communication for the entire TCP session, the session ID can be used to track frame flow for the entire TCP session.

## Slide 10: Session ID Substitution without PIP:Client to Server
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Vmac
Cmac
B62A
CIP
VIP
037A
2155
80
Client
Vmac
Cmac
B62A
CIP
VIP
037A
2155
80
Alteon Switch
Rmac
Cmac
48A0
CIP
RIP
C107
2155
80
Rmac
Cmac
48A0
CIP
RIP
C107
2155
80
Real Server
Notes: •A Session ID is the combination of the client’s IP address and TCP client port number. The switch uses the Session ID to record current client requests in its internal tables.•Since the client points to services using a Virtual IP (VIP) address, and the real servers each have their own real IP address, one of the key functions of a web switch is Session ID Substitution.
•The destination IP address of packets sent from the client is the virtual IP (VIP).
At the Layer 2 level, the VIP is associated with a MAC address, which we call the v_mac. Depending on implementation, each VIP may have a unique v_mac, or several can share the same v_mac. •The destination MAC address of the packet sent by the client is either the v_mac, if the client and web switch are on the same LAN, or the MAC address of a router which can forward the packet towards the web switch’s LAN. One way or another, a packet arrives a the web switch with destination IP address equal to VIP and destination MAC address equal to v_mac. •Through processes discussed below, the web switch makes a decision of which real IP (RIP) to send the packet to. As the packet passes through the web switch, the destination IP address is changed to RIP, the destination MAC address is changed to r_mac, the IP and TCP/UDP Checksums are adjusted, and (if port mapping is configured), the destination port number is changed.

## Slide 11: Session ID Substitution with PIP:Client to Server
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Vmac
Cmac
644B
CIP
VIP
A786
2155
80
Client
Vmac
Cmac
644B
CIP
VIP
A786
2155
80
Alteon Switch
Rmac
Pmac
823F
PIP
RIP
02C5
10420
80
Rmac
Pmac
823F
PIP
RIP
02C5
10420
80
Server

## Slide 12: Session ID Substitution without PIP:Server-to-Client
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Client
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Alteon Switch
Cmac
Rmac
823F
RIP
CIP
0A15
80
2155
Cmac
Rmac
823F
RIP
CIP
0A15
80
2155
Real Server
Notes: In the opposite direction, the real server IP (RIP) transmits packets with destination IP address of the client and destination MAC address of the client (or whatever router is being used to get to the client).
The web switch must determine whether packets arriving at server ports are associated with virtual services or native communication between end stations. The web switch makes that determination based upon the following rules:
If a service identifier (SID) has been recorded for the source IP/source port combination, the packet is associated with a virtual service.
If the source IP corresponds to a configured real server (RIP) address, and the packet is a fragmented UDP packet, the packet is assumed to be associated with a virtual service if UDP has been activated for the VIP the real server serves. Note that this rule and the next one imply a configuration limitation a fragmenting real server cannot be configured to support services associated with two different VIPs.
If the source IP corresponds to a configured real server address, and the packet is a fragmented TCP packet, the packet is assumed to be associated with a virtual service if any TCP service has been activated for the VIP the real server serves.
If, based upon the above rules, the packet arriving at the server port is deemed to be associated with a virtual service, the web switch changes the source IP address to the VIP, modifies the destination port number (if port mapping is configured), and adjusts the IP and TCP/UDP checksums. All other traffic is switched using Layer 2 processes.

## Slide 13: Session ID Substitution with PIP:Server-to-Client
TCP
IP
MAC
Dst MAC
Src MAC
IP Checksum
Src IP Address
Dst IP Address
TCP Checksum
Src Port
Dst Port
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Client
Cmac
Vmac
644B
VIP
CIP
761A
80
2155
Alteon Switch
Pmac
Rmac
823F
RIP
PIP
0A15
80
10420
Pmac
Rmac
823F
RIP
PIP
0A15
80
10420
Server

## Slide 14: SLB Topology Requirements
Switch performs address translation in both directions
  Therefore, frames associated with load balanced sessions must traverse the switch in both directions
Client-to-server --- client sends frames to the VIP address
Server-to-client --- two methods
  Topological
  Logical

## Slide 15: Configuration and Operations

## Slide 16: Configuration Components a.k.a - the things you have to configure to make it work
RIP addresses (two or more)
  Must enable
RIP group (one or more)
  Add RIP servers to the group
VIP address (one or more) and TCP/UDP ports
  Must enable
Enable client and server processing as required
Turn on SLB, apply and save - you’re done!
Notes: RIP – real IP, private addresses given to the internal servers
VIP – virtual IP, public address given to the web switch

## Slide 17: Basic Configuration
Notes: This reference configuration is used on the next few slides to exemplify configuration options.
This slide shows the simplest configuration where the same real servers (RIPs) are used to support two virtual services.
The two virtual services are 192.168.2.100/21 and 192.168.2.100/80 (VIP/dport).
All four real servers support each of these virtual services. The web switch balances load between these servers and monitors the health of these servers.

## Slide 18: Separate Real Server Groups
Notes: This example shows how the same two virtual services defined on the previous page can be configured in a different way - different real server pools per virtual service.
This approach may have server administration advantages - maintenance of content and protocols associated with HTTP on fewer servers and the same for FTP. This approach also allows the separation of server bandwidth decisions by protocol load. If there is a lot more HTTP traffic than FTP traffic, more real servers can be added to the 192.168.2.100/80 real server group to meet the demand with no impact on FTP administration.
The negative aspect of this approach is that if the traffic patterns ebb and flow between HTTP-oriented and FTP-oriented, fewer real sServers are available to service each protocol at any point in time.

## Slide 19: Multiple VIPs
Notes: This slide shows two examples.
In the first example, two separate real server pools are used to support two different virtual services (each with the same VIP).
In the second example, an important function called “port mapping” is exemplified. Port mapping allows different content, accessed using the same protocol (HTTP in this example), to be hosted on a single real server. From the client perspective, this is no big deal, they each just resolve a different VIP address for each domain name. However, from a real server perspective, since the destination VIP is stripped off by the web switch and replaced with the RIP, another method of “tagging” the incoming frame to know which HTTP process to forward it to is needed. Similarly, for traffic sent from the server towards the client, the web switch needs to know which domain the traffic is associated with in order to substitute the proper source IP address.
These needs are met via TCP “port mapping”. The real servers are administered for a unique port address per domain supported. In this case port 80 (native port number) is used for www.right.com and port 8001 is used for www.left.com for all real servers supporting that domain (not just the ones also supporting www.right.com).
In the client-to-server direction, destination port substitution is performed by the web switch. In the server-to-client direction, the local port numbers are changed back to port 80 (in this example) by the web switch.

## Slide 20: Back-Up and Overflow Servers
Real servers can be configured as backup/overflow servers for other real servers or virtual services
Backup servers are activated as overflow servers when the server(s) reach the maxconns threshold
Notes: Real servers can be configured as backup/overflow servers for other real servers or virtual services
  When backing up a real server, the backup server comes into service if the real server fails
  When backing up a virtual service, the backup server comes into service if all real servers in the virtual service group fail
Support for backup servers alone might be compelling reason for customers to invest in web switching
Backup servers are activated as overflow servers when the server(s) reach the maxconns threshold

## Slide 21: Back-Up Server Examples
Real Server Back-Up
Virtual Service Back-Up
Combination (w/ Port Mapping)
Notes: In the real server back-up example, server 4, is configured to be a back-up server for each of servers 1-3. In this example, if any of servers 1-3 fails, server 4 will come into service as a back-up. If the failed server comes back into service, server 4 will return to back-up status.
In the virtual server back-up example, server 4 is configured to be a back-up server for servers 1-3 in supporting a specified virtual service (HTTP for Domain Name www.left.com in this case). In this example, if each server 1-3 fails, server 4 will come into service as a back-up for the virtual service. If any of the failed servers come back into service, server 4 will return to back-up status.
The concept of real server back-up and virtual server back-up can be combined with port mapping. In the combinational example, the VIPs supporting www.left.com and www.right.com are port mapped for HTTP. Real server 1 supports www.left.com, real servers 2 and 3 support www.right.com, and real server 4 provides virtual back-up for both domain names.

## Slide 22: Basic Operations: Client-to-Server Traffic
Recognize received SYN packet addressed to a VIP (TCP connection request)
  Bind Session
  Session ID Substitution
Recognize successive packets associated with the same session and send to the same real server
Unbind upon reception of a FIN packet or time-out
Packets not addressed to a VIP are switched at L2
Notes: Recognize received SYN packet addressed to a VIP (TCP connection request)
  Bind the session to a real server (implement the load balancing algorithm)
  Implement session ID substitution and forward out appropriate physical port
Recognize successive packets associated with the same session and send to the same real server
  Implement session ID substitution and forward out appropriate physical port
Unbind upon reception of a FIN packet or time-out
  Details vary from protocol to protocol (see later section)
Packets not addressed to a VIP are switched at L2
Unbinding (or dis-association of a Client Session to a Server) is influenced by the “pbind” setting, or Persistent Bindings option which is settable on a service-by-service basis, and the “tmout” Inactivity Timeout timer, settable per real server.
The Activity Timeout timer is a fail safe mechanism to ensure unbinding if for some reason there is an on-going SYN/FIN count imbalance, which might be possible if multiple SYNs were required to initiate the connection. In this case, packet activity for a bound Session ID is monitored. If no activity occurs for the number of minutes indicated by the Activity Timeout Timer, the Session ID is unbound.
Half-open connections are rapidly aged, independent of the “tmout” setting
If the”pbind” option is set for a VIP, the Inactivity Timeout timer determines how long the switch waits to unbind a Session ID after the active connection has been terminated. For TCP services, session termination is observed by subtracting the number of FIN packet arrivals on a Server Port for that session from the number of SYN packet arrivals on a Client Port. When that number reaches zero, the connection is deemed to be complete.
If the “pbind” option is set, and there is no active connection associated with the given user, the Inactivity Timer will start to count down. If a new connection request (SYN) with a Source IP address that matches the existing SID arrives it will be bound to the same Real Server as the previous binding and the Inactivity Timer will be reset. If no new connection request (SYN) arrives with a matching Source IP by the time the Inactivity Timeout timer times out, the Session ID will be unbound.
The choices for the Inactivity Timer are between 2 and 60 minutes, with even numbers only.

## Slide 23: Basic Operations: Server-to-Client Traffic
All packets must be “watched”
Determine whether arriving packets are associated with virtual services or native communications
Implement session ID substitution if the packet is associated with a virtual service
Forward using L2 switching if the packet is not associated with a virtual service
Notes: All packets must be “watched” (there is no VIP addressing from server-to-client)
Determine whether arriving packets are associated with virtual services or native communications
  If a Session ID has been recorded for the source IP/source port combination, the packet is associated with a virtual service
  Special rules are needed for fragmented packets (see notes)
Implement session ID substitution if the packet is associated with a virtual service
Forward using L2 switching if the packet is not associated with a virtual service

## Slide 24: Load Balancing Options

## Slide 25: Load Balancing Algorithms
Load-based algorithms
  LeastConns
  Round Robin
Persistence-based algorithms
  Hashing
  Minimum Misses
Options
  Weights
  MaxConns
  Web OS API
Notes: Load balancing is attempted every time a new binding event occurs.
When a new binding event occurs, a decision can be made as to which real server to bind that connection to. Various methods can be used to drive that decision. The load balancing policy is a user configurable parameter.
Existing sessions are not redistributed between servers in a high-load situation.

## Slide 26: LeastConns Load Balancing
New connections are assigned to the server with the fewest active connections
Weighting option
Maximum connections option
LeastConns is the most often used policy
  Most self-regulating policy
Notes: LeastConns
In this policy, the number of active connections supported by each server is tracked. As new connections are received, they are forwarded to the server with the fewest active connections. This is often viewed as the “fairest” policy because those servers who can close connections faster due to inherent capacity or the nature of the content they are serving, will naturally get forwarded more connection requests over time.
Implementing this policy requires tracking the number of active connections for each real server.
Weighted LeastConns
Just as with weighted round robin, static weightings are provided to influence the amount of active connections provided to various servers when “in balance”. The idea is that servers with greater inherent capacity should support a larger number of active connections.
Round Robin, LeastConns Configuration Option - MaxConns
The MaxConns feature allows users to set the maximum number of active connections to be assigned to a particular server. When a server reaches MaxConns, it will receive no more connections until it either (a) drops back below MaxConns, or ALL servers are at MaxConns. When all servers are at MaxConns, new conenction requests are dropped until one or more servers drop below MaxConns

## Slide 27: Round Robin Load Balancing
New connections distributed in round-robin fashion
Weighting option
  Connections sent to servers in proportion to their weighting
Maximum connections option supported
Sometimes used temporarily as part of slowstart and other mechanisms
Notes: Round Robin
Each new connection request is sent to physical servers in a round robin fashion such that over time, each server gets the same amount of connection requests. This doesn’t mean that each server will have the same number of active connections. Some servers will close connections faster than others
No tracking of number of connections or traffic load is needed to implement this policy.
This is one of the most commonly used balancing policy used by customers today when the servers are roughly equal in their capacity.
Weighted Round Robin
Like round robin above, but each server is given a static weighting function which is based on some view of the capacity of each server. Servers are presented connection requests in proportion to their weighting relative to the total capacity of the system.
The default weighting is one. Other choices are ¼, ½, 2, 4, 8, 16, 32, and 64
As an example, suppose a customer has three servers A, B, and C, which are assigned the following weightings.
A1 (default)
B2
C1 (default)
Servers A and C will each receive ¼ of the incoming connection requests and server B will receive ½.

## Slide 28: Persistency Requirements
Successive connections must go to the same server
  Data associated with a user
  Caches requests
  Firewalls
  Secured HTTP connections via SSL
Notes:   Server has data associated with the user that is not dynamically shared with other servers
    E.g., users filling out forms, shopping carts, search engines
  Caches where successive requests for same content should go to same server
  Firewalls where successive connections must traverse the firewall that has authenticated the user
  Secured HTTP connections via SSL
    e-commerce applications where users enter credit card and personal information

## Slide 29: Server Binding Mechanisms
Immediate Binding
  Decision about which real server to send the request to is made upon arrival of the TCP SYN packet
Delayed Binding
  Decision about which real server to send the request to is made after the TCP 3-way handshake is complete

## Slide 30: Immediate Binding Persistency-Hashing
Source IP address used to generate an index into a table containing all servers in group
All requests from same user are sent to same server
  True as long as no servers enter or leave group
  Useful in e-commerce applications and FLB where state must be maintained across multiple TCP sessions
Table recomputed when a server leaves or enters group
  Existing connections not rehashed if their server is up
Weighting has no effect
Maximum connections option supported
Notes: Choosing the HASH algorithm has the affect of distributing server load on a statistical basis across the available real servers. The amount of “load balancing” that occurs is totally based upon the number and distribution of the IP addresses that serve as endpoints for each session. Small numbers or uneven distributions of IP addresses will result in a uneven or skewed distribution of connections between all servers.
This SLB method is preferred over MinMisses.
For each new connection processed by the hash function, either the frame’s IPSA, IPDA, or the IPSA and IPDA have a hash algorithm executed on them to determine the server that will receive the connection. Once the server is determined, that connection is associated with the chosen server until the connection/session closes.
Specific Config Behaviors
  Hash occurs on IPSA only (IPDA will be the VIP, and constant)
  This option is VERY useful to emulate persistent connections, as an alternative to PBIND. The same user will be sent to the same server, unless that server is unavailable.
  This option has the added benefit of emulating “session persistence” across switches in a hot-standby configuration. If a hot-standby swap-over occurs, the users accessing the VIP will still be sent to the same real servers. The benefit is that existing open sessions between users and servers can be “maintained”, so that users experience TCP resets from servers, or have their sessions abnormally terminated.
  Reaching MaxConns limit on a server results in the “next” server being chosen

## Slide 31: Immediate Bindings Persistency - MinMisses
Similar to hash in that source IP address used to generate an index into a server table
Unlike hash, when a server leaves the group, the table is recomputed to reassign only the failed server’s users
Weighting has no effect
Maximum connections option supported
Notes: Similar to hashing, choosing the MinMisses algorithm has the affect of distributing server load on a statistical basis across the available real servers. The amount of “load balancing” that occurs is totally based upon the number and distribution of the IP addresses that serve as endpoints for each session. Small numbers or uneven distributions of IP addresses will result in a uneven or skewed distribution of connections between all servers.
Hash is a preferred SLB method instead of MinMisses.

## Slide 32: Using Hashing and MinMisses
Hashing offers more even distribution of connections across servers than minmisses
Minmisses results in less disruption of server assignments when a server fails
All clients coming from behind a proxy may use the same source IP address
  Traffic from all clients is sent to the same server, defeating load balancing
If load distribution uneven, try SSL session ID tracking or cookie-based tracking

## Slide 33: Persistence Mechanisms Using Delayed Bindings
SSL session ID load balancing
Cookie-based load balancing
Discussed further in the Alteon Certified Engineer Course

## Slide 34: Web OS API
The API provides an interface to Alteon Web Systems switches that allows external devices (such as a server management workstation running a process daemon) to dynamically control switch parameters
Notes: The API provides an interface to Alteon WebSystems switches that allows external devices (such as a server management workstation running a process daemon) to dynamically control switch parameters, including –
  Server weight
  Server maximum connections
  Server availability* (server online/graceful offline/immediate offline)
  Server group membership (what servers are serving what applications)
  Filter manipulations:
    Examples
      Add permanent filters to perform a REDIR, ALLOW, or DENY action.
      Add dynamic/temporary filters, i.e., an ALLOW filter to prevent traffic from going to a cache

## Slide 35: Server and Service Failover and Start-Up

## Slide 36: Server and Service Monitoring
Detecting failed servers and services and directing new requests to healthy devices is the #1 value of load balancing
Issues
  Probability of failure detection
  Probability of false alarm
  New, healthy service start-up
  Granularity of fail-over domains

## Slide 37: Multi-Level Health Checking
Physical layer mechanisms
ICMP pings
TCP connection requests
Content-based health checks
Service groups available for TCP and content health checks
Network manager configures type of health check to use

## Slide 38: Physical Layer Mechanisms
Web switch monitors physical link status of switch ports connected to real servers
If the physical link to a real server goes down, switch immediately marks the server as failed
  No new connection requests forwarded to server
  Does not forward any more traffic associated with existing sessions to that server
  Immediately removes all existing sessions bound to that real server from its binding table

## Slide 39: ICMP Ping-based Health Checks
Switch sends ICMP pings to servers and listens for response
Interval between attempts is user-configurable
User-configurable number of consecutive failures puts the server into the failed state
Recommended when all IP traffic or a UDP application other than DNS is load balanced

## Slide 40: TCP-based Health Checks
Layer 4 connection requests (TCP SYN requests) sent to each configured service on each server
Interval between attempts is user-configurable
When connection request succeeds (switch receives TCP SYN response), connection is quickly closed (switch sends TCP FIN request to server)
User-configurable number of consecutive failures puts the service (group) into the failed state

## Slide 41: Content-based Health Checks
HTTP
  Executes an HTTP GET command on the target server
  Verifies that the configured health check content URL (index.html, /cgi-bin/test.html, etc.) results in a valid return code of “200 OK”
POP3
  Executes a USER and PASS command on the target server
  Verifies that the configured health check content USER:PASS (bert:mypass) combination exists on the server
  Return code of “+OK” is expected during login.
SMTP
  Executes a VRFY (verify) command with the configure USERNAME against the target server
  Defined health check content is username
  Return code of 250 is expected
WSP
  WSP/UDP packet is sent to WAP gateway
  If expected response does not match the byte string, the gateway fails the healtcheck
Notes: WSP – wireless session protocol. When unencrypted, WSP is connectionless and Alteon switches can provide connectionless WSP health checks. Wireless devices communicate with Wireless Application Protocol (WAP) gateways using WSP.

## Slide 42: Content-based Health Checks (cont’d)
NNTP
  Executes a GROUPLIST command against the target server
  Uses the defined health check content newsgroup name (like comp.dcom.lans.ethernet)
  Return code of 211 is expected
FTP
  Executes a SIZE command against the target server
  Uses the defined health check content filename
  Server must allow anonymous logins
  Return code of 213 is expected
DNS
  Executes a DNS Resolve command against the target server
  Uses the defined health check content of hostname
  Expect successful getByHostname return of an IP address

## Slide 43: Content-based Health Checks (cont’d)
IMAP
  Admin configures Username:Password
  Switch contacts IMAP server and executes LOGIN command to verify server availability
  Switch expects “OK” in cleartext
RADIUS
  Admin configures the shared secret on both the switch and the RADIUS server, up to 16 alphanumeric characters
  Also configures a username:password
  Switch executes “Access-Request” to the RADIUS server, using appropriate protocols and info above
  Switch expects “Access-Accept” message, else the server is unavailable
SSL
  Verify that the SSL process responds to client Hello requests
  Enhance SSL health checks by verifying that the SSL process responds to client Hello requests

## Slide 44: Service Groups
Concept of service groups supported for TCP and content-based health checks
User configures real server group for each desired service group
User places one more service in each service group
Interval between attempts is user-configurable
When connection request succeeds (switch receives TCP SYN response), connection is quickly closed (switch sends TCP FIN request to server)
User-configurable number of consecutive failures puts the service (group) into the failed state

## Slide 45: Bringing Servers/Services Into Service
Servers and service groups in failed state are regularly checked to see if they are healthy
  For UDP or when configured, health checks use L3 pings
  Otherwise, health checks use L4 connection request (and content check, if configured)
  Individual service groups brought back on-line as successful connection attempts have been achieved to all services in the group
Slow-Start
  Load balancing policy temporarily switches to round robin for all VIPs associated with the real server
  Avoids flooding the new server/service

## Slide 46: Configuring and Monitoring Server Load Balancing

## Slide 47: Configuring SLB with the CLI

## Slide 48: Configuring SLB with the CLI (cont’d)

## Slide 49: Configuring SLB with the CLI (cont’d)

## Slide 50: Configuring SLB with the CLI (cont’d)

## Slide 51: Configuring SLB with the CLI

## Slide 52: Server Load Balancing (SLB) Summary
Alteon web switches support SLB functionality for improved performance, scalability and availability
Reviewed a client/server HTTP session for SLB services
Reviewed configuration and operation of SLB
  Real servers and IP addresses
  Assignment of RIPs to a real group
  Create a Virtual IP (VIP) for the group
  Enable client and server processing
  Turn on SLB, apply and save
Reviewed SLB statistics