## Slide 1: Firewall Load Balancing

## Slide 2: Firewall Load Balancing Objectives
Upon completion of this module, the student should be able to:
  Understand firewall load balancing concepts
  Understand two and four switch firewall load balancing operations
  Configure a two switch firewall load balancing implementation (sandwich)

## Slide 3: Firewall Load Balancing
Redirect incoming and outgoing traffic to group of firewalls
Automatic load balancing across multiple firewalls
Filter packets at ingress port so firewalls see only relevant packets
Benefits:
  Increase firewall performance
  Reduce response time
  Redundant firewalls ensures Internet access
Campus LAN
Load-sharing, redundant firewalls
External servers

## Slide 4: FWLB Concepts
FLB is an extension of application redirection where all IP traffic is redirected
Uses hash metric
ICMP or HTTP health checks
Static routes for health checks
FW 1
Redir
Filter
Redir
Filter
FW 2
Notes: The concept of firewall load balancing rests with the redirection filters. The redirection filters exist on the ports that are not connected to the firewalls. Their job is redirect all information that they receive to the firewalls. The firewalls will then filter all packets they receive and forward them to the other side of the network. There is a redirection filter required for each direction of data flow. This allows all incoming and outgoing communications to be directed to the other side via the firewalls.

## Slide 5: Notes on Hash Metric
For SLB, uses the IPSA
For WCR or FTP redirection, uses the IPDA
For FWLB, uses both the IPSA and IPDA
Notes: Hash algorithm uses different parameters based on the type of load balancing or application redirection selected
When used with a VIP for SLB, the algorithm uses only the IPSA
  All requests from the same client are sent to the same real server
  Used to maintain client session persistency
When used with HTTP or FTP redirection filter, only IPDA is used
  Improves hit rate by sending all requests for same site to same cache
For any other criteria, both the IPSA and IPDA are used
  Maintains session persistence and symmetry for firewall load balancing

## Slide 6: Two-Switch: FWLB Configuration
Internet,
Web Servers
Secured Network
Clients
Alteon Switch
Firewalls
Alteon Switch
Firewall Sandwich
Notes: The firewall sandwich is scalable. The customer is not limited to a single or a hot standby firewall. All of the customer’s firewalls can be actively used. This allows the customer to scale the number of firewalls (and the amount of filtered throughput) to meet their requirements.

## Slide 7: Two-Switch: FWLB Data Flow
Internet,
Web Servers
Secured Network
Clients
Alteon Switch
Firewalls
Alteon Switch
Client data enters clean side switch
Data is redirected by
the entry port to the firewalls
Client data exits dirty side switch
Notes: Traffic hits redirection filter at ingress to firewall sandwich
Hash metric sends traffic to the clean side based on the IPSA and IPDA
Traffic arrives on the clean side and is processed
Traffic hits redirection filter on the egress switch
Hash metric ensures that the firewall that is used for ingress is used for egress (again, based on the IPSA and IPDA), preserving session state on the firewalls

## Slide 8: Two-Switch : FWLB Health Check Flow
Internet,
Web Servers
Secured Network
Clients
Alteon Switch
Firewalls
Alteon Switch
ICMP health checks pass through the firewalls to the opposing switch to detect if firewall is up
Notes: Health checks are not performed on the firewalls but through the firewalls.
Either switch checks L3 interfaces on the opposite side switch.
If the health checks on the opposite side switch pass, the customer is sure that the firewall is working properly.

## Slide 9: Redirection Filters
Redirection filter on all ports not connected to firewalls on both switches
Sample redirection filter
/cfg/slb/filt 200/sip any/smask 0.0.0.0/dip any/dmask 0.0.0.0
/cfg/slb/filt 200/proto any
/cfg/slb/filt 200/log disabled/actio redir/ena
/cfg/slb/filt 200/group 1/rport 0
Local access filter
/cfg/slb/filt 100/sip A.0/smask 255.255.255.0/dip A.0/dmask 255.255.255.0
/cfg/slb/filt 100/proto any
/cfg/slb/filt 100/log disabled/actio allow/ena
FW 1
Client
FW 2
A.1
A.10
B.10
B.1
D.1
D.10
C.1
C.10
Switch 1
Switch 2
Filters
Filters

## Slide 10: FWLB Health Checks
FW 1
Server
Client
FW 2
A.1
A.10
B.10
B.1
D.1
D.10
C.1
C.10
Switch 1
Switch 2
B.1
D.1
C.1
A.1
Each switch checks opposite side switch
  Opposite’s interfaces treated as RIPs
  Opposing interfaces must be assigned same real server number (A1=B1=RS1)
  Switch has static routes to opposite side switch real servers
Notes: Firewalls must allow pings between interfaces on clean-side and dirty-side switches
ICMP health check method
Opposing switch interfaces (not firewall interfaces) are configured as RIPs and checked
  Ensures that complete path to other switch is passing traffic
Static host routes to opposing interfaces are defined on each switch
  Switch 1: static route - B.1 via A.10
  Switch 1: static route - D.1 via C.10
  Switch 2: static route - A.1 via B.10
  Switch 2: static route - C.1 via D.10

## Slide 11: Four-Switch: FWLB Configuration
Offers a higher level of fault tolerance because there are no single points of failure
Firewall Farm
Internet
Secured Network

## Slide 12: Bridging Firewalls
Supported for two and four switch configurations
Internet,
Web Servers
Secured Network
Clients
Alteon Switch
Firewalls
Alteon Switch
Firewall Farm
Internet
Secured Network

## Slide 13: Configuring FWLB
Create an appropriate set of filters and enable them
  Local access filters
  Filters to prevent falsely successful health checks
  Redirection filters
Client and server processing do not have to be enabled
Configure static routes to opposing switch interfaces
Configure the opposing switch interfaces as real servers and place them into real server group, selecting hash as the metric
Apply the local access and redirection filters to the clean and dirty network ports and enable filtering on those ports
Apply the health check filters to the appropriate ports on the inside of the sandwich
Turn on server load balancing
Apply, save and you’re done!

## Slide 14: Filter Ordering
Filters are processed in order according to filter number
Place exclusionary rule or bypass rules first
  Forward traffic that does not get redirected (ALLOW rules)
  Drop traffic that is not to pass through the switch (DENY rules)
Place high hit rate rules next
  Web cache redirection, DNS redirection, etc.
Default filter last
  A global filter to ALLOW, DENY or REDIRECT all traffic

## Slide 15: A Note on NATing Firewalls
Running NAT on the firewalls interferes with proper hash algorithm operation
Configure a PIP on each port on the inside of the firewall sandwich and configure filters to enable source NATing
Configure allow filters on the clean and dirty ports
  If IP DA of incoming frame = PIP address, allow the frame to go to the PIP without being redirected

## Slide 16: Basic FWLB Summary
Alteon switches provide firewall load balancing for increased performance and firewall redundancy
Reviewed Alteon firewall load balancing options
Reviewed Alteon FWLB configuration
  Define redirection filters
  Configure SLB with opposite switch interfaces as RIPs
  Define static routes through firewalls
  Enable SLB
  Apply and save
Discussed FWLB troubleshooting