## Slide 1: Alteon VRRP
(Virtual Router Redundancy Protocol)

## Slide 2: VRRP Objectives
Upon completion of this module, the student will be able to:
  Understand layer 3 and layer 4 redundancy
  Understand active-standby and active-active configuration
  Configure virtual interface routers
  Configure virtual service routers

## Slide 3: High Availability in Web OS
Alteon provides the option of configuring a survivable L3 and L4 interface in case of switch failure
  Virtual default gateway
  Virtual VIP
Active-standby and active-active redundancy
  Supports Virtual Router Redundancy Protocol (VRRP)
  Supports Alteon extensions to VRRP

## Slide 4: VRRP and Alteon WebOS
VRRP
  Allows multiple routers/switches to be active at the same time
  RFC 2338 supports layer 3 redundancy only
Alteon extensions to VRRP
  Supports Layer 4 redundancy with Virtual Server Routers (VSR)
Notes: VRRP
  Based on RFC 2338
  Similar to Cisco’s HSRP
  Allows multiple routers/switches to be active at the same time
  Supports layer 3 redundancy only
Alteon extensions to VRRP
  Supports Layer 4 redundancy with support for Virtual Server Routers (VSR)
  Sharing of interfaces supports active-active configurations
  Tracking to modify priority of a VRRP router based on dynamic state of the switch when sharing not used

## Slide 5: Redundant Operation Modes
Active-standby
  All switches actively perform load balancing and/or routing functions, but for different virtual services and/or interfaces
Active-active
  All switches can actively forward traffic for the same virtual services and/or interface
Hot Standby
  One master with one or more backups. Only master processes layer 4 traffic
Notes: No limit on number of switches in redundant setup
Configuration synchronization
  Each VRRP-capable switch is autonomous
  No automatic synchronization of configurations
Topology requirements
  Bridging loops
  Simultaneous frame processing
Health monitoring of virtual interfaces (L3 and VIP) based on VRRP advertisements

## Slide 6: Hot-Standby Redundancy
Active for Service #1
Active for Service #2
Active for Service #3
Standby for Service #1
Standby for Service #2
Standby for Service #3
…….
Internet
Active
Standby
Master
Backup

## Slide 7: Active-Standby Redundancy
Active for Service #1
Standby for Service #2
Active for Service #3
Standby for Service #1
Active for Service #2
Standby for Service #3
…….
Internet
Active
Active
Master
Backup
Notes: Although both switches are processing packets at the same time, only one switch is actively processing packets for any one service at any time. Notice that on switch 1 (left switch), service 1 and service three are active there while on switch 2 (right switch), service 1 and service 3 are in standby. Switch 2 is active also, but only for service 2, which is being backed up by switch 1. Note however, both switches are working however. The standby switch is forwarding frames to the active switch. But only the active switch is processing L3 and L4 frames.

## Slide 8: Active-Active Redundancy
…….
Internet
Active
Active
Active for Service #1
Active for Service #2
Active for Service #3
Active for Service #1
Active for Service #2
Active for Service #3
Master
Backup
Notes: In contrast to Active Standby, Active-Active allows both switches to actively process L3 and L4 frames on both switches. Note that the master switch (left switch) is actively processing frames for services 1, 2 and 3 and the backup switch is actively processing frames for services 1, 2 and 3 also.

## Slide 9: Layer 3 Redundancy
Physical L3 Interfaces
if #1 = 10.10.10.11
if #2 = 10.10.20.11
Internet
Server 3
IP #3 = 10.10.20.3
IP #4 = 10.10.20.13
DefGW = 10.10.20.100
Physical L3 Interfaces
if #1 = 10.10.10.10
if #2 = 10.10.20.10
Server 1
IP #1 = 10.10.10.1
IP #2 = 10.10.10.11
DefGW = 10.10.10.100
Active “Virtual” L3 Interfaces
10.10.10.100
10.10.20.100
Server 2
IP #1 = 10.10.10.2
IP #2 = 10.10.10.12
DefGW = 10.10.10.100
Server 4
IP #3 = 10.10.20.4
IP #4 = 10.10.20.14
DefGW = 10.10.20.100
Notes: In this example, we are dealing with L3 interfaces. L3 redundant interfaces can be seen as virtual default gateways. If the master virtual L3 interface fails, the virtual L3 interface on the backup switch takes over. Note that the switch handles multiple virtual L3 interfaces. Also note the default gateways on the servers. They are set to the virtual L3 interface. If there is a failure of the master switch, the backup switch takes over seamlessly without any required changes to the servers.
The added benefit of Active-Active allows both switches to process frames simultaneously.

## Slide 10: Layer 4 Redundancy
Active VIP #1
VIP = 205.178.13.100
Active VIP #2
VIP = 205.178.13.200
…….
Internet
Active VIP #1
VIP = 205.178.13.100
Active VIP #2
VIP = 205.178.13.200
VIPs on both switches
are active at the same
time
Notes: With L4 redundancy, we have “virtual VIPs”. As with L3 redundancy, if the master switch is lost, the backup switch will be able to process any client requests to the VIPs represented.

## Slide 11: Advantages: Active-Active Setup
Increase availability
  L3 or L4 interfaces supported on two or more switches
  Continued operation in event of switch failure
Increase performance
  OSPF load sharing for incoming traffic
  Default gateway load sharing for outgoing traffic
  Increased processing power to handle traffic spikes
Group 1
VIP #1:active
VIP #2:active
VIP #1:active
VIP #2:active

## Slide 12
Virtual Router Redundancy Protocol (VRRP)
and Web OS Extensions

## Slide 13: VRRP Terminology
VRRP Router
  A router running VRRP, e.g., an Alteon switch
Virtual Router (per RFC 2338)
  Virtual interface that represents a set of IP addresses
Virtual Interface Router (Alteon terminology)
  A Virtual Router supporting layer 3 interfaces
Virtual Server Router (Alteon terminology)
  A Virtual Router supporting layer 4 (VIP) interfaces
Virtual Router ID (VRID)
  Unique within a LAN
  Used for building the Virtual Router MAC address

## Slide 14: VRRP Terminology (cont.)
IP Address Owner
  A VRRP router where the associated L3 interface’s IP address equals the VRRP interface’s IP address
  Maximum of one per virtual interface router
IP Renter (Alteon terminology)
  A VRRP router that is not an IP address owner
Virtual Router Master
  Answers ARP requests
  VRRP router that forwards packets sent to the virtual router
Virtual Router Backups
  VRRP routers available to assume forwarding responsibility for a virtual router if the master fails

## Slide 15: Virtual Router MAC Address
First five octets are the standard MAC prefix for VRRP packets as defined in RFC 2338
VRID becomes the final octet
00-00-5E-00-01-02 for VRID = 2

## Slide 16: VRRP Terminology
Internet
Internet
VRRP Router
VRRP Router
VRID = 1
VR IP address = 205.178.13.226
MAC address = 00-00-5E-00-01-01
Priority = 255
VRID = 1
VR IP address = 205.178.13.226
MAC address = 00-00-5E-00-01-01
Priority = 100
Virtual Router (VR) #1 Master
Virtual Router (VR) #1 Backup
Host #1
Default Gateway = 205.178.13.226
Host #2
Default Gateway = 205.178.13.240
VRID = 2
VR IP address = 205.178.13.240
MAC address = 00-00-5E-00-01-02
Priority = 100
Virtual Router (VR) #2 Backup
VRID = 2
VR IP address = 205.178.13.240
MAC address = 00-00-5E-00-01-02
Priority = 255
Virtual Router (VR) #2 Master

## Slide 17: VRRP: Advertisement Messages
Used for negotiation to determine the master
Only the master sends advertisement messages
Backup failure operation
Advertisement interval
Notes: If backups do not receive an advertisement messages by a timeout period
  Backups assume the master is dead
  Backups negotiate with each other to elect a master
  Backup with the highest priority becomes the master
Advertisement interval
  Default is 1 second
  Ranges from 1 - 255 seconds

## Slide 18: Web OS Extensions to VRRP
Virtual Server Routers (VSRs)
Sharing of interfaces
Tracking
Notes: Virtual Server Routers (VSRs)
  Support VIPs
  Only Master VSR responds to ARPs
Sharing of interfaces
  Supports active-active configuration
  Discussed in Alteon Certified Engineer course
Tracking
  Modifies priority of a VRRP router based on dynamic state of the switch
  Discussed in Alteon Certified Engineer course

## Slide 19: Priority and Preemption
Priority
  Used to determine which is the master router
  VRRP router with highest priority will be the master
Preemption
  Allows higher priority virtual router backup to preempt the master router and become the master router
Notes: Priority
  Used to determine which is the master router
  Ranges from 1-254 for renters
  Per standard, owner’s priority is 255
  Default setting is 100
  VRRP router with highest priority will be the master
Preemption
  Allows higher priority virtual router backup to preempt the master router and become the master router

## Slide 20
Configuration and Operations

## Slide 21: Configuring VRRP
Configure L2 and L3 parameters on all VRRP routers
Setup Layer 4 parameters on one of the switches
Define all filters needed
Setup the VRRP parameters on the switch
Synchronize layer 4 and VRRP configurations
Modify configurations if necessary
Notes: Configure L2 and L3 parameters on all VRRP routers
  VLAN, L3 interfaces, default gateways, DNS …etc.
  Turn VRRP and SLB on
Setup Layer 4 parameters on one of the switches
  RIP, server group, VIP, etc.
Define all filters needed
Setup the VRRP parameters on the switch
  Layer 3 and Layer 4 (VIP) interfaces, …etc.
Synchronize layer 4 and VRRP configurations
  Need to explicitly “push” configurations to other VRRP capable switches
Modify configurations if necessary
Use the synchronize command with caution:
Synchronization will cause the switches to have exactly the same layer 4 configurations
This may or may not be the desirable behavior
Each VRRP router does not necessary have the same layer 4 configurations

## Slide 22: Configuring VRRP with the CLI

## Slide 23: Active-Active Redundancy FAQ
VRRP capable switches are autonomous, therefore they can have different configurations
Use caution when performing configuration synchronization

## Slide 24: VRRP Summary
Alteon switches provide L3 and L4 redundancy, as well as support for sharing interfaces (Active-Active feature)
Reviewed VRRP operations and services
Reviewed VRRP configuration