## Slide 1: Switch Troubleshooting

## Slide 2: Troubleshooting Objectives
At the completion of this module, the student shall be able to:
  Recognize and troubleshoot:
    Switch bootup issues
    Switch management issues
    Link issues
    Switch panic issues
    Connectivity issues
    L4 issues
  Use L3 and L4 CLI commands to gather troubleshooting information

## Slide 3: Bootup Issues
If the switch will not boot
  Check LED patterns
  May need to do a serial download
If the switch will boot but generates errors during bootup
  Boot image wrong or corrupt
  Bad CRC
  Could not read active/backup config blocks

## Slide 4: Switch Management Issues
If the user:
  Cannot ping the switch IP interface(s)
  Cannot telnet to the switch IP interface(s)
  Cannot bring up the WebUI
  MIB browser cannot discover the switch
  Switch does not log messages to the syslog host
  Switch does not send SNMP traps
This could be an indication of L2 issues

## Slide 5: Link Issues
Apply basic troubleshooting techniques
  Check cable (could be wrong type or a bad cable)
  Check link negotiation (especially for Gigabit connections)
  Check for port configuration mismatches on either end of the connection (speed/mode/fctl)
  Check LED status
Alteon specific techniques
  Use the /info/link command
  Use the /stats/port #/link command

## Slide 6: Panic/Crash/Hang Issues
Recognizing a core dump
  Switch resets
  Banner
Forcing a panic
  /maint/panic
Forcing a switch panic should only be done when requested by tech support
Hard reset
  /boot/reset hard

## Slide 7: Collecting Core Dumps
Ensure terminal logging is turned ON prior to initiating this command
  /maint/dump

## Slide 8: Trace Buffers
Trace buffers are used to selectively track activities the management processor (MP) and switch processors (SPs) perform while the switch is in operation.
Extract MP trace buffer
  /maint/debug/tbuf
Extract SP trace buffer
  /maint/debug/sptb <port-number>
Tracing levels and tracing events can be set or reset at run time (/maint/sys/tmask)

## Slide 9: Connectivity Issues
Flaky port connections
  check port statistics and look for error counters, for example
    /stats/port <port-number>/ether
    /stats/port <port-number>/if/ifInErrors
  check link on either ends (refer to Link Issues)
  check STP states
  check LED patterns
  note changes after disconnecting/connecting cable and/or resetting the switch

## Slide 10: Utilization Issues
Heavy CPU and session utilization can slow performance
  To view port CPU utilization
    /stats/port X/cpu
  To view management processor utilization
    /stats/mp/cpu
Notes: CPU and Session utilization measurements can help an administrator determine how much head room they have for expansion and capacity planning.

## Slide 11: L4 Issues
Clients cannot access the real server’s service port directly
  security feature
  use port mapping, PIP on client-side port or
  direct access mode (DAM)
Periodic L3 health check failures
  check IP interfaces on both ends
Periodic L4 health check failures
  check if service is up and running
  might need network traces between Alteon and the real servers
Periodic content based health check failures
  verify that the requested http object is present on the real server(s)

## Slide 12: L4 Issues (cont.)
Clients cannot contact the VIP
  Make sure client and server processing are enabled on the appropriate ports
  Ensure the VIP is enabled
  VIP needs to be ‘well known’
  Can be an upstream Layer 2 ARP cache or forwarding database (fdb) issue
Cannot telnet to the switch
  Make sure the concerned interface is enabled
  Make sure the station you are telneting from is within mnet/mmask range

## Slide 13: L4 Issues (cont.)
Clients cannot access the services through the VIP when the real server(s) are marked operational
  Possible condition with L3 health checks, service could be down but server might be UP
VRRP and VIP issues
  Break connectivity to the VIP when VRRP is disabled and the upstream L2 device still has the VRMAC cached (even though the VMAC now needs to be used for the VIP/VSR IP address)
  Flush the upstream L2 devices cache or wait for the VRMAC to age out and be replaced by the VMAC

## Slide 14: L4 Issues (cont.)
VRRP and Web UI: Get Web UI when going to VSR. Occurs when VRRP VSR created before its associated VIP.
  Reset the switch or reconstruct the VSR/VIP in the right order (VIP before VSR).
Customer complains about sessions not being “evenly” distributed between constituent real servers
  Need to explain the metric being used as it may not be very apparent by looking at the statistics

## Slide 15: L4 Issues (cont.)
Web cache redirection issues
  Configure transparency on the cache server or full-NAT on the switch
Filters not working
  Enable filters and/or enable filtering on the port
Redir filter that specifies a dip does not work. The switch does not respond to ARPs for a DIP specified in a redir filter

## Slide 16: Layer 2 : Useful CLI Commands
/info/sys
/info/link
/info/fdb/dump
/info/arp/dump
/cfg/dump
/stats/port <num> <ether/if/link>
/stats/if <num>

## Slide 17: Layer 4 : Useful CLI Commands
/info/slb
/info/dump
/cfg/slb/cur
/cfg/dump
/stats/slb/group <real-server-group-number>
/stats/slb/real <real-server-number>
/stats/slb/virt <virtual-server-number>
/stats/slb/maint

## Slide 18: Useful Tips
For syslog hosts, make sure that rpcbind services are running. Otherwise, the switch will not log messages to syslogd
Active-FTP load balancing will not work if PIP is configured on the “client” ports

## Slide 19: Troubleshooting Summary
Alteon provides the user with a full suite of troubleshooting tools within the switch
Other network management tools (such as syslogd and network analyzers) can be used to further troubleshoot a problem