## Slide 1: Web Cache Redirection (WCR) and Application Redirection (AR)

## Slide 2: What is Web Caching and Why Do I Care?
Store Web content close to user
Improve user response time and satisfaction
Reduce traffic from campus to ISP POP (if cache in corporate campus)
Reduce traffic from ISP POP to Internet backbone (if cache in ISP POP)
Notes: So, we should begin at the beginning. What is web caching and why should anyone care about it?
The basic idea behind web caching is to store frequently accessed web pages close to users. This improves user response time by 1) allowing the user to access web pages without traversing the Internet and it’s potentially slow WAN links and 2) increasing the total server processing available to popular web pages by storing their content on many servers (web caching essentially implements a distributed processing system).
In the enterprise environment, caches are deployed on campus networks, reducing costs by reducing the amount of traffic that has to get to the Internet or across private WAN links. In the ISP environment, caches are deployed in POPs, reducing costs by reducing the amount of traffic that has to get to the Internet backbone.
So caching is a good example of a win/win situation. Users are happy because they get better response and the folks providing service are happy because they get lower costs.

## Slide 3: Basic Cache Operation
Cache receive requests for web page
If cache has the page stored locally, it sends the page to the requestor without having to get it across the Internet from the server hosting the site
If cache does not have the page stored locally, it
  Goes to the Internet to get the page from the server hosting the site
  Sends the page to the requestor
  Stores the page locally so that future requests for it can be handled from the cache
Notes: Now let’s talk about how basic caching systems operate. First, the cache has to receive a request for a web page. This happens either because a browser has send a request directly to the cache or because a requested generated by a browser to a server hosting a web page has been intercepted and redirected to the cache. This will be discussed in more detail in the next several slides.
Once the cache has received a request for a web page, it checks to see whether or not it has the requested content. If it has the content, it sends it directly back to the requestor. If the cache does not have the requested content, it sends a request across the Internet to retrieve the content. When it receives the content from the server that hosts the content, it relays the content back to the requestor and caches the content so that future requests for the same content can be handled from the cache.
Caching solutions use a variety of mechanisms to ensure that content is current. At a minimum, they must use some sort of LRU algorithm to remove content when memory gets full. More sophisticated caches use other mechanisms such as timeouts on content and checking with the source of the content to ensure currency.

## Slide 4: Web Cache Systems Without Redirection
Proxy caching
  Browsers send requests for web pages to cache instead of server hosting web site
Transparent proxy caching
  Browsers send requests for web pages to server hosting web site
  Cache sits in data path, examines all packets bound for the Internet, intercepts web traffic and processes web requests
Notes: Caching solutions use one of three deployment options to ensure that requests for web pages go to the cache and not the server hosting the content.
The first option is called proxy caching. With proxy caching, browsers are configured to send requests for web pages directly to the cache instead of to the web server hosting the content.
The second option is called transparent proxy caching. With transparent proxy caching, browsers send requests for web pages to the web server hosting the content, as usual. The cache itself sits in the data path, examines all packets bound for the Internet, intercepting and servicing the web traffic (i.e., any traffic with a TCP destination port equal to 80, the well-known port for HTTP). Sitting in the data path can be accomplished by locating the cache somewhere in the physical data path, usually around the last router hop before the WAN, and configuring it as a router hop or by configuring the client’s to use the cache as their default router. It’s best to put the cache as close to the WAN as possible so that intranet traffic can be served from the hosting servers and not the cache.
The third option is another form of transparent proxy caching that adds another component called a web cache redirector. Transparent proxy caching with web cache redirection removes that caches from the data path. Another device, usually a LAN switch or router, sits in the data path, examines all packets bound for the Internet, intercepts the web traffic and sends it to the cache for processing.
Now, let’s take a closer look at each of these options and their pros and cons vis-à-vis the ideal caching solution outlined earlier.

## Slide 5: Web Cache Redirection: The Alteon Solution
Intercepts and redirects Internet requests to a group of cache servers
HTTP requests are rapidly inspected and forwarded to the appropriate cache server
Cache IP destination address (DA) is used to maximize cache hits
Frame modification – Destination MAC with Cache MAC
Notes: Alteon’s application redirection software automatically intercepts HTTP requests destined for the Internet and forwards them to a transparent proxy cache
HTTP requests are rapidly inspected and forwarded to the appropriate cache server
The only frame modification is to replace MAC DA with the appropriate cache servers’ MAC address.
With Full NAT option, caches may be across a routed network
  Can also use to remove the transparency software from the cache
The cache to redirect to is chosen by executing a function on the IP DA, which results in maximizing the cache hit rate

## Slide 6: Cache Redirection
Without Redirection

## Slide 7: Cache Redirection
With Redirection
Notes: Adding Web cache redirection to a transparent proxy cache solution eliminates the drawbacks of transparent proxy without redirection. Much of this is due to the fact that the cache is moved out of the data path and network functions such as examining each packet to determine which are for HTTP and performing network address translation are offloaded from the cache to the redirector.
Web cache redirection is generally run on a networking device such as a LAN switch or router. Because the packet examination is by a device optimized for examining packets and can therefore do it very fast, there is minimal impact on non-Web traffic. The cache redirector can also remove the network address translation function from the cache. Moving these two functions to the web cache redirector frees up CPU cycles on the cache server for serving web pages -- the job the cache is really supposed to do. Also, removing the network address translation function from the cache means that the cache doesn’t have to be configured with network address translation software. Since transparent proxy already eliminated the browser configuration, adding the redirector brings caching as close to zero administration as possible.
Using a cache redirector that is separate from the cache server allows the client load to be spread over multiple caches, while directing requests for content to the cache holding that content. This increases hit rate which, in turn, decreases WAN traffic and user response time. Also, because the cache redirector is aware of the different physical caches, if multiple caches have been deployed, it can perform health checks on the caches and direct requests for web pages only to healthy caches. Further, redundant redirectors can be deployed, eliminating any single point of failure and yielding the ultimate in uptime.
The biggest negative to web cache redirection is that the redirector must be purchased and deployed, increasing modestly the expense of the solution and incurring some additional administration because of the need to configure the redirector.

## Slide 8: Actions on Policy Trigger
  Switch takes one of the following options
    Allow and express forward through switch
    Drop frame upon entry to switch switch
    Redirect frame to a specific (group of) device(s)
      Cache servers, routers, firewalls, any other IP device
    Perform network address translation
      Discussed in Alteon Certified Engineer course
  Logging options
  Statistics

## Slide 9: Configuring: Web Cache Redirection
Directly attach transparent proxy caches to Alteon switch
Set up filters
  E.g., filt 21/sip any/dip any/proto tcp/sport any/dport 80/act redir/rport 80/group 1/ena
Note that client and server processing do not have to be enabled for application redirection
Configure all the caches as real servers and enable them
Place the real servers into real server group
Apply the filter(s) to the port incoming client HTTP request
Enable filtering on the client port
Turn on server load balancing
Apply, save and you’re done!

## Slide 10: Notes on Hash Metric
Hash algorithm uses different parameters based on the type of load balancing or application redirection selected
When used with a VIP for SLB, the algorithm uses only the IPSA
When used with HTTP or FTP redirection filter, only IPDA is used
For any other criteria, both the IPSA and IPDA are used
Notes: When used with a VIP for SLB, the algorithm uses only the IPSA
  All requests from the same client are sent to the same real server
  Used to maintain client session persistency
When used with HTTP or FTP redirection filter, only IPDA is used
  Improves hit rate by sending all requests for same site to same cache
For any other criteria, both the IPSA and IPDA are used
  Maintains session persistence and symmetry for firewall load balancing

## Slide 11: Configuring: Filters with the CLI

## Slide 12: Configuring: Filters with the CLI (cont.)

## Slide 13: Application Redirection Example: Differentiated Services
Reduce costs and increase trans-Pacific access performance:
  Redirect non-time sensitive traffic to high-latency satellite links
Multiple tiers of service
  Redirect premium users to high-end servers
  Pass through premium site traffic to internet, otherwise redirect to local caches
Internet
Dialup
xDSL, Cable
Premium
Service
Standard service
HTTP
FTP, Email

## Slide 14: Application Redirection Summary
Alteon WebOS provides Application Redirection/Web Cache Redirection support for better application performance
Reviewed caching operations
Reviewed filtering capabilities
Reviewed configuration of application redirection
  Define filters
  Apply filters to client ports
  Turn on SLB (without client/server processing)
  Enable filters, apply, save