## Slide 1
FWLB with Static and Dynamic NAT on Firewalls
Method 1

## Slide 2
Complex!
Works with TCP sessions initiated from the internal network AND external network.
Tested successful with leastconn load-balancing metric.
Works with small modifications on the firewall. All that is needed to be changed on the firewalls are the IP interfaces (multinetting).
Only works with TCP packets, excluding FTP.
… about this FWLB configuration (Method 1)

## Slide 3
FW 1
CheckPoint FW-1 4.0
NT4.0 SP4
FW2
CheckPoint FW-1 4.0
NT4.0 SP4
FWLB with Static/Dynamic NAT on Firewalls - Method 1
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.2.1.1 / 16
202.140.11.206 / 27
Default gw: 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
10.4.1.1 / 16
10.5.1.2 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180 SW Rel/5.2.21
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
Port 1: PIP: 10.5.2.1
Port 2 PIP: 10.5.2.2
AD2 SW Rel/5.2.21
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1: PIP: 202.140.11.211
Port 2 PIP: 202.140.11.213
FW1 performs dynamic source IP NAT for internal clients accessing the Internet using 202.140.11.205 (one-to-many NAT)
FW2 performs dynamic source IP NAT for internal clients accessing the Internet using 202.140.11.206 (one-to-many NAT)
Both firewalls will IP NAT 202.140.11.210 to 10.5.1.10 (one-to-one NAT)
Public IP address
Private IP address
Port 1
Port 2
Port 1
Port 2
Port 8
Port 8

## Slide 4
FW 1
Packet flow - Internal clients accessing the Internet
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
① Packet arrives from the Internal client. IPSA: 10.5.1.11 IPDA: Public IP address X
② SW2 load-balances to FW1 using rule # 200. IPSA: 10.5.1.11 IPDA: Public IP address X
③ IP source NAT by FW1. IPSA:202.140.11.205 IPDA: Public IP address x
④ SW1 performs IP source NAT using rule # 120. IPSA: 202.140.11.211 IPDA: Public IP address x. The switch replaces the source IP address of the packet to the PIP address of the switch port receiving the frame from the firewall. This ensures that the packet returns to the correct firewall even though the firewall has performed a NAT function on the packet.
①
②
③
④
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1: PIP: 202.140.11.211
Port 1
Port 1

## Slide 5
FW 1
Packet flow - Internal clients accessing the Internet (continued)
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1: PIP: 202.140.11.211
① Reply packet arrives from the Internet. IPSA: Public IP address X IPDA: 202.140.11.211
② SW1 filters the packet as ‘allow’ using rule # 91, and performs a NAT on the IPDA back to the original address, and forwards to FW1. IPSA: Public IP address X IPDA: 202.140.11.205
③ IP destination NAT by FW1. IPSA: Public IP address X IPDA:10.5.1.11
④ SW2 filters the packet as ‘allow’ with ack-bit match, using filter rule # 110. Forwards back to Client.
①
②
③
④
Port 1
Port 1

## Slide 6
FW 1
Packet flow - External Clients accessing the Internal Server
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
Port 1: PIP: 10.5.2.1
① TCP request arrives from the external client. IPSA: Public IP address Y IPDA: 202.140.11.210
② SW1 load-balances the packet to FW1 using rule # 200. IPSA: Public IP address Y IPDA: 202.140.11.210
③ IP source NAT by FW1. IPSA: Public IP address Y IPDA: 10.5.1.10
④ SW2 performs IP source NAT using rule # 120. IPSA: 10.5.2.1 IPDA: 10.5.1.10. The switch replaces the source IP address of the packet to the PIP address of the switch port receiving the frame from the firewall. This ensures that the packet returns to the correct firewall even though the firewall has performed a NAT function on the packet.
①
②
③
④
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1
Port 1

## Slide 7
FW 1
Packet flow - External Clients accessing the Internal Server (continued)
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
Port 1: PIP: 10.5.2.1
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
① Server replies to client request. IPSA: 10.5.1.10 IPDA: 10.5.2.1
② SW2 filters the packet as ‘allow’ using rule # 100, and performs a NAT on the IPDA back to the original address, and forwards to FW1. IPSA: 10.5.1.10 IPDA: Public IP address Y
③ IP source NAT by FW1. IPSA: 202.140.11.210 IPDA: Public IP address Y
④ SW1 filters the packet as ‘allow’ with ack-bit match using rule # 110. Forwards back to the router.
①
②
③
④
Port 1
Port 1

## Slide 8
The purpose of the filters
Switch 1:
Rule 90: Allows management access to the switch.
Rule 91: Allows the response packet to travel back to the port where the request packet was received via the firewall.
Rule 92: Same as rule 91.
Rule 109: Allows ICMP packets to pass (ie: HealthCheck packets).
Rule 110: Allows Response Packets to pass the switch without being source NAT to the PIP address.
Rule 120: Performs the source NAT to the PIP address of the port receiving the packet.
Rule 200: Redirects the packet to the firewalls using the selected load-balancing method.
Switch 2:
Rule 80: Allows ICMP packets to pass (ie: HealthCheck packets).
Rule 100: Allows the response packet to travel back to the port where the request packet was received via the firewall. Also allows management access to the switch.
Rule 110: Allows Response Packets to pass the switch without being source NAT to the PIP address.
Rule 120: Performs the source NAT to the PIP address of the port receiving the packet.
Rule 200: Redirects the packet to the firewalls using the selected load-balancing method.

## Slide 9
FWLB with Static and Dynamic NAT on Firewalls
Method 2

## Slide 10
Much simpler method of operation.
Does everything the ‘method 1’ setup does, and also supports UDP and FTP.
Need to change the security policies - Requires the firewall to perform NAT on IPDA and IPSA.
Application tested - http, FTP, telnet, SNMP, RealVideo, DNS.
Use Hash as metric if using FTP.
… about this FWLB configuration (Method 2)

## Slide 11
FW 1
CheckPoint FW-1 4.0
NT4.0 SP4
FW2
CheckPoint FW-1 4.0
NT4.0 SP4
FWLB with Static/Dynamic NAT on Firewalls - Method 2
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.2.1.1 / 16
202.140.11.206 / 27
Default gw: 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
10.4.1.1 / 16
10.5.1.2 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180 SW Rel/5.2.21
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
AD2 SW Rel/5.2.21
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
FW1 performs dynamic source IP NAT for internal clients accessing the Internet using 202.140.11.205 (one-to-many NAT)
FW2 performs dynamic source IP NAT for internal clients accessing the Internet using 202.140.11.206 (one-to-many NAT)
Both firewalls will IP NAT 202.140.11.210 to 10.5.1.10 (one-to-one NAT)
Public IP address
Private IP address
Port 1
Port 2
Port 1
Port 2
Port 8
Port 8

## Slide 12
FW 1
Packet flow - Internal clients accessing the Internet
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
① Packet arrives from the Internal client. IPSA: 10.5.1.11 IPDA: Public IP address X
② SW2 load-balances to FW1 using rule # 200. IPSA: 10.5.1.11 IPDA: Public IP address X
③ IP source NAT by FW1. IPSA:202.140.11.205 IPDA: Public IP address x
④ SW1 forwards the packet to the router.
①
②
③
④
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1
Port 1

## Slide 13
FW 1
Packet flow - Internal clients accessing the Internet (continued)
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1: PIP: 202.140.11.211
① Reply packet arrives from the Internet. IPSA: Public IP address X IPDA: 202.140.11.205
② SW1 filters the packet as ‘allow’ using rule # 91, and forwards to FW1. IPSA: Public IP address X IPDA: 202.140.11.205
③ IP destination NAT by FW1. IPSA: Public IP address X IPDA:10.5.1.11
④ SW2 forwards the packet to the Client.
①
②
③
④
Port 1
Port 1

## Slide 14
FW 1
Packet flow - External Clients accessing the Internal Server
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
① TCP/UDP request arrives from the external client. IPSA: Public IP address Y IPDA: 202.140.11.210
② SW1 load-balances the packet to FW1 using rule # 200. IPSA: Public IP address Y IPDA: 202.140.11.210
③ FW1 performs the following:
Destination NAT: IPDA changed from 202.140.11.210 to 10.5.1.10 (static NAT)
Source NAT: IPSA changed from public IP address Y to 10.3.1.1 (dynamic NAT)
④ SW2 forwards the packet to the server.
①
②
③
④
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
Port 1
Port 1

## Slide 15
FW 1
Packet flow - External Clients accessing the Internal Server (continued)
SW 1
SW 2
10.1.1.1 / 16
202.140.11.205 / 27
Default gw : 202.140.11.193
10.3.1.1 / 16
10.5.1.1 / 16
Server: 10.5.1.10/ 16
Default gw: 10.5.1.3
Router
202.140.11.193 / 27
Client: 10.5.1.11/ 16
Default gw: 10.5.1.3
Alteon180: Single VLAN
If1: 10.5.1.3/16
If2: 10.3.1.2/16
If3: 10.4.1.2/16
AD2: Single VLAN
If1: 202.140.11.207/27
If2: 10.1.1.2/16
If3: 10.2.1.2/16
① Server replies to client request. IPSA: 10.5.1.10 IPDA: 10.3.1.1
② SW2 filters the packet as ‘allow’ using rule # 100, and forwards to FW1.
③ FW1 performs the following:
Destination NAT: Changed from 10.3.1.1 to original public IP address
IP source NAT: Changed from 10.5.1.10 to 202.140.11.210
④ SW1 forwards the packet to the router.
①
②
③
④
Port 1
Port 1

## Slide 16
The purpose of the filters
Switch 1:
Rule 90: Allows management access to the switch.
Rule 91: Allows the response packet to travel back to the corresponding firewall.
Rule 92: Same as rule 91.
Rule 200: Redirects the packet to the firewalls using the selected load-balancing method.
Switch 2:
Rule 100: Allows the response packet to travel back to the port where the request packet was received via the firewall. Also allows management access to the switch.
Rule 200: Redirects the packet to the firewalls using the selected load-balancing method.

## Slide 17
FWLB with NAT (Method 2) - Firewall NAT policies
FW1
Private_10.5_net - Network object defined as 10.5.0.0 / 255.255.0.0
Private_10.5_net (Hiding Address) - NAT from 10.5.x.x to the FW1 public address (202.140.11.205)
Public_net - Network object defined as 0.0.0.0 / 0.0.0.0
Support1 - This Firewall (FW1) 10.3.1.1 / 255.255.0.0

## Slide 18
FW2
Private_10.5_net - Network object defined as 10.5.0.0 / 255.255.0.0
Private_10.5_net (Hiding Address) - NAT from 10.5.x.x to the FW2 public address (202.140.11.206)
Public_net - Network object defined as 0.0.0.0 / 0.0.0.0
Support2 - This Firewall (FW2) 10.4.1.1 / 255.255.0.0
FWLB with NAT (Method 2) - Firewall NAT policies