## Slide 1: ENNI Protection
M Vinod Kumar
Tejas Networks Ltd

## Slide 2: Agenda
Example
Requirements
Possible solutions

## Slide 3: MEF Definition
A Network-to-Network Interface (NNI) defines how two networks handshake and communicate.
An E-NNI is a layered interface built on a point-to-point physical link or multiple point-to-point physical links connecting two MENs where the two MENs belong to different administrative domains.
  MEF Specification: E-NNI Interface Phase 1
An E-NNI (External NNI) join one network with another, typically two networks operated by different Service Providers, but it might also consist of two internal networks in separate maintenance regions of the same Service Provider.
Source: MEF
Notes: Source: MEF

## Slide 4: Topology
MTNL
L2 Network
BSNL
L2 Leased Line
C1
C2
Carrier
Ethernet/
EoSDH
Carrier
Ethernet/
EoSDH
MTNL’s
L2 Service
Customer
MTNL’s
L2 Service
Customer
MTNL wants p2p L2VPN from C1 to C2
MTNL leases L2 service from BSNL
ENNI Protection issue
ENNI
Work
Protect

## Slide 5: Three Deployment Types
Same operator technology
Different operator technology
Different operator technology and ENNI is a third network between the operators
  Is the third network an ENNI anymore or an operator?

## Slide 6: Requirement 1
MTNL
L2 Network
BSNL
L2 Leased Line
C1
C2
Carrier
Ethernet/
EoSDH
Carrier
Ethernet/
EoSDH
MTNL’s
L2 Service
Customer
MTNL’s
L2 Service
Customer
Working-ENNI fails  traffic switches to protection-ENNI
  Protection-ENNI could be defined over the 4 topologies mentioned
ENNI
Work
Protect
Fault
Notification

## Slide 7: Requirement 2
MTNL
L2 Network
BSNL
L2 Leased Line
C1
C2
Carrier
Ethernet/
EoSDH
Carrier
Ethernet/
EoSDH
MTNL’s
L2 Service
Customer
MTNL’s
L2 Service
Customer
Fault within the operator may lead to ENNI protection
ENNI
Work
Protect
Fault
Notification

## Slide 8: Requirement 3
MTNL
L2 Network
BSNL
L2 Leased Line
C1
C2
Carrier
Ethernet/
EoSDH
Carrier
Ethernet/
EoSDH
MTNL’s
L2 Service
Customer
MTNL’s
L2 Service
Customer
No change to the customer frames
ENNI
Work
Protect
Tunnelled
Carrier
Frames
Customer
Frames
Translation
of Frames

## Slide 9: Some ENNI Topologies
=
O
|8|
8
|M:N|
M:N

## Slide 10: Requirements
MEF Requirements: E-NNI Technical Specification Phase 1
Work for all the topologies shown: =, 0, 8, |8|, M:N, |M:N|, etc.
If working-ENNI fails then traffic be switched to the protection-ENNI
  Protection from failure of ENNI link or ENNI bridge
  Sub-50 msec protection switching
  Protection-ENNI may share zero, one, or two terminal bridges with working-ENNI
  Fault notification may be sent to one or both operators
Fault within the operator cloud may lead to traffic movement from working-ENNI to protection-ENNI
  Example: when the node bridging MTNL and working-ENNI fails
  Fault notification be sent towards ENNI or the peering operator
  M:1 protections
No change to the customer frames and end-to-end SLA
  Provider identifiers like S-VLAN, B-VLAN, TESI-ID, etc. may change at the ENNI from provider to provider
  Bi-directionally congruent service path
Work for PBB-TE based operator network (and possibly based on PB and PBB using SPB)
Allow maintenance of each ENNI entity
  The entity is owned by only one operator, and not both
  The fiber is owned by one, and the bridges on either side of fiber is owned by each operator
Scalable: Service and MAC
  B-SA translation at ENNI will avoid learning of B-MAC of one operator in another operator

## Slide 11: Possible solutions
Enhancing PBB-TE with
  Multi-domain PBB-TE and ISP
  Advantages: Leverages existing standards and provides a more general solution
SPB
  For PB and PBB based operator network interconnection
Inviting contributions/collaboration on these ideas

## Slide 12: Solution Example 1
MTNL
L2 Network
BSNL
L2 Leased Line
C1
C2
Carrier
Ethernet/
EoSDH
Carrier
Ethernet/
EoSDH
MTNL’s
L2 Service
Customer
MTNL’s
L2 Service
Customer
A multi-domain TESI is protected using multi-domain IPG
ENNI
Work-IS
Protect-IS

## Slide 13: Closing
Requesting permission for bringing a new PAR

## Slide 14: Thank You