## Slide 1: Transport Services Layer Protection Switching Types Interacting with DRNI
Maarten Vissers
2011-07-20
v01

## Slide 2: Introduction
http://www.ieee802.org/1/files/public/docs2011/axbq-vissers-drni-and-sncp-interworking-0511-v00.pptx presented “DRNI and G.8031 ETH SNCP interworking” aspects
G.8031 ETH SNCP operates in the MEF “Ethernet Services Layer”
Interworking aspects of DRNI with protection switching inside the MEF “Transport Services Layer” were not included in the above presentation
This presentation introduces some of the Transport Services Layer protection switching methods that may interact with DRNI

## Slide 3: DRNI within the MEF Ethernet Services Architecture
Data Plane
Control Plane
Management Plane
Transport Services Layer
Ethernet Services Layer
Application Services Layer
Ordering , Provisioning, Billing,
Management and Support
DRNI is performed in this layer, which is an ETH(S-VLAN) or ETH(BSI) layer
EC signals are transported over p2p VLAN, ESP, PW, transport-LSP, VC-n, ODUk, mp2mp B-VLAN, mp2p LSP+p2p PW connections and 802.3 links
This layer supports Ethernet Connections (EC)
EC protection switching G.8031 ETH SNCP p802.1AXbq DRNI
Transport Service Layer protection alternatives: ESP protection, VC-n protection, ODUk protection, transport-LSP protection, G.8032 ERP

## Slide 4: Multi-Domain Carrier Network Architecture
Access
Access
PBB-TE
Metro
EOTN
Core
Ethernet
Metro
3
4
6
5
B
7
8
10
9
A
2
1
Carrier X Network
UNI
UNI
i
EC Terminating or Bridging Node
Physical link
Ethernet virtual link supported by Transport Services layer connection
Aggregation & Encapsulation
Aggregation
Aggregation
EVC
EC
Protected ESP connections
A
2
4
6
8
10
B
Protected ODUk connections
Ethernet Ring Protected Links
G.8032 ring protection
ODUk protection (ODUk SNCP or ETH CL-SNCG/I)
PBB-TEprotection
(ESP protection)

## Slide 5: Transport Services Layer protection example in Multi-Carrier Network Architecture
MPLS-TP
Core
Access
EOTN
Core
Ethernet
Metro
3
4
6
5
A
2
1
Access
PBB-TE
Metro
B
10
9
13
14
11
12
7
8
Carrier X Network
Carrier Y Network
E-NNI
UNI
UNI
DRNI
i
EC Terminating or Bridging Node
Physical link
Ethernet virtual link supported by Transport Services layer connection
G.8032 Ring Protection
ODUk Protection
ESP Protection
Transport-LSP Protection

## Slide 6: Transport Services Layer Protection Characteristics
Protects a segment of an EC within a carrier network
  metro network segment
  core network segment
  G.8032 ERP protects against Ethernet link and node failures
  ESP protection protects against ESP trail failures
  ODUk, VC-n, transport-LSP SNCP protects against ODUk, VC-n, transport-LSP sub-network connection failures
  ETH CL-SNCG/I protection protects against ODUk, VC-n, transport-LSP trail failures
Does not protect against EC switch fabric/configuration failures
CL-SNCG/I: Compound Link Sub-Network Connection Group protection with Inherent monitoring (see c11.3.5/G.808.1)

## Slide 7: Transport Services Layer Protection Characteristics
ESP Protection:
Clause 6.10 in I-Component
ESP Protection:
Clause 6.11 in B-Component
VC-n, ODUk, tLSP MEP
EC aggregation
& encapsulation
Protected EC signals
VC-n, ODUk, tLSP switch fabric
W
P
MEP
VC-n, ODUk, tLSP SNC Protection
trail
Sub-network connection
ESP, VC-n MEP
EC aggregation
& encapsulation
Protected EC signals
ESP, VC-n switch fabric
MEP
ESP, VC-n Trail Protection
trail
aggregation
& encapsulation
aggregation
& encapsulation
W
P
ESP, VC-n protection switch
SNCP MEP
Single aggregation & encapsulation process, working and protection trails
    Single aggregation & encapsulation process, single trail, working and protection sub-network connections
Protection Control
Protection Control
EC switch fabric
EC switch fabric
ESP Protection:
S-VLAN Relay in I-Component
ESP Protection:
B-VLAN Relay in B-Component

## Slide 8: Transport Services Layer Protection Characteristics
ETH CL-SNCG/I Protection
VC-n, ODUk, tLSP MEP
EC aggregation
& encapsulation
Protected EC signals
VC-n, ODUk, tLSP switch fabric
MEP
trail
aggregation
& encapsulation
W
P
EC switch fabric with Group prot.
    Working and protection aggregation & encapsulation processes, working and protection trails
Protection Control
ETH Ring Protection
Ethernet Link MEP
EC aggregation
& encapsulation
Protected EC signals
Ring Protection Control
Ring-APS Half MIP
ERP
Control
Ring Protection Control
trail
    Working and protection aggregation & encapsulation processes, working and protection trails
east
west
EC switch fabric with Ring prot.

## Slide 9: Interacting with DRNI
DRNI requires that the VC-n, ODUk, transport-LSP and ESP protection architectures be complemented with a distributed version
Ethernet Ring Protection supports sub-rings, which provides a dual node interconnection; DRNI would replace “Sub-Ring 3” in Figure 9-12/G.8032:

## Slide 10: Carrier domain protection interacting with DRNI
DRNI should be able to interact with the following protection switching methods deployed inside the carrier domains:
  G.8031 ETH SNC protection
  G.8032 Ethernet Ring Protection
  G.841 VC-n protection
  G.873.1 ODUk SNC protection
  transport-LSP protection (under development)
  802.1Qay ESP protection
  G.873.2 ODUk ring protection (under development)
  ETH CL-SNCG/I protection (based on G.808.1)
Should DRNI operation be
  interacting with the set of control protocols of the above protection methods?
  independent of the above protection methods/protocols and be interconnected via S-VLAN/BSI reference points, possibly located inside EC switch fabric (MAC Relay, ETH_C)?
11
12
13
14
Carrier X
Eth Serv Layer Prot:
- ETH SNCP
Tran Serv Layer Prot:
- Eth Ring Protection
- VC-n, ODUk, tLSP SNCP
- ESP, VC-n trail protection
- ETH CL-SNCG/I protection
DRNI
DRNI
DRNI
DRNI
EC Type 1
or Type 2
(virtual)
ref. points
E-NNI
Carrier Y
Eth Serv Layer Prot:
- ETH SNCP
Tran Serv Layer Prot:
- Eth Ring Protection
- VC-n, ODUk, tLSP SNCP
- ESP, VC-n trail protection
- ETH CL-SNCG/I protection
EC Type 1
or Type 2
(virtual)
ref. points

## Slide 11: Illustrating the two options
11
12
13
14
DxxxP
DxxxP
DxxxP
DxxxP
Carrier X
Carrier Y
DRNI
DRNI
DRNI
DRNI
E-NNI
Prot
Ctrl
Prot
Ctrl
11
12
13
14
DxxxP
DxxxP
DxxxP
DxxxP
Carrier X
Carrier Y
DRNI
DRNI
DRNI
DRNI
E-NNI
Prot
Ctrl
Prot
Ctrl
EC Type 1
or Type 2
(virtual)
ref. points
EC Type 1
or Type 2
(virtual)
ref. points
INDEPENDENT
INTERACTING
Distributed XXX Protection process

## Slide 12: DRNI independent of protection type in carrier networks and interconnected via set of S-VLAN/BSI reference points, possibly located inside EC switch fabric
Seems to be the best approach
Faults/degradation in carrier network does not impact DRNI status and fault/degradation in DRNI “network” does not impact protection status in carrier network
  Need to verify that there is no interaction/information exchange necessary between DRNI and protection used in carrier network
Allows to develop DRNI independent of the set of protection types used in carrier networks
Allows to develop distributed versions of the set of protection types used in carrier networks independent of DRNI