## Slide 1: Quality of Service: AVB “support” for PRI QoS IEEE 802.1 AVB WG Jul 2011
Presented by: Philippe Klein, Broadcom
phkl-srp-qos-0711-v01

## Slide 2: Priority QoS vs. Parametrized QoS (1)
The issues:
  Not every network physical medium is really Paramterized QoS (PQoS) able.
  Prioritized QoS is the most common QoS today. PQoS is gaining acceptance on PQoS-able medium but the acceptance will be very gradual over Priority QoS.
  Using different Stream management Protocol for QoS and PQoS will affect the acceptance and deployment of AVB…

## Slide 3: Priority QoS vs. Parametrized QoS (2)
The proposal:
  Same SRP protocol for both Prioritized and Parameterized QoS
  Add a new Prioritized/ Parameterized QoS attribute of toTalker Advertise to characterize the stream
  The same LR MAD_Join.request primitive is handled differently in fct of the Stream’s Prioritized/ Parameterized QoS attribute:
    For Pri QoS: LR MAD_Join.request is translated to a network specific BW ADMISSION (based on PRI stream traffic statistics)
    For Param QoS LR MAD_Join.request is translated to a network specific BW RESERVATION
  Both PRI and Param QOS Streams could be managed on the same path relative to the configured BW ratio between PRI and Parametrized QoS

## Slide 4: “AVB Ready” Bridges
“AVB Ready” bridges could be bridges supporting SRP for Prioritized QoS in the first stage until PQoS Stream management is added at a later stage
Question: What is the best way to promote “AVB Ready” ?
    An informative new profile in BA ?
    Or…

## Slide 5
Thank you