## Slide 1: Loopback & Linktrace with ECMP
Xiao Min, ZTE
Huang Lu, China Mobile

## Slide 2: Loopback without Reverse Flow Hash
Cited from bp-mackcrane-ECMP-CFM-0412.ppt:
LBMs sent to individual DA with Flow Hash to select path
LBM MIP TLV contains MIP address
MIP responds with LBR
LBR may take different path from LBM
  Could add Flow Hash TLV to LBM to attempt to make LBR symmetric…
  But there is no guarantee that LBR is symmetric if network is misbehaving!
LBM to Individual DA, MIP address in TLV
LBR to LBM SA

## Slide 3: Loopback with Reverse Flow Hash
LBM sent to individual DA with both Flow Hash and Reverse Flow Hash to select both forward path and reverse path
LBM MIP TLV contains MIP address
MIP responds with LBR
LBR sent to individual DA with Flow Hash which equals to Reverse Flow Hash taken from LBM
LBR may take symmetric path or unsymmetric path with LBM, and it’s predicted and controlled by the operator
LBM to Individual DA, Reverse Flow Hash in TLV
LBR to LBM SA, Flow Hash equals to Reverse Flow Hash in LBM

## Slide 4: Application Example 1 of Loopback with Reverse Flow Hash
Request symmetric reverse path:
LBM sent to individual DA with both Flow Hash and Reverse Flow Hash to request symmetric reverse path
LBR sent to individual DA with requested Flow Hash
Benefits
  It’s unnecessary to execute loopback from Node B to Node A again
  If one reverse path is in failure, other two loopbacks won’t be affected
LBM to Individual DA, Reverse Flow Hash in TLV
Symmetric LBR to LBM SA
A
B

## Slide 5: Application Example 2 of Loopback with Reverse Flow Hash
Request non-fail reverse path:
Unicast CCM makes it known that one reverse path is available
LBM sent to individual DA with both Flow Hash and Reverse Flow Hash to request non-fail reverse path
LBR sent to individual DA with requested Flow Hash
Benefits
  If it’s known that one reverse path is non-fail, the operator can request LBR to take the non-fail reverse path, to avoid possible loopback fail due to failed return path
CCM to Individual Address
Flow Hash C
B
LBM to Individual DA, Reverse Flow Hash in TLV
LBR with Flow Hash C to LBM SA
A

## Slide 6: Linktrace with only one LTR
Cited from bp-mackcrane-ECMP-CFM-0412.ppt:
LTM sent to individual DA with specific Flow Hash
Each hop sends back LTR (if LTM TTL is not 0)
Forwards LTM to ECMP selected hop (if LTM TTL is >1)
LTR frames identify path for DA+Flow Hash
LTM to individual address w/ flow hash
LTR may take any path

## Slide 7: Linktrace with one or more LTRs
LTM sent to individual DA with specific Flow Hash
Each MIP/MEP sends back one or more LTRs (if LTM TTL is not 0), the number of LTRs equals to the number of reverse paths
Forwards LTM to ECMP selected hop (if LTM TTL is >1)
LTR frames identify path for DA+Flow Hash (use different Flow Hash to cover all reverse paths)
Benefit
  To avoid possible path failure of one specific reverse path
LTM to individual address w/ flow hash
Multiple LTRs with different Flow Hash to cover all possible reverse paths
B
A
Flow Hash A
Flow Hash B
Flow Hash C

## Slide 8: Proposals
Add Reverse Flow Hash to LBM
Require MIP/MEP to reply one or more LTRs to cover all reverse paths

## Slide 9: Thank you!