## Slide 1: Common OAM between IEEE 802.1 and IETF/TRILL
Tissa Senevirathne
Donald Eastlake
September, 2012

## Slide 2: Re-cap from San Diego to Santa Cruz
We presented high-level goal of the effort
  i.e. to create a common OAM framework between IETF/TRILL and IEEE 802.1
Following IEEE participants volunteered to work with TRILL WG team
  Norm Finn, Stephen Haddock, Ben Mack-Crane, Ali Sajassi, Sue Hares.
  Reviewed Frame Format and MP Addressing model.
Rest of this presentation captures the discussions that occurred between the team from San Diego to Santa Cruz
Your Comments and Feedback are welcome

## Slide 3: TRILL OAM Frame Structure
OAM Ether Type.
- Clearly Identify the OAM channel
- Allows different technologies to easily integrate OAM channel
Encapsulation Header
Client PDU fragment
OAM PDU
Addresses MEP (end Points)
Drives Forwarding decisions
Influence Forwarding decisions
Fixed size (128 bytes for TRILL)
May not be present in IEEE 802.1 technologies such as Qbp
Drives OAM Functions
ET-OAM
Forwarding Header
Below is the proposed TRILL OAM frame structure
Client PDU fragment, may or may not be present based on the technology

## Slide 4: TRILL MP addressing
802.1ag MP address can interface basis (Individual address model) or Bridge (Shared address model).
TRILL MP addressing is per RBridge basis
  Use shared addressing model of 802.1ag
TRILL MP addressing summary
  TRILL MP addressed by egress nickname
    OAM frames are filtered/ separated from data frames with TRILL OAM Flag and EtherType.
  Please see slide 7 for details
  NOTE: TRILL OAM flag is one of the reserved bits in the TRILL header

## Slide 5: TRILL MP Model with Combined Shared and Trunk Ports
TRILL OAM
Processing
MEP
802.1Q VLAN Processing
Logical 802.1/802.3 Processing
802.3 PHY
802.1Q VLAN Processing
Logical 802.1/802.3 Processing
802.3 PHY
RBridge
TRILL Trunk Ports
(TRILL Frames)
Shared Ports
(TRILL and Native Frames)
MUX/DEMUX
TRILL Encap/Decap
Access Ports
(Native Frames)
C-Component
TRILL Encapsulated
MEP
802.1Q VLAN Processing
Logical 802.1/802.3 Processing

## Slide 6
TRILL Rbridge Components
802.1Q
C-Component
TRILL
“R-Component”
OAM Port
Interconnect Port
MUX/DEMUX
TRILL Trunk Port
TRILL Encap/Decap
native
TRILL Encap

## Slide 7: TRILL OAM Frame identification
If M==1 and R(OAM) ==1 then
Copy to CPU AND Forward normally
Else if R(OAM) ==1 and (egree nickname is local) then
It is an OAM frame; AND redirect to CPU, DO NOT FORWARD
If R(OAM) ==1 then
Do NOT de-capsulate and forward as a native frame
Receive Processing
Transmit Processing

## Slide 8: Use of 802.1ag Messages for TRILL
Use 802.1ag header as defined in 802.1Q Rev5 2011.
MD-Level semantics are the same as in 802.1ag
Separate Op-code space for TRILL specific OAM functions
Re-use existing TLV where applicable
Separate TLV space for TRILL specific TLV
Details in draft-tissa-trill-oam-fm-00

## Slide 9: Next Steps
What should be the next steps ?
  Conclude on addressing and frame format
  Detail discussion on use of 802.1ag messaging
  Formal request from IETF/IEEE ?

## Slide 10: Reference
Requirement document
  https://datatracker.ietf.org/doc/draft-ietf-trill-oam-req/
Framework document
  https://datatracker.ietf.org/doc/draft-salam-trill-oam-framework/
Fault Management
  https://datatracker.ietf.org/doc/draft-tissa-trill-oam-fm/