## Slide 1: 802.1Qbg Maintenance Items
Paul Bottorff
Paul.Bottorff@hp.com

## Slide 2: MIB Problem: VSIMgrID size
Problem: ieee8021BridgeEvbVSIMgrID object defines an octet string object with size 1, with a reference to subclause 41.1.3 'VSI Manager ID'. However this subclause states that 'The value 0 means ... indicating that the Bridge should select a default value. Any other value is interpreted as an IPv6 address, as defined in IETF RFC 4291.' In addition the 'VSI Mgr ID' field in the VSI manager ID TLV is defined as 16 octets. This seems to imply the object size should be 16 bytes.
Recommendation: Ieee8021BridgeEvbVSIMgrID size should be 16 octets not 1 octet.

## Slide 3: MIB Problem: VSIMvFormat Size
Problem: The values for ieee8021BridgeEvbVSIMvFormat object are 'basic (1)', 'partial (2)', and 'vlanOnly (3)‘, however the reference for this object is subclause 41.2.8 'Filter Info format' which states 'The Filter Info formats defined by this standard are shown in Table 41-6.'. Table 41-6 however defines values of 'VID (41.2.9.1) 0x01', 'MAC/VID (41.2.9.2) 0x02', 'GroupID/VID (41.2.9.3) 0x03' and 'GroupID/MAC/VID (41.2.9.4) 0x04' which don't match the object vales.
Recommendation: The value list should match Table 41-6.

## Slide 4: ieee8021BridgeEvbVDPCounterDiscontinuity
Problem: The description for the ieee8021BridgeEvbVDPCounterDiscontinuity object is 'The time (in hundredths of a second) since the last counter discontinuity.' and while I assume it is either associated with, or derived from, ifCounterDiscontinuityTime there appears to be no further definition of this object and there is no reference subclause.
Recommendation: The discontinuity referred to is VSIDBEntry creations which can occur at any time since these entries can be created and destroyed dynamically along with the VDP machine instances. The timer which may have a discontinuity is the ieee8021BridgeEvbVSITimeSinceCreate. Some text should be added to the VDPCounterDiscontinuity indicating that it is set when the VSIDBEntry is created.

## Slide 5: Maintenance Item #91
Table | Clause 12 Object | Type | Clause 17 Object | Type | State Machine
12-18 | evbSysEcpDfltAckTimerInit | Timer Exp | ieee8021BridgeEvbSysEcpAckTimer (?ieee8021BridgeEvbSysEcpDfltAckTimerInit) | U32 usec | 
 | evbSysVdpDfltRsrcWaitDelay | Timer Exp | ieee8021BridgeEvbSysVdpDfltRsrcWaitDelay | U32 usec | 
 | evbSysVdpDfltReinitKeepAlive | Timer Exp | ieee8021BridgeEvbSysVdpDfltReinitKeepAlive | U32 usec | 
12-19 | sbpVdpOperRsrcWaitDelay | Timer Exp | ieee8021BridgeEvbSbpVdpOperRsrcWaitDelay | U32 usec | resourceWaitDelay 41.5.5.7
 | sbpVdpOperReinitKeepAlive | Timer Exp | ieee8021BridgeEvbSbpVdpOperReinitKeepAlive | U32 usec | toutKeepAlive 41.5.5.13
12-26 | urpVdpOperRsrcWaitDelay | Timer Exp | ieee8021BridgeEvbURPVdpOperRsrcWaitDelay | U32 usec | respWaitDelay 41.5.5.9
 | urpVdpOperReinitKeepAlive | Timer Exp | ieee8021BridgeEvbURPVdpOperReinitKeepAlive | U32 usec | reinitKeepAlive 41.5.5.5
12-26 | ecpOperAckTimerInit | Timer Exp | ieee8021BridgeEvbEcpOperAckTimerInit | U32 usec | ackTimer 43.3.6.1
 | ecpOperMaxTries | Int | ieee8021BridgeEvbEcpOperMaxRetries | U32 | maxRetries 43.3.7.3
Need a single unit for all these
  Timer Exp: This is the power of 2 passed in the EVB TLV
  10 usec: This is the timer unit used in the state machines
  Usec: This is the unit currently specified in the SNMP MIB/Annex D
Document uses both Timer Exp and 10 usec

## Slide 6: Notes On #91
Since VDP timers have a resolution of 10 usec (41.5.4) the variables toutKeepAlive (41.5.5.12) and respWaitDelay (41.5.5.9) should be in units of 10 usec (1/100,000 sec), and the equations should not include the 10x multiplier. Need to add units to the two equations.
References to urpVdpResourceWaitDelay are incorrect, they should be urpVdpOperRsrcWaitDelay.
Default times in 41.5.5.12 and 41.5.5.9 need to be increased by the 1.5 factor.
Annex D.2.13.6, D.2.13.8, D.2.13.9 need to be changed to exclude the 10x factor when setting the ECP and VDP timer initialization values to match the timer resolutions of 10 usec.