## Slide 1: Solutions for P802.1Qbz / P802.11ak: Station subset issue
Norman Finn
January, 2013
Version 2

## Slide 2: Introduction
This presentation is available at: http://www.ieee802.org/1/files/public/docs2012/bz-nfinn-soln-station-subset-0113-v01.pdf
It attempts to answer one of the questions raised by: http://www.ieee802.org/1/files/public/docs2012/bz-nfinn-pt-to-pt-problem-list-1112-v02.pdf

## Slide 3: Station subset problem
AP sends the “same” multicast from X to stations behind station/bridges A through E.
But, tagging differences and VLAN translations result in three different resultant frames, and at least three transmissions: VID 6 (A and B), VID 7 (C), and untagged (D and E).
How do we send each one to the right subset of stations?
AP/B
B
C
D
X
E
tagged
with VID 6 or 7
untagged
A
6
6
7

## Slide 4: Alternative 1: Four address format

## Slide 5: Alternative 1: Four address format
802.11 defines four addresses for every frame:
  Receiver Address: Which station(s) (AP or non-AP) should receive frame.
  Destination Address: Destination address in original MAC service request.
  Source Address: Source address in original MAC service request.
  Transmitter Address: Which station (AP or non-AP) that transmitted frame.
Typically, AP and non-AP stations use only three addresses per frame, by using formats that combine two addresses into a single 6-byte field:
  UP TO AP: Receiver (the AP), Destination, Source = Transmitter (non-AP).
  FROM AP: Receiver = Destination (non-AP), Source, Transmitter (the AP).
  Which, of course, is the root of the “reflection” problem.

## Slide 6: Just use all four addresses!
If you simply use all four addresses for exactly the purpose described in 802.11, this problem can be solved.
The key is the definition of the Receiver address:
  Receiver Address: Which station(s) should receive frame,
And to notice that the Receiver Address can be a multicast address.
Each non-AP (or AP) station attached to the transmitting AP “subscribes to” (accepts frames containing) some multicast Receiver Addresses (the right ones) and discards frames with other multicast Receiver Addresses (the wrong ones).

## Slide 7: Alternative 2: 802.11n-2009 A-MSDU

## Slide 8: IEEE Std 802.11n-2009 A-MSDU
The A-MSDU described in 802.11n is a three-address frame (on the outside) that carries any number of encapsulated frames.
The encapsulated data frames’ Destination and Source addresses are internal to the frame, and not used in the outer three address fields.
The outer Source/Transmitter address can be used by a transmitting non-AP station bridge to discard reflections, using the Source address of the reflected frame, in exactly the same way it discards them, now.
The outer Destination and Receiver addresses are always the AP/Bridge on frames sent towards the AP, and the Destination/Receiver address on frames sent by the AP is a multicast address denoting some subset of the non-AP stations.

## Slide 9: Both alternatives

## Slide 10: For either alternative, 2 issues to settle:
The AP and its attached stations have to agree on what to use for the multicast Receiver (four-address alternative) or Receiver/Destination (A-MSDU alternative) addresses.
We have to make sure that existing non-AP stations will not do the wrong thing when they receive frames containing multicast Receiver addresses that are not the broadcast address.

## Slide 11: Receiver multicast addresses
There is a protocol described in IEEE Std 802.1BR for distributing a mapping between multicast MAC addresses and a list of delivery ports (e.g. for non-AP stations S1, S2, …):
Distributing the vectors has problems with delays that are similar to the delay problems when distributing MAC address mappings in the proposal by Zhuang and Wang (document 12-1449).
These problems can be minimized by suitable rules regarding what kinds of changes can be made to the vector list.
MAC address | S1 | S2 | S3 | S4 | S5 | S6 | S7 | …
01-80-C2-XX-00-01 | Y | Y | N | N | Y | N | Y | …
01-80-C2-XX-00-05 | Y | Y | Y | N | Y | Y | Y | …
01-80-C2-XX-00-12 | N | N | N | Y | Y | N | N | …
… | … | … | … | … | … | … | … | …

## Slide 12: Old non-AP stations
One easy solution, very similar to what is often done, today:
Non-AP stations that expect frames without a VLAN tag, and that do not understand multicast Receiver addresses, use different SSIDs, one per VLAN.
Non-AP stations that understand VLAN tags, but do not understand the new multicast Receiver addresses, can all go on one SSID, different from the above (but could use the above SSIDs.
New non-AP stations that understand multicast Receiver addresses, whether bridges or not, must go on one SSID, different from all of the above.
Some day, when all stations understand multicast Receiver addresses, only the last SSID is needed.

## Slide 13: No Free Lunch
It was mentioned in the architecture solutions deck (see references) that bridging makes no demands on an AP for behaviors not already exhibited by many APs.
The use of multicast Receiver addresses does introduce a new behavior.
Before, the AP used destination MAC address and VLAN ID to select the security association on which to transmit a frame.
Now, the AP must do the above, but must also use that information, plus the ingress port (security association ID), in order to select the Receiver MAC address.

## Slide 14: Details: vector distribution rules

## Slide 15: Multicast vector distribution rules
The AP generates and maintains a list of addresses and distribution vectors as shown in the table, above.
Each non-AP station maintains only a vector with one bit per multicast Receiver address (they are all in a relatively small range), stating whether that station accepts frames with that address, or not. Bits for unknown addresses are 0. It does not bother to remember the vectors.
When a vector is created, changed, or deleted, the AP sends messages to update the stations as necessary, and retransmits as necessary, until all notified stations have acknowledged the update.
A vector can be used by the AP before the acknowledgements are received (or even before the notifications are sent), due to these rules:
  A station can be added, but never removed, from an existing address’s vector.
  A vector can be deleted, and after all ACKs are received, the address can be redefined with any value.
With these rules, when the vectors change, extra frames will likely be discarded, but none will be relayed when they should not be.