## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Why L2R on 802.15
Date Submitted: 2 September, 2013
Source: Clint Powell
Company: Powell Wireless Commsulting, LLC
Address: 1563 W Kaibab Dr, Chandler, AZ 85248
Voice:[], FAX: [],
E-Mail: cpowell@ieee.org
Re: Overview of need for and problem(s) to be solved with Layer 2 Routing.
Abstract: Layer 2 Routing
Purpose: Presentation to IEEE 802.1
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Why Layer 2 Routing in 802.15 (802.15.10) Clint Powell from 15-12-0600-01-0l2r-L2R November 2012 Tutorial

## Slide 3: Motivation for L2R
Growing use of 802.15 in large mesh network applications such as Utility and more generally in Field Area Networks
Need to address general requirements for L2 routing in Field Area Networks utilizing newer 15.4g and 15.4e amendments
Support and use in higher layer protocols – the Internet of Things

## Slide 4: Some Example FANs
Smart Metering (HAN and NAN)
Smart City - Street Lighting/Parking/Meters…
Environmental Monitoring
Smart Home

## Slide 5: Characteristics of These Applications
Data flows
  One-to-many, Many-to-one
  Point-to-point
Topologies
  Collection tree
  Mesh
  Adaptive
Routing strategies
  Proactive
  Reactive
Management
  Planned
  Self Organising
Communications domains
  Internal
  External
    Multiple ingress/egress points
Latency vs. QoS vs. reliability
  Low latency
  Priority of frames
Power saving
  Sleepy end devices
  Sleepy routers

## Slide 6
Concentrator 1
Concentrator 2
Concentrator3
Concentrator1
Concentrator2
Concentrator4
Concentrator2 is deactivated
Concentrator2 is reactivated
PAN1
PAN2
PAN3
PAN1
PAN3
Example Scenario for Managing FAN
Network should be configurable and work automatically.
Less cost repairing process is required when the network has a problem.
After the problem has gone, network should be reformed (maybe to almost the original ) to reduce the load.

## Slide 7
Address allocation mechanism of IEEE 802.15.5
    Step 1 : Create a tree structure by joining from top level to lower
    Step 2 : Report the number of children (including reservation) to parent from lowest level nodes to the highest. After gathering all the number of children, root node assigns address spaces to nodes from top to bottom.
Issue
  Network topology plan needs to be made before network formation.
  Functionality of address space reservation for future use and adjustment of assignments is needed to help in extending network. However, it is difficult in this case, and the network must start over from address assignment to address changes in routing topology.
1
5
1
1
2
8
1
5
1
1
2
8
Inform number of children
Assign address spaces by root
1
5
1
1
2
8
New joiner
Join
No address to allocate!
Assign address spaces by root
×
Scalability Issues in 802.15.5

## Slide 8
Outline of routing algorithm of IEEE 802.15.5
  Exchange the information with neighbors (address spaces, tree level etc.)
  Choose next hop from the information
Issue
  Since routing algorithm is based on address assignment, network must start over from address assignment to address changes in routing topology.
    In public field area networks, changes in routing topology occur often.
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
×
⇒
[1:8]
[2:6]
[3]
[4:5]
[5]
[6]
[9:14]
[10:14]
[7:8]
[8]
[11:13]
[13]
[14]
[12]
[0:14]
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
[1:8]
[2:6]
[3]
[4:5]
[5]
[6]
[9:14]
[10:14]
[7:8],[11:13]
[8]
[11:13]
[13]
[14]
[12]
[0:14]
Can’t merge address spaces!
×
Self Healing Issues in 802.15.5

## Slide 9: Why do L2 Routing?
Robustness & survivability
  Multiple / Alternative paths
    Avoid single point of failure
  Load balancing
    Avoid choke points in a network
Range Extension
  Why not just shout louder?
    Technology / Cost / Regulatory / Power consumption
Data Aggregation
Appropriateness
Notes: Technology – cost of 15.4 vs 802.11 nodes
Regulatory – only allowed 1mW in many countries for 15.4
Tx/Rx is major component of power consumption in low power devices – increase range increases power consumed
Data aggregation – allows distribution of cheaper devices (less storage) at edges of network , reduces number of independent transmissions nearer to collection point – greater efficiency
Robustness – provide several ways to get to destination (may require more hops) to either help in face of failure/interference. Also helps with network installation where an extra routing node can be added to improve reachability of part of network. Avoid single point of failure (requires control of topology) Load balancing between multiple paths between source and destination if one route is becoming congested – switch to an alternative

## Slide 10: Additional Requirements
Reliability
  Reduction of End-to-End retransmissions
  Failure detection
Scalability
  Node density, network size etc.
  Hardware resource requirements
  Behaviour at restarts
Management of flooding, multicasts
  Timing, grouping etc.
Congestion avoidance, flow control, Load balancing
Security
  Provisioning, Joining

## Slide 11: The Internet of Things
Aim to connect many billions of devices to the internet and each other
  Enables finer control of processes
  Enable new synergies between systems
  Enable new applications and improve old ones
  Its really cool to be able to control things from my phone, tablet, laptop…
Enabling communications to devices on this scale must be small fraction of overall cost to be viable
  Wireless device eg 802.15.4, Bluetooth etc
But we still want to use the tried and tested protocols used on the Internet
Specifically, need to use IPv6 to cope with the expected volume of devices

## Slide 12: IP Routing in Multi-hop Networks
Classic IP uses IP addresses to perform the routing between hosts on different subnets
Mechanisms (eg Neighbor Discovery) designed with the assumption that IP multicast will work over link-local scope
But this simple model breaks down if the underlying media doesn’t allow all hosts in a subnet to see each other (eg wireless)
  In this case we need some way to connect the hosts in a subnet together – more routing
Two methods can be used
  Route-Over (L3 or IP routing)
  Mesh-Under (L2 routing)
Each has slightly different characteristics

## Slide 13: Route-over
Treats each host as a router in an independent subnet
  Each hop to the destination is an IP transfer
  Therefore it looks like the message is going from one router between subnet to the next
Problems with Route-over
  Breaks lots of things
    Difficult to define the scope of message
    Link-local is no longer equivalent to “my segment”
  Efficiency issues

## Slide 14: Mesh-under
Use L2 routing to connect devices in the subnet
Multiple L2 hops are transparent to L3
IP packet transfers from (Border) router is one IP hop
  IP hop count controlling a packet’s Time-To-Live is still sensible
  Media boundary (eg Wireless PAN) is link local scope
  Maintains appearance of “ethernet like” network
Things just work
  Multicast can be dealt with at L2

## Slide 15: L2 Routing
Simplifies higher layers – doesn't break IP
Provides for hierarchical architecture
Can better fit to idiosyncrasies of link
Can improve performance
  Remember fragmentation?
  Each IP packet has to be fragmented at source and reassembled at destination
  With Route-over solution this is every hop
  With Mesh-under this only happens at the source and destination nodes – otherwise we just forward and route L2 packets
  But it may not be as big a problem with the introduction of big L2 packets
Can provide more efficient multicast

## Slide 16: Potential Issues to Resolve
Do we really need multicasting?
Really? Battery powered routers? Really!
Rapid connectivity changes
Wireless is not wired
Are all nodes in the mesh in a single IP subnet?
Making use of 6lowpan mesh header?
What functions of the MAC do we require (join)?

## Slide 17: Things to Look At
Efficient multicast at L2
Leveraging recent MAC improvements (4e)
  Information elements to carry routing information
  Synchronisation mechanisms for low duty cycle (sleeping) networks
Security in the mesh
  Securing multicast
  Network security
Bridging
  Cross Media bridging
  Bridging between similar protocols (eg 4g & 4m)