## Slide 1: Layer 3 for TSN
Layer 3 TSN – draft 4
Jouni Korhonen, Philippe Klein
July 2014

## Slide 2: Scoping for the discussion
This presentation looks at the “Layer 3 TSN” from the SoHo or larger networks point of view. However, the solution space is not constrained to those. This is just a start for the discussion and proposing a set of protocols.
There are no considerations for virtualized network infrastructure as of now.
There are no considerations for redundancy as of now..

## Slide 3: Remember the “homenet” architecture ?
L3 routers are connected by multiple L2 segments not managed by L3.
The challenge:
  How to manage path selection & reservation between L3 devices?
  How to manage path selection & reservation across L2/L3 boundaries?
CPE
ISP
DHCPv6-PD ->
TV etc
e.g. TV feed
Home Automation
Remote managed utilities
/64
/64
/64
/64
/64
/64
Public
server
NAS
HNET
RTR
HNET
RTR
HNET
RTR
Visitor nw
3rd party
Managed nw
Home IoT
Media nw
Home nw
Common nw
? (unintentional loop)

## Slide 4: Architecture based on PCE-PE model
Clear separation of “independent” but cooperating layers:
  Layer 3 topology and (non-)adjacent layer 2 topologies are handled separately.
Role separation for layer 3 router:
  “L3 PCE + L2 PCE” or “L3 PCC + L2 PCE”.
  One router is an elected or preconfigured g0d-box.
One L2 PCE per Layer 2 topology.

## Slide 5: Router model with L3 AND l2 PCE capabilities
PCEs for both layer 3 and layer 2 purposes:
  They have different topology view..
  An L3 PCE knows L2 circuits (logical paths) to the next L3 hop(s) and an L2 PCE knows its own network links/hops.
Layer 2 could use any standard link-state protocol (e.g. IS-IS or equivalent) for path management.
Layer 2 circuits computed based on Layer 3 path requests.
PEs are managed by an L2 PCE..
PEs do not have any access to L3 information
PEs do not perform any local path computation.
Assumption: A PE (switch or bridge):
Does not necessarily feature an IP stack.
Allows remote management of FIB.

## Slide 6: L2 PCE (as a part of the router)
It must know the layer 2 topology it manages:
  Either it learns it dynamically or it is pre-configured.
It must manage the switch/bridge (PE) QoS & reservations:
  The PCE must be informed of the any PE locally originated configurations, initial configuration and obviously its own configuration commands.
Service the L3 PCE for a path computation and selection:
  L3 circuit establishment request is serviced by L2 PCE computation and path selection.
  L2 PCE provides an aggregated summary of L2 information.
Layer 2 path management and reservation:
  Independent of the protocol solutions at the L3!
  Could use .1Qca (/w ECTs) or other adequate protocol such as Netconf over SSH, etc.

## Slide 7: L3 PCE / PCC (as a part of the router)
Layer 3 routers have a dual role:
  Either an L3 PCE Client (PCC) or a g0d-box (PCE).
  Based on the IETF PCE architecture and model.
PCE must know the layer 3 topology:
  Either PCE learns it dynamically (e.g., IS-IS, HNCP, OSPF) or it is pre-configured.
  Layer 2 topology knowledge is not relevant beyond “circuits”.
PCE must know both layer 3 and layer 2 QoS & reservations:
  Reporting from other L3 PCCs /w L2 summaries or.. L3 PCE just knows..
Layer 3 “circuit” management and reservation:
  Independent of the protocol solutions at the L2!
  Proposal to use IETF “PCE initiated LSP model” (with modification) to push the layer 3 path to other L3 routers that then take care of the layer 2 path.
No path reservation protocol like RSVP-TE in this proposal..

## Slide 8: PE (switch/bridge)
Simple device.. hopefully..
  Remote management of FIB must be possible.
  PE should accomodate static FIBs.
  Proper security must be in place..
Unaware what happens at layer 3 circuit computation and most likely also on layer 2 path computation:
  However, it may needs to report its own capabilities & status to L2 PCE..

## Slide 9: Protocol considerations
Layer 3 – IETF protocols could & should be reused but unfortunately not possible without being extended:
  PCE architecture – [RFC4655].
  Stateful PCE – [draft-ietf-pce-stateful-pce].
  PCE initiated LSP + delegation – [draft-ietf-pce-pce-initiated]
    Apply to this specific context TBD. (since we have/assume no MPLS here..)
  PCEP – [RFC5440]
    Capability indication TBD.
    Adding the listener/talker models TBD.
    Dynamic reporting TBD.
  PCE discovery – e.g. [RFC5088, 5089] for IS-IS & OSPF.
  Possibly Netconf over HTTP or SSH – e.g. [RFC5539, 6242].
Layer 2:
  Minimal changes.. e.g. 1Qca + ECT sound promising (for .1aq capable PEs).
Data model:
  For exchanging specs and etc..
  Could be YANG.. At the same time transportation over PCEP should also be considered!

## Slide 10: Additional thoughts..
The illustrated solution approach is for layer 3 traffic. Then how to differentiate flows for differentiated treatment?
  A typical layer 3 five-tupple lookup sufficient? DSCP QoS approach?
  Would VLANs or input/ouput ports as a differentiator suffice?
  Other solutions also possible but applicability needs to be evaluated.
When layer 2 (or non-IP) transmission is needed, then layer 2 frames need to be tunneled over layer 3 network:
  PseudoWire could fit in there.. but would require MPLS support.. which is not necessarily a fit for small networks.
  PCE initiated LSP model would allow the use of segment routing -> no LSP setup signaling/reservation.
Listener/talker model in case of PCEP as the control protocol?
  TAs to be notified to L2 PCEs and the L3 PCE.
  LRs to trigger L2 PCEs for part management & reservations and possibly also L3 PCE for ”circuit” management & reservation.

## Slide 11: Summary
A comprehensive L3 and L2 PCE model with a clear layer separation is a must:
  We cannot let homenet and equivalent run ahead without putting enough considerations on L2.
  L2 TSN alone without a comprehensive L3 solution is at risk to achieve limited adoption only.
Allows plumming together, arbitrary layer 3 networks with support for path management & reservation at layer 2 as well.
Aims to maximize protocol & prior work re-use.

## Slide 12: Questions, comments and next steps ?
Pick up a protocol and start executing?
Thank you..