## Slide 1
Future homenet meets IEEE
Draft 6
Jouni Korhonen, Philippe Klein
July 2014

## Slide 2: Future Homenet activities - IETF
IETF Homenet WG works an a set of solutions to enable “next generation” IPv6 home networking environment, where multiple routers and devices can be plugged together in an ad-hoc manner by hopelessly non-technical people.
Entirely a Layer 3 only, IP centric, solution – it is assumed Layer 2 just works.. (*)
Homenet must support:
  Routing, Prefix configuration for routers, Name resolution, Service discovery, and Network security.
Architecture and requirements are documented:
  draft-ietf-homenet-arch-17 (in IESG already..)
(*) not quite right in reality.. This is where TSN & IWK can give a hand and cooperation needed across layers.

## Slide 3: Goals and principles
Solutions MUST work with IPv6, and IPv4 support is a bonus..
Must support multiple routers and arbitrary topologies with any number of subnets/prefixes/links.
Support for multiple ISPs and/or multiple CPEs.
Plug’n’play auto/zeroconf; e.g. loops must not confuse the system.
Adequate default security; from outside the network and within the network.
Possibility to isolate parts of the network e.g. for own, visitor, utility, IoT and 3rd party managed network segments.

## Slide 4: Architecture example..
Network segmented for different uses
  Using L3 addressing
  Each segment _may_ have further switched L2
L3 routing essential to make the homenet topology to work..
CPE
ISP
DHCPv6-PD ->
TV etc
e.g. TV feed
Home Automation
Remote managed utilities
/64
/64
/64
/64
/64
/64
Public
server
NAS
HNET
RTR
HNET
RTR
HNET
RTR
Visitor nw
3rd party
Managed nw
Home IoT
Media nw
Home nw
Common nw
? (unintentinal loop)

## Slide 5: Architecture example – Two ISP
Source address selection becomes essential
  IP packets with ISP#1 configured source address are not routable via ISP#2 CPE (ingress filtering is common).
It is possible that a host configures addresses from both ISPs
  Would be “normal” with IPv6 when SLAAC is used..
ISP#1 CPE
ISP#2 CPE
ISP #1
ISP #2
Internal
network
HNET RTR
Host
Host
Host
Host

## Slide 6: Architecture example – two isp one cpe
CPE
ISP #1
ISP #2
Internal
network
HNET RTR
Host
Host
Host
Host
Source address selection “complexity” in a different form
  IP packets with ISP#1 configured source address are not routable via ISP#2 CPE (ingress filtering is common).
  End hosts see only one CPE and source for addressing.. However.. only certain range of source addresses can be used to reach e.g. ISP#2 services..
“Content” services accessible only via ISP#2.. (TV etc..
CPE provides “aggregate” of configuration information..

## Slide 7: The solution space
No changes to end hosts -> existing host configuration protocols remains unchanged (SLAAC, DHCPv6, DNS(SD), etc).
Minimal changes to existing management/infra protocols:
  New protocols or extensions may be introduced if seen necessary.
  On the table: Source Address Dependent Routing, Prefix Coloring & Assignment and Boundary Detection etc.
No requirement for a “homenet wide” routing protocol:
  Plug-ins for OSPFv3 do exist already to assist zeroconf..
Routers synchronize state across home network using the using the Home networking Control Protocol (HNCP) in order to facilitate automated configuration and use of routing protocols without homenet specific extension:
  Automated configuration requires support for host configuring & serving “daemons” to be HNCP aware.
  Must allow mixing “legacy” CPEs a’la RFC7084.

## Slide 8: The homenetworking control protocol
A Trickle-driven [RFC6206] multicast state flooding + unicast state synchronization protocol on top of UDP.
  Link scope and IPv6 link-local addressing.
  Trickle (per each link) makes sure the flooding is not too babbling and not everybody floods at the same time.. Rapid propagation, low maintenance.
  Protocol documented in [draft-ietf-homenet-hncp-01].
  Download implementation: https://github.com/sbyx/hnetd
Configuration information (e.g. originally received by the CPE facing ISP network via DHCPv6-PD, etc...) distributed to homenet aware routers..
MC=Multicast
UC=Unicast

## Slide 9: HNCP features – more detailed rundown
State (i.e. database) synchronization between routers
  link-local multicast transmission
  unicast fallback for bulk synchronization
  collision and conflict detection and resolving
Prefix distribution and allocation
  IPv6 prefix delegation
  IPv4 prefix allocation
Routing setup
  Selection of a shared routing protocol
  Fallback mechanism to setup routes autonomously
Dynamic border-detection for IPv4 and IPv6
  On-demand firewall reconfiguration
  On-demand RA/DHCP/DHCPv6 server configuration
  Integration of fixed external connections (e.g. PPP, 6rd, ...)
Sharing of DNS and Service Discovery configuration
  Local DNS configuration
  mDNS / DNS-SD hybrid proxy configuration

## Slide 10: HNCP data model
Flexible TLV-only message structure.
Each router has:
  An unique identity, for example, it may be a public key, unique hardware ID, or some other unique blob of binary data.
  A synchronized configuration data set (ordered set of TLVs), with:
    Latest update sequence number.
    Relative time, in milliseconds, since last publishing of the current TLV data set.
    Hash over the set for fast comparison.
  A public/private key-pair for authentication.
Change in state / data noticed when the hash calculated (and advertised) over the data changes..

## Slide 11: Actually there is more in the pipe..
Recent Autonomic Networking” (AV) activity and non-WG forming BoF on UCAN steps into home networking area as well:
  Aims at self-management, including self-configuration, self-optimization, self-healing and self-protection of the network.
  AN will need to discover information about the surrounding network and to negotiate parameter settings with their neighbors and other nodes.
  Possible a learning and cognitive capability, i.e. the ability for distributed entities to self-adapt their decision making process based on information and knowledge gained from their environment (sensing).
Defines a new “Configuration Discovery and Negotiation Protocol for Network Devices” (CDNP).
HNCP is a database synchronization protocol while CDNP is a generic negotiation protocol.. but can be used to achieve the same thing..
AN and CDNP targets larger networks than home networks but..

## Slide 12: And how this relates to 802.1Qca et al..?
In certain deployments, like, home networking environment:
  L3 and L2 are developing their own.
There should be a standard way to make these two layers to communicate; for example:
  When doing path computation and reservation over multiple L3 segments.
  When segmenting the network for different purposes so that both layers have the same view of the topology.
The list goes on.. Basically ensuring alignment.

## Slide 13: Architecture considerations for .1Qca
Path reservation over multiple L3 segments:
  L2 may still have arbitrary non-loop-free cabling..
  L2 area in a L3 segment may contain arbitrary switched topology..
L2 using IS-IS SPB, whereas L3 can be e.g. IS-IS, OSPFv3 or nothing..
Need for a L3 to L2 communication for path reservation and coordinated network segmentation?
CPE
ISP
DHCPv6-PD ->
TV etc
e.g. TV feed
Home Automation
Remote managed utilities
/64
/64
/64
/64
/64
/64
Public
server
NAS
HNET
RTR
HNET
RTR
HNET
RTR
Visitor nw
3rd party
Managed nw
Home IoT
Media nw
Home nw
Common nw
? (unintentional loop)
How does .1Qca fit here?

## Slide 14: Architecture considerations for .1Qca
How would 802.1Qca with PCE – PE architecture fit here..
  Multiple PCEs and Pes. Also PCE to PCE communication..
  See ca-farkas-small-nets-0514-v02.pdf
ISP#1 CPE
ISP#2 CPE
ISP #1
ISP #2
Internal
network
HNET RTR
Host
Host
Host
Host
PCE1
PCE2
PEs for
PCE1
PEs for
PCE2
.1Qca
(br to br)
.1Qca
PCE to PE
What if a host belongs to two CPEs? A PE belongs still to one PCE..

## Slide 15: Architecture proposal forming..
L2 protocols exports service points to the L3 protocols to allow these protocols to be deterministic while network agnostic.
Ok.. The architecture applies to larger or smaller scale networks than a home network; it just serves a good starting point..
PCE ”part of” the router or CPE
PEs agnostic to the multiple PCEs and L3 segments
L3 PCE to PCE link missing..? .1Qca or something else..?
L3-L2 “PCE” service point missing..?

## Slide 16: conclusions
Need for alignment with L2 and L3 efforts:
  For example in home networking.
Solution for L2 and L3 cooperation for e.g. path reservations:
  Expose required service points.
  Agree on minimum set of required information elements passed between functions and layers.
Fitting the (.1Qca) PCE – PE model with L3 developments.
The same architecture principles should work for:
  Large networks (with added bells and whistles); and
  Smaller networks (with reduced “dynamic” parts).