## Slide 1: Radio over Ethernet standards activity in IEEE1904
Jouni Korhonen
IEEE802.1TSN @Atlanta 2015

## Slide 2: Disclaimer
This is not an official IEEE1904 WG output; just an informal update what is happening regarding Radio over Ethernet in IEEE1904.

## Slide 3: What, when and where..
What:
  Standards development for Radio over Ethernet (RoE) encapsulation and mappers.
When:
  PAR form submitted to NesCom in 19-Nov-2014.
  PAR approved by SASB in Dec 2014.
  First f2f meeting on week 6 in Feb 2015.
Where:
  Sponsored by IEEE ComSoc/SDB.
  Hosted by IEEE 1904 ANWG as a 1904.3 TF.
  IEEE 1904.3 is individual project and anyone can join.

## Slide 4: PAR content in a nutshell
The encapsulation of digitized radio payload (e.g. IQ data), possible vendor specific, management and control data channels/flows into an encapsulating Ethernet frame payload field: -> define a Native RoE Encapsulation Transport Format.
The header format for both structure-aware and structure-agnostic encapsulation transport formats. The structure-aware encapsulation has detailed knowledge of the encapsulated digitized radio transport format content. The structure-agnostic encapsulation is only a container for the encapsulated “alien” digitized radio transport frames: -> allow also alien format encapsulation and transport.
A structure-aware mapper for CPRI and payloads to/from Ethernet encapsulated frames. The structure-aware encapsulation is not restricted to current CPRI – other mappers are possible: -> define a “CPRI to Native RoE Format” mapper.
(the mapper cannot obviously map any reserved and stuffing bits if those are
used to carry meaningful data.. )

## Slide 5: What is not part of the PAR
No changes to Ethernet Packet format
No changes to MAC
No normative queuing, timing and synchronization definitions.. Only ensure that:
  Desired RoE traffic fits into the available link capacity with the encapsulation overhead.
  Desired RoE traffic (structure aware or agnostic flows) have a realistic chance to meet their respective timing requirements.

## Slide 6: RoE encapsulation overview – Ethernet packet remains unchanged
Preamble + SFD
MAC DA
MAC SA
EthType
Payload >= 64
octets
FCS
Inter Packet GAP
No
change
to
Ethernet
packet
format
Reserve EthType(s)
Define RoE encapsulation
Implementation / Operational
Clarifications (only when necessary)
PAR scope
Ethernet Frame

## Slide 7: RoE Encapsulation Alternatives: Structure Agnostic Encapsulation
Preamble + SFD
MAC DA
MAC SA
EthType
RoE Header ->
Length, Type = structure agnostic, etc
FCS
Inter Packet GAP
OBSAI frame(s)
OBSAI frame(s)
OBSAI frame(s)
unchanged
OBSAI frame(s)
OBSAI frame(s)
CPRI frame(s)
unchanged
RoE Payload
Ethernet
frame
payload
OBSAI frame(s)
OBSAI frame(s)
XYZ format frame(s)
unchanged
Ethernet Frame

## Slide 8: RoE Encapsulation Alternatives: RoE Structure Aware Encapsulation
Preamble + SFD
MAC DA
MAC SA
EthType
RoE Header ->
Length, Flow ID, Flow Type = IQ/ vsd/ctrl/C&M/etc, Sample size, etc
FCS
Inter Packet GAP
RoE Payload
Ethernet
frame
payload
OBSAI frame(s)
OBSAI frame(s)
Transport of mixture of Antenna Carriers e.g., IQ data (LTE, 3G, 2G, ..)
Can be unmodified, preprocessed, compressed, ..
OBSAI frame(s)
OBSAI frame(s)
Other flows (provide only transport, content opaque)
Ethernet Frame
i.e. the “Native RoE Format”

## Slide 9: Q & A
More data available:
  http://www.ieee1904.org/3/index.shtml