## Slide 1
Bridging 64-bit MACs
with
48-bit MACs
Behcet Sarikaya
Li Yizhou

## Slide 2: Current IoT Networking
IETF is developing IPv6 solutions for addressing and routing in the PAN
IETF is developing only IPv6 solutions on IoT in an effort to push IPv6
IPv6 solution requires home network to terminate IP and then restart IPv6 routing downstream
802.3 frame from IoT server in the Internet can not be bridged at PAN coordinator
Layer 2 is not end-to-end

## Slide 3: 64-bit MACs vs 48-bit MACs
In the PAN, there are nodes connected to two IEEE 802 technologies like 802.15 and 802.3, PAN coordinator and intermediate routers if any
This brings MAC frame format incompatibilities especially MAC addresses, MPDU and timing issues

## Slide 4: Where to Bridge in the PAN?
Scenario 1. At the PAN Coordinator
Scenario 2. At lower levels in the PAN
We need to add other scenarios like IPv4 usage

## Slide 5: Frame Formats
802.15.4 MAC Data Frame
Only 802.15.4 MAC has 64 bit MAC addresses, others like Bluetooth or 802.15.1 are 48 bit
802.3 MAC Data Frame
8 6
6 2 0 to 1500 0 to 46
4
Preamble
Destination
address
Source
address
Type
Data
Pad
Checksum

## Slide 6: 802.15.4 to 802.3 Adaptation or Bridging
Address bridging: 802.15.4 MAC address long format is 64 bits or 8 octets, 802.3 supports 48 bit MAC address, i.e. 6 octets
MPDU bridging: Some 802.15.4 PHY limit MPDUs to 127 octets, 802.3 has 1500 octet MPDUs
Timing bridging: See later

## Slide 7: MAC address adaptation
48-bit MAC addresses can be converted (mapped) into 64-bit addresses as in IEEE Guidelines standards.ieee.org/develop/regauth/tut/eui64.pdf
  Unfortunately it was found out that IEEE Guidelines was wrong, so no solution for 48-bit MAC to 64-bit MAC exists
No solution for 64-bit to 48-bit MAC address conversion
New developments in this area include 802.1 PAR dealing with local addresses and Layer 2 Routing protocol

## Slide 8: 802.1 Local Address Study Group
IEEE 802.1 started a Study Group on Local addresses, http://www.ieee802.org/1/pages/lasg.html
48-bit MAC addresses are depleting like IPv4 addresses because of Data Center, IoT, etc.
Local address SG will recommend how to use local addresses, 7th bit in Byte 1 set to 1
Local address SG will develop protocols to acquire local addresses
Address Bridging: 64-bit to 48-bit address adaptation work is needed in 802.1
Local addresses can be used by the bridge during address bridging

## Slide 9: L2R
IEEE 802.15 Task Group 10 finished developing a new protocol on Layer 2 routing in Wireless Personal Area Network (WPAN)
After the incoming frame if bridged to 802.15 network, L2R protocol can route it to the destination

## Slide 10: MPDU Size Adaptation
802.15 amendments that can support 1500 octets: 802.3d, 802.15.4g, 802.15.4m
Other 802.15 technologies that have smaller MPDU sizes like 127 octets in 802.15.4.e
Ethernet can carry frame sizes 64 to 1500 octets
MPDU bridging: Bridge may receive frames longer than 802.15 can handle, fragmentation/reassembly is needed in 802.15
Notes: Check these 802.15.3 802.15.1 802.15.6

## Slide 11: Timing Considerations
Bridge keeps a frame for a maximum of 1sec until it reaches the destination
This value can be increased to 4sec maximum value
802.15 has sleeping nodes (4e, 4f, 4k, 15.1, 15.6)
Timing Bridging: The work has to address this issue in 802.1
There are wakeup frames defined in 802.15.4e, 4k
Ways to wake up in other cases

## Slide 12: MPDU Size for 802.15.4
802.15.4 amendments that can support 1500 octets: 802.15.4g, 802.15.4m
Others like 802.15.4k do not
Limit the adaptation to those that can support
Limit point to point link establishment to those that can support
Notes: Check these 802.15.3 802.15.1 802.15.6

## Slide 13
Thank you! Questions
Notes: Fragmentation, timing in ethernet and 802.15 , low power