## Slide 1: P802.1CQ Assignment and Validation of Unicast Address
Hiroki Nakano

## Slide 2: Problem Statement
How can we assign locally-unique unicast addresses?
  orchestration protocols?
  T11 FC-BB-6?
  random?
  Some other protocols?
  In case of multicast addresses, it may be impossible to detect collision and it’s harmless relatively (really?)
The most important thing is ‘UNIQUE’
  This is a prerequisite of 802 networks.
  Duplicate addresses are always an annoying problem for network administrators.
  Cheating address breaks forwarding databases and enables attackers to intercept frames. (although it is not directly related to assignment...)
How can we assure uniqueness?

## Slide 3: Assurance of Uniqueness
Historically, a globally-unique address is assigned to each port by manufacturer.
  Operational errors always occurs.
Do ‘address assignment servers’ assure uniqueness?
  When you operate multiple assignment protocols on a network, how do they cooperate?
My proposal is: 802 should have a single validation protocol as well as assignment protocols. (although it may be optional)

## Slide 4: Assignment and Validation
Multiple assignment protocols can be operated on a network and hosts can choose one of them.
One validation protocol at most is operational.
Results of validation are utilized by 802.1X, 802.1AE, etc.
Assignment
Validation
Assignment
Assignment
UNIQUE
DUPLICATE

## Slide 5: Validation on Managed and Adhoc
Managed Network
Networks administrators manage.
Administrators know when, where and what is connected to networks.
For example:
  802.1X can be used to check MAC addresses.
    MAC-based authentication is a common function for switches.
  802.1aq can be used to gather active MAC addresses.
Adhoc Network
Networks nobody manages like home networks, wireless networks.
Splitting into and uniting two networks sometimes happens.
How?
  Is 802.1aq usable? other ideas?
  Address collision can occur when two networks unite. How does it resolve?

## Slide 6: Other considerations
IEEE802.11ai
  This is an effort to reduce time for Initial Link Setup. MAC address assignment may be included in ‘Initial Link Setup’ procedure. To achieve this goal, timeout-less protocol is expected for 802.1CQ, that is, no ’timeout’ procedure in normal successful operation.