## Slide 1: IETF YANG models for VLAN interface classification
draft-wilton-netmod-intf-vlan-yang
Robert Wilton (Cisco)

## Slide 2: Presentation Objectives
To explain what this IETF model is trying to achieve
To justify why this is being standardized in IETF
To hopefully get agreement from IEEE 802.1 that it is acceptable for IETF to standardize this model …
  Without this model a lot of standard IETF protocols are unconfigurable via YANG, or unusable with 802.1Q VLAN tagged traffic!
  Draft is currently blocked in IETF at the equivalent of the PAR phase – we don’t want to antagonise IEEE 802.1 by starting a project that conflicts with IEEE.

## Slide 3: What is an interface?
Based on the IFMIB & ietf-interfaces.yang, an interface can be defined as a generic container with the following characteristics:
It identifies a stream of network traffic (potentially at any layer)
It is an anchor point to apply features and protocol forwarding configuration on that stream of traffic
It has an interface type (IANA defines many different flavours)
It has a default set of traffic statistics
It can be enabled/disabled via configuration

## Slide 4: What is a child interface? Why is it needed? (1)
Sometimes it is necessary to apply the feature and forwarding rules to a subset of traffic on an interface
This can be modelled cleanly using child-interfaces:
Parent interface
E.g.
Phy Ethernet, LAG,
Pseudo-wire,
…
Child interfaces
Traffic forwarded by IP in VRF x
Traffic forwarded by IP in VRF y
Traffic forwarded via VPLS instance
…

## Slide 5: What is a child interface? Why is it needed? (2)
A child interface is a type of interface that allows separate feature and forwarding rules to be applied to a subset of the traffic of any parent interface.
  Feature/forwarding schema paths are the same as for any other type of interface!
  Lots of different parent interface types can have child interfaces: Physical Ethernet, LAG, Pseudo-wire Headend, Bridge virtual interface, Frame Relay, ATM, …
A parent interface can have many child interfaces if required
Multiple layers of interface hierarchy are possible
Classification rules are used to demux traffic from a parent interface to its children interfaces
  For interfaces with Ethernet framing VLAN Ids are often used as the demux classification
Forwarding is configured via other IETF protocol YANG models (IPv4, IPv6, MPLS, Pseudowires, VPLS, EVPN, L2TPv3)
Notes: Actually will be modelled as a property rather than a specific IANA type.
Also sometimes called a logical interface.
All L3 and feature configuration can generally apply to it.
Has standard interface properties like stats/MTU/etc.

## Slide 6: What isn’t a child-interface?
It is not just traffic associated with a particular single VLAN Id
  It is far more flexible, matching on sets of tags, or other fields.
It has no predefined forwarding semantics
  Forwarding models can just refer to an if:interface without caring about what type of interface it is, or whether it is a parent or child. IETF forwarding models work with VLANs with no extra changes required.
It is not an alternative way of configuring an IEEE 802.1Q bridge
  Mostly devices that implement child interfaces don’t implement IEEE 802.1Q bridging, although there is no reason why they can’t coexist on the same device.
A LAG member is not a child interface
  A different relationship is required because there are N LAG members to one LAG, and no explicit demux is required.
Notes: LAG interface N:1 relationship is the other way around.

## Slide 7: Why standardize? Why in IETF?
Many vendors have proprietary configuration constructs similar to what is being proposed.
No existing standards exist for this technology in any standards body because historically the end user configuration has not been standardized.
However, there is now a strong market demand for automation via standard YANG models.
Many IETF forwarding YANG models are incomplete without being able to configure them on VLAN child interfaces.
IETF is the right place because IETF owns the generic interface model, this is just an extension and VLANs are one example.

## Slide 8: Clearing up other areas of confusion
Q. Doesn’t ietf-interfaces already model this?
  No, it has read-only leaves for operational state, separate configuration leaves are required.
Q. Is the long term plan for IEEE to adopt ownership of this model?
  No, this model covers different technology/protocols to those standardized in IEEE.
Q. Does this model allow different VLAN traffic on different LAG member interfaces?
  No, this model can’t be used for LAG membership.
Q. Will this model redefine VLAN types?
  No, it will be updated to use the IEEE defined types where possible - we may request that some additional ones get added/defined by IEEE.

## Slide 9: Next steps?
Can we reach agreement for the draft to proceed in IETF as a WG document from this meeting?
Otherwise what is required to unblock it:
  A formal liaison from IETF to IEEE?
  Presenting at the next IEEE plenary/interim?
In the meantime I will continue to incorporate feedback and evolve the model (on the assumption that it will eventually get unblocked 

## Slide 10: Backup slide
More generic picture of how child interface can be used to configure different forwarding services.
L2 child interface connected to a Pseudowire
MPLS
L3
L3/VRF
VPLS
VPLS VFI
Local Connect
Physical interface with 802.1Q tagged traffic classified to child-interfaces
VPLS or PWs
VPLS
BVI
PW
PW
PW HE
L3 child-interface
Physical interfaces with 802.1Q tagged traffic classified to child-interfaces