## Slide 1: Goals and objectives
Project(s): MBH IA Phase 4 Transport for 5G Networks
Purpose of the contribution: Input to MBH IA Phase 4
Abstract: Overview on the IEEE P802.1CM Time-Sensitive Networking for Fronthaul project
Motion: no

## Slide 2: IEEE P802.1CM Time-Sensitive Networking for Fronthaul
János Farkas – Ericsson
April 25, 2017 MEF 61035

## Slide 3: Agenda
Introduction
  IEEE 802.1 Time-Sensitive Networking (TSN) overview
  5G overview, 5G fronthaul, Radio Base Station split
Approach to Ethernet-based fronthaul
IEEE 802.1CM TSN for Fronthaul – goals and objectives
Collaborative effort of CPRI Cooperation and IEEE 802.1
Top Down Approach
Requirements
Fronthaul Profiles (so far)
Summary of IEEE P802.1CM
Potential MEF 22 – P802.1CM collaboration items

## Slide 4: IEEE 802.1 Time-Sensitive Networking (TSN) Overview
TSN Components Common Standards
Latency
Bounded low latency: Credit Based Shaper (802.1Qav) Frame preemption (802.3br & 802.1Qbu) Scheduled Traffic (802.1Qbv) Cyclic Queuing and Forwarding (802.1Qch) Asynchronous Traffic Shaping (P802.1Qcr)
Reliability
Ultra reliability: Frame Replication and Elimination (P802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (P802.1AS-Rev)
Synchronization
Time synchronization: Timing and Synchronization (802.1AS) includes a profile of IEEE 1588
Guaranteed data transport with bounded low latency, low delay variation, and extremely low loss
Zero congestion loss
http://www.ieee802.org/1/pages/tsn.html
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (P802.1Qcc) YANG (P802.1Qcp) Link-local Registration Protocol (P802.1CS)
API: Application Programming Interface; YANG: a data modeling language
Note: selecting features is a task in the P802.1CM TSN for Fronthaul project

## Slide 5: 5G Overview
Ethernet-based fronthaul is integral part of 5G
Cloud Infrastructure
Network integrated compute and storage
5G Radio Access
3 GHz
10 GHz
30 GHz
100 GHz
Higher Frequencies
Larger BW
Spectrum Flexibility
Access-backhaul Integration (incl. self-backhauling)
Ultra-lean Design
Device-to-Device Communication
Inter-Site Cooperation
Multi-antenna technologies
5G Core functionality
Utilize NFV and SDN Network programmability
Flexible deployment of network functions
Service enablers and optimizations
Multi-use case
Common toolbox
Fixed access
Legacy RATs
5G Use Cases
Broadband everywhere
Smart vehicles transport and infrastructure
Media everywhere
Critical control of remote devices
Interaction human IoT
… and more
5G Transport
SDN
Backhaul
Fronthaul
Aggregation
Network programmability
Optical enablers
Management
Orchestration
Network management
Analytics

## Slide 6: 5G Fronthaul – Simplified Architecture
Radio Base Station (RBS)
backhaul
fronthaul
Radio Equipment (RE)
Radio Equipment Control (REC)
backhaul
Radio Base Station (RBS)
baseband
RBS split

## Slide 7: Radio Base Station Split
Current focus of P802.1CM is the functional split specified by the Common Public Radio Interface (CPRI) 7.0
Next step in P802.1CM is eCPRI (http://www.cpri.info/press.html)
Further functional splits can be addressed in 802.1CM amendment
Current split (CPRI 7.0)
PDCP
RLC
MAC
PHY
Radio
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Controller
No split
PDCP
RLC
MAC
PHY
Radio
Possible splits
Layer 3
Layer 2
Layer 1
Radio
Layer 3
Layer 2
Layer 1
Radio
Layer 3
Layer 2
Layer 1
Radio
Further splits are possible
eCPRI
Layer 3
Layer 2
Layer 1
Radio
Layer 3
Layer 2
Layer 1
Radio

## Slide 8: Approach to Ethernet-based Fronthaul
IEEE 802.1/802.3 Ethernet network
RE
fronthaul
REC
interface
Radio Domain
Packet Domain (Ethernet-based)
MEF UNI
MEF Services
Ethernet networking specified by IEEE 802.1CM TSN for Fronthaul

## Slide 9: IEEE 802.1CM TSN for Fronthaul Goals & Objectives
Standard TSN Profiles for fronthaul
  Enable the transport of fronthaul streams in a bridged network
A TSN Profile
  Specifies aspects of bridge operation
  Set of feature and option selections
  Configuration guideline
RE1
Bridged network for Fronthaul
REC1
REC2
RE2
RE3

## Slide 10: Collaborative effort of CPRI Cooperation and IEEE 802.1
Both organizations have proven that they deliver
P802.1CM TSN for Fronthaul is a collaborative effort
  Joint sessions: face-to-face and virtual
  Common members
Ethernet-based packet fronthaul is on its way
CPRI Cooperation
  http://www.cpri.info/
  Fronthaul experts
  Continuous development of CPRI specifications for 15 years
  eCPRI (http://www.cpri.info/press.html)
IEEE 802.1
  http://www.ieee802.org/1/
  Ethernet networking experts
  Packet networking standards for decades
  Time-Sensitive Networking (TSN)

## Slide 11: P802.1CM Project Takes Top Down Approach
Collect requirements
  CPRI Cooperation provides use cases and requirements
Collect the packet networking and synchronization features to address requirements
  Bridging features and characteristics
  Time-Sensitive Networking features
  Synchronization solutions and approaches
    ITU-T Q13/15 contributes (e.g., how to leverage the IEEE 1588 Telecom profile)
Specify solution details
  Profiles specify how to meet the fronthaul requirements in an Ethernet network

## Slide 12: Requirements – Contributed by CPRI Cooperation
Class 1
  RBS functional split is according to CPRI 7.0
  CPRI information flows are separated from each other
    IQ data and the C&M data are independent data streams, NO CPRI  Eth mapping “as is”
    IQ data requirements
      maximum end-to-end One-way Frame Delay = 100 μs (no requirement on Frame Delay Variation)
      maximum Frame Loss Ratio = 10-7
    C&M data requirement: maximum Frame Loss Ratio = 10-6
Class 2
  eCPRI (to be added)
Synchronization
  Synchronization is provided separately from IQ and C&M, e.g., GNSS, PTP
  4 time synchronization requirement Categories for different 3GPP features

## Slide 13: Fronthaul Profiles for Class 1 (so far)
Profiles are engineered taking into account the worst-case
Profile A
  Keep it as simple as possible
  Based on strict priority
    IQ data  high priority traffic class
    C&M data  lower priority traffic class
  Max frame size for all traffic: 2000 octets (IEEE 802.3)
Profile B
  Leverage simple TSN features
  Based on strict priority and frame preemption (802.3br and 802.1Qbu)
    IQ data  high priority traffic class; express traffic
    C&M data  lower priority traffic class; preemptable traffic
  Frame size maximized for IQ data; arbitrary for other traffic

## Slide 14: Ethernet-based Fronthaul with IEEE 802.1CM
RE
REC
Radio Domain
Packet Domain
fronthaul interface
CPRI, eCPRI, etc.
IEEE 802.1CM Fronthaul Profiles
  meet the requirements of fronthaul flows
Synchronization can be provided by packet network, e.g., Sync as a Service (SaaS)
IEEE 802.1/802.3 Ethernet encapsulation
fronthaul flows are separated, e.g., by priority, VID
synchronization is separated from fronthaul data flows
IEEE 802.1CM
MEF UNI
edge ports perform std IEEE 802.1/802.3 Ethernet encapsulation
MEF Services
separated fronthaul flows
separated fronthaul flows
user (IQ)
C&M
C&M
user (IQ)
SaaS
SaaS

## Slide 15: P802.1 CM Summary
IEEE 802.1CM specifies TSN Profiles for Fronthaul
It is a collaborative effort of CPRI Cooperation and IEEE 802.1
The project takes top down approach: requirements  solution
Requirements are provided by CPRI Cooperation
Current focus: RBS split according to CPRI 7.0 and the different fronthaul information flows are supported separately
Two Fronthaul Profiles (so far)
Support for eCPRI is next step
Work in progress; Welcome to contribute! http://www.ieee802.org/1/pages/802.1cm.html

## Slide 16: Potential MBH IA – P802.1CM Collaboration Items
Sync as a Service (SaaS)
  SaaS provided by the Ethernet network is one of the options to provide synchronization for fronthaul if the requirements are met
  SaaS specified by MEF 22.2 and 22.2.1 is referred in IEEE 802.1CM
Potential discussion items for MBH IA Phase 4 Transport for 5G
  3 different CoS are needed for fronthaul: user (IQ) data + C&M + Sync
  Sync is already defined
  The requirements of user (IQ) data and C&M have to be met
  Any new CoS?