## Slide 1
Ting Ao
ao.ting@zte.com.cn
Local MAC Address Protocol

## Slide 2: Prior Contributions Review
802.1CQ PAR&CSD: This standard specifies protocols, procedures, and management objects for locally-unique assignment of 48-bit and 64-bit addresses in IEEE 802 networks. Peer-to-peer address claiming and address server capabilities are specified.
  http://www.ieee802.org/1/files/public/docs2015/dcb-thaler-1CQ-par-local-address-prot-1115-v0.pdf
  http://www.ieee802.org/1/files/public/docs2015/dcb-thaler-1CQ-csd-local-address-prot-1115.pdf
802.1CQ Objective:
  Allow for acquiring multiple addresses
  Allow for edge bridge / access point proxy
  http://www.ieee802.org/1/files/public/docs2016/cq-thaler-objectives-1116.pdf
Assignment and Validation of Unicast Address
  802 should have a single validation protocol as well as assignment protocols.
  http://www.ieee802.org/1/files/public/docs2016/cq-cas-assignment-and-validation-0316-v00.pptx
Structured MAC address assignment with Server
  Assign structured MAC address hierarchically
  http://www.ieee802.org/1/files/public/docs2016/cq-ao-local-address-assignment-1116-v00.pptx
LAAP：Local MAC Address Assignment Protocol
  Support server assignment and peer-to-peer claim assignment
  http://www.ieee802.org/1/files/public/docs2017/ cq-ao-LAAP-proposal-0317-v02.pptx
LAAP solution：
http://www.ieee802.org/1/files/public/docs2017/cq-ao-LAAP-proposal-0317-v02.pptx
http://www.ieee802.org/1/files/public/docs2016/cq-ao-local-address-assignment-1116-v00.pptx

## Slide 3: LAAP contains
Assignment part
  Server mode
  Declare mode
  Hybrid mode
Coordination part
  Improve the assignment time
  Avoid some address conflict case
Server
Proxy
Proxy
Server
applicant
applicant
applicant
applicant
applicant
applicant
applicant
applicant
applicant
applicant
applicant
applicant

## Slide 4: LAAP-assignment
Server mode
  Every Host sends MAC Address Request Message to ask for MAC address .
  Server sends MAC Address Response Message to assign MAC addresses to the Host.
  To make sure that the Request Message and Response Message is one-to-one relationship, there should be a Message ID in Request Message and Respond Message.
  Bridge in the network forward the Request Message to Server, and then forward the Response Message to the Host according to the Message ID.
Server
B1
B2
B11
B12
B22
B21(P21)
H1
H2
H3
H4
H5
H6
H7
H8
1
2
3
4

## Slide 5: LAAP-assignment
Declare mode
  Host sends a Register Message to claim its MAC address
  Host sends a Declare Message to declare its MAC address if there is no Conflict Message received in a period
  An Message ID also must be included to differentiate every request no matter it’s a Register Message, Conflict Message or Declare Message.
  A Proxy entity is involved to make the claim action be more efficient. A proxy can be a server.
B
T
B
L
B
L
B(P)
1
2
3
4
5

## Slide 6: LAAP-assignment
  Hybrid mode
    Host sends a Register Message to claim its MAC address
  Once the Server receive the Register Message, it will check if there is conflict.
    If there is no conflict, send a Confirmation Message.
    If there is conflict, send a MAC Address Response Message to assign MAC addresses.
  Host will send a Declare Message to announce its own MAC addresses.
  An Message ID also must be included in every message.
B
T
B
L
B
L
S
1
2
3
4
5

## Slide 7: Assignment Message
Destination address: A dedicated MAC address( A server address or a multicast MAC address based on different mode)
Source address: a temporary MAC address
Message type:
  Request Message: To request assignment of MAC addresses
  Respond Message: To assign MAC addresses
  Register Message: To register MAC addresses in the network
  Conflict Message: To inform that the registered MAC addresses have conflict
  Confirmation Message: To confirm that the registered MAC addresses are available
  Declare Message: To declare the own of MAC addresses. Once declared, these MAC addresses can be used by the declarant.
Message ID:
  ID Type: The type of the Identifier
  Identifier: the unique identifier based on ID Type
MAC address TLV

## Slide 8: LAAP-Coordination
Server-Server, Server-Proxy and Proxy-Proxy would coordinate each other.
Once a MAC address has been assigned, Servers and proxies should be flushed.
Every coordination function has two components:
  Database components: All the MAC addresses that have been confirmed are stored in this database.
    MAC address from Declare Message is stored as user-side MAC address
    MAC address from Synchronization Message is stored as network-side MAC address
  Synchronization component: Send out Synchronization Message according to the update of the local database or timely.
Once a Proxy has a synchronization function, it can be considered as a server and will judge the conflict and terminate the Registration Message to the network.
Based on LRP(802.1CS) in an option.

## Slide 9: LAAP-Coordination
As declare mode assignment procedure, T declare its MAC address by Declare Message.
Proxy update its database according to the Declare Message.
Proxy send out Synchronization Message to other proxies or servers to notify the MAC address has been assigned.
Proxy receiving the Synchronization Message update its database.
B
T
B(P)
L
B
L
B(P)
1
2
3
4
5
6
7

## Slide 10: Coordination Message
Destination address: Multicast address first. After the discovery, change to its neighbor's address.
Source address: Server’s address
Message Type：
  Sych Message：Update-driven sending and periodic keepalive
  Ack Message: Confirm the update
MAC info TLV
  MAC address: The new assigned user-side MAC address.
  Timestamp: Time the corresponding user-side MAC address is assigned.

## Slide 11: Next step
Other specific conflict cases still need to be considered.
We should start this draft now.