## Slide 1: h
Ting Ao(ZTE)
ao.ting@zte.com.cn
Local MAC Address Assignment Protocol(LAAP)
-- Thought on 802.1CQ

## Slide 2: Content
Previous Arts
Basic Requirements for LAAP
Two modes in LAAP
  Server Mode
  Peer-to-Peer Mode

## Slide 3: Prior Arts
802.1CQ PAR&CSD: This standard specifies protocols, procedures, and management objects for locally-unique assignment of 48-bit and 64-bit addresses in IEEE 802 networks. Peer-to-peer address claiming and address server capabilities are specified.
  http://www.ieee802.org/1/files/public/docs2015/dcb-thaler-1CQ-par-local-address-prot-1115-v0.pdf
  http://www.ieee802.org/1/files/public/docs2015/dcb-thaler-1CQ-csd-local-address-prot-1115.pdf
802.1CQ Objective:
  Allow for acquiring multiple addresses
  Allow for edge bridge / access point proxy
  http://www.ieee802.org/1/files/public/docs2016/cq-thaler-objectives-1116.pdf
Assignment and Validation of Unicast Address
  802 should have a single validation protocol as well as assignment protocols.
  http://www.ieee802.org/1/files/public/docs2016/cq-cas-assignment-and-validation-0316-v00.pptx
Structured MAC address assignment with Server
  Assign structured MAC address hierarchically
  http://www.ieee802.org/1/files/public/docs2016/cq-ao-local-address-assignment-1116-v00.pptx

## Slide 4: Requirements on LAAP
LAAP: Local MAC Address Assignment Protocol
Basic requirements:
  Support server assignment and peer-to-peer claim assignment*
  Allow proxy for fast assignment*
  It should be a lightweight protocol
  Avoid addresses conflict
  Avoid too many multicast packets and avoid loop

## Slide 5: Server Mode
Principle:
  Every Host sends MAC Address Request Message to ask for MAC address .
  Server sends MAC Address Response Message to assign MAC address to the Host.
  To make sure that the Request Message and Response Message is one-to-one relationship, there should be a Message ID in Request Message and Respond Message.
  Bridge in the network forward the Request Message to Server, and then forward the Response Message to the Host according to the Message ID.
  Some Bridges can play as a Proxy to request MAC address block first, so that once it get Request Message, the Proxy can respond instead of Server .

## Slide 6: Message Content
Message Type
  MAC Address Request Message
  MAC Address Respond Message
Message ID
  Identify each message
  60 bits/80 bits:48/64 bits MAC address+ 16 bits random number
MAC address block
  MAC address starting address
  Quantity: number of MAC addresses in the block

## Slide 7: Scenarios on Server mode-1
①H(Host) send Request Message with Message ID and address number
②B(Bridge) save the mapping information of Message ID and ingress port, and forward the Request Message to the Server
③S(Server) get the Request Message and assign a MAC address block in Response Message. The Response Message has the same Message ID with corresponding Request Message.
④B forward Response Message back to the Host according to the mapping information
Server
B1
B2
B11
B12
B22
B21(P21)
H1
H2
H3
H4
H5
H6
H7
H8
1
2
3
4

## Slide 8: Scenarios on Server mode-2
①B(Bridge) as a Proxy send Request Message to ask a MAC address block as a minor MAC address resource
②S(Server) assign some MAC address to B first
③H(Host) send Request Message to get MAC addresses
④B(Bridge) as a proxy send Response Message instead of Server with assigned MAC address.
Note: Bridges as Server Proxy can be hierarchical.
Server
B1
B2
B11(P11)
B12
B22
B21(P21)
H1
H2
H3
H4
H5
H6
H7
H8
1
2
3
4

## Slide 9: Peer-to-Peer Mode
Principle:
  Every Host sends a Register Message to claim its MAC address
  Every Requester sends a Declare Message to confirm its MAC address if there is no Conflict Message received
  An ID must be included to differentiate every request no matter it’s a Register Message, Conflict Message or Declare Message.
  A Proxy entity is involved to make the claim action be more efficient.

## Slide 10: Message Content
Message Type
  Register Message: To register MAC address block in the network
  Conflict Message: To inform the conflict
  Declare Message: To declare MAC address block in the network. Once declared, the MAC addresses can be used by the declarant.
Message ID
  Identify each message
  60 bits/80 bits:48/64 bits MAC address+ 16 bits random number
MAC address block
  MAC address starting address
  Quantity: number of MAC addresses in the block

## Slide 11: Scenarios on Peer-to-Peer mode-1
①T(Talker) send Register Message with Message ID and MAC address block
②B(Bridge) save the mapping information of Message ID and ingress port, and forward the Register Message to other ports except ingress port
③L(Listener) get the Register Message and check the MAC address block if there is a conflict. If yes, L send out a Conflict message with the same Message ID in the Register Message. If not, terminate the Register Message.
④Bridge forward the Conflict Message according to the mapping information.
⑤If T get the Conflict Message and start a new registration cycle. If not, T send Declare Message to the network
B
T
B
L
B
L
B
1
2
3
4
5

## Slide 12: Scenarios on Peer-to-Peer mode-2
①T(Talker) send Register Message with Message ID and MAC address block
②B(Bridge) save the mapping information of Message ID and ingress port, and forward the Register Message to other ports except ingress port
③P(Proxy) check the MAC address block in the Register Message whether there is a conflict. If yes, send out Conflict Message back to T. If not, forward the Register Message to other ports.
④If T get the Conflict Message, it starts a new registration cycle. If not, T send Declare Message to the network
⑤P record the MAC address block to be used according to the information in Declare Message.
B
T
B
L
B
L
B(P)
1
2
3
4
5

## Slide 13: Scenarios on Peer-to-Peer mode-3
①T(Talker) send Register Message with Message ID and MAC address block
②B(Bridge) save the mapping information of Message ID and ingress port, and forward the Register Message to the Server
③S(Server) not only can assign MAC address , but also can check the MAC address block in the Register Message whether there is a conflict. If yes, send out Conflict Message back to T.
④If T get the Conflict Message then start a new registration cycle. If not, T send Declare Message to the network
⑤S record the MAC address block to be used according to the information in Declare Message., and will not assign these MAC addresses to other Requester.
B
T
B
L
B
L
S
1
2
3
4
5

## Slide 14: Some thought to be considered
What should LAAP based?
  MRP, LRP?
  LLDP, VDP?
  Or as a new protocol
Multicast address assignment will be considered
VM migration may lead to issues to the protocol
No matter MAC Address Request Message , MAC Address Register Message or MAC Address Declare Message, they are multicast packets, and loop avoidance should be considered.
Coordination need to be considered when multiple assignment protocols co-exist.

## Slide 15
Thanks!