## Slide 1: IEEE 802.1 Time-Sensitive Networking (TSN)
TSN Components Common Standards
Latency
Bounded low latency: Credit Based Shaper (802.1Qav) Frame preemption (802.3br & 802.1Qbu) Scheduled Traffic (802.1Qbv) Cyclic Queuing and Forwarding (802.1Qch) Asynchronous Traffic Shaping (P802.1Qcr)
Reliability
Ultra reliability: Frame Replication and Elimination (P802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (P802.1AS-Rev)
Synchronization
Time synchronization: Timing and Synchronization (802.1AS) includes a profile of IEEE 1588
Zero congestion loss
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (P802.1Qcc) YANG (P802.1Qcp) Link-local Registration Protocol (P802.1CS)
Guaranteed data transport with bounded low latency, low delay variation, and extremely low loss
API: Application Programming Interface; YANG: a data modeling language
http://www.ieee802.org/1/pages/tsn.html