## Slide 1: 802.1Qcj D1.0 Status
Paul Unbehagen
Big Switch Networks
Scott Fincher
Extreme Networks

## Slide 2: Commenting Statistics
8 Approved
3 Disapproved
33 Abstained
44 total voted
IEEE 802.1Qcj / D0.4 Status Update

## Slide 3: Status – D1.0
TLV use description needs refinement
Auto Attach State Machine to be added
State Machine description to be added
Update of normative language
IEEE 802.1Qcj / D0.4 Status Update

## Slide 4: Comment Summary
Shall/Should/May
  18,29,43,46,53 Total:5
Editorial notes
  3,11,24,25,30,31, 40,54 Total:7
MIB’s (& Yang)
  5,34,36,37,39,59 Total:6
Normative Terms
  Requester/Grantor/Element/System
  4,16,17,19,20,23,48 Total:7
State Machine
  41,42, 44, 55, 56,103 Total:3
HMAC
  13,112,113,114,115,116 Total:6

## Slide 5: MIB & Yang
MIB and Yang models are complete, but need editorial assistance.
MIB having some compile issues, expertise from a MIB Dr needed
Yang structure for Qcj is written, but need Yangsters help to make sure its properly used in the IEEE YANG tree structure.

## Slide 6: Auto Attach terms – D1.0
Current Semantics are
  Auto Attach “Registrar” (AAR) = PBB BEB
  Auto Attach “Device” (AAD) = non-PBB network device (bridge or end-station)
Comments 16,19,20 address whether system or element is the proper term
Normative terms from 802.1Q, 802.1AB, and 802.1CS
  SYSTEM: System(s) is used in Q (968 instances), AB (462 instances) and CS (356 instances). A System is described as a Bridge or End Station.
  ELEMENT: Element(s) is used in Q (193 instances), AB (13 instances) and CS (2 instances). An Element is described as a management element, information, application function or within a software system.
  END STATION: End Station is used in Q (567 instances), AB (6 instances) and CS (5 instances). An End Station is described as: a functional unit in an IEEE 802 network that acts as a source of, and/or destination for, link layer data traffic carried on the network.
  APPLICANT: Applicant is used in Q (157 instances), AB (0 instances) and CS (135 instances). An Applicant is described as: The applicant controls a database that the Link-local Registration Protocol replicates to the registrar in the neighbor Portal.
  REGISTRAR: Registrar is used in Q (114 instances), AB (0 instances) and CS (94 instances). An Registrar is described as: The registrar receives the copy of the database that the Link-local Registration Protocol replicates from the applicant in the neighbor Portal.
IEEE 802.1Qcj / D1.0 Status Update

## Slide 7: Auto Attach terms (2) – D1.0
Options for consideration:
  Auto Attach Registrar = PBB BEB
    Auto Attach BEB
    Auto Attach Grantor (PB comment #20)
    Auto Attach Applicant
  Auto Attach “Device” = bridge or end-station
    Auto Attach Requestor
    Auto Attach Registrar?
Editor suggestion is to use
  Auto Attach BEB (AAB) instead of AAR
    the PBB BEB that advertises itself as such and also manages ISID/VLAN Binding table for all attached AAD’s
  Auto Attach Device (AAD)
    the non-PBB Bridge or End Station that advertises itself as such and uses LLDPDUs to request I-SID / VLAN assignments
  Rename AA Element to AA System
IEEE 802.1Qcj / D1.0 Status Update

## Slide 8: State Machine
Propose update text to include state machine diagram
Propose using the LLDP state machine to provide starting point for Qcj State machine
  802.1AB Clause 9.2.8 or 9.2.9?
This may reduce the amount of text needed to describe Qcj operation

## Slide 9: HMAC
Does the group align with Algorithm concept? (#112)
Does consolidation of digest to 16 octets add enough value to change TLV? (#113)

## Slide 10: Plan
Comment resolution at this meeting.
Full working group ballot for next draft.
PAR extension

## Slide 11: End