## Slide 1: 802.1CBdb draft text contribution
IEEE 802.1 Plenary Vancouver
March, 2019

## Slide 2: Contents
Baseline Stream identification proposal
Additions and changes to 802.1 CBdb

## Slide 3: New Proposal
M&M identification on top of the EISS

## Slide 4: Baseline proposal
Mask & Match stream identification function as passive stream identification function on top of the EISS
  implemented only up the stack
  using a subset of the EM_UNITDATA.indication primitive parameters as input
(
destination_address,
source_address,
mac_service_data_unit*,
priority,
drop_eligible,
vlan_identifier,
frame_check_sequence,
service_access_point_identifier,
connection_identifier,
flow_hash,
time_to_live
)
* If the frame is VLAN-tagged, the mac_service_data_unit is the mac_service_data_unit provided by the ISS, which VLAN-tag has been removed.

## Slide 5: Baseline proposal
Union of 2 sets of masks to determine the parameter information to be matched:
  {da_mask, sa_mask, vlan_id_mask} U {msdu_mask}
  {msdu_mask} = {(offset1, length1), (offset2, length2), …, (offsetN, lengthN)} or Ø

## Slide 6: Baseline proposal
How to determine if a frame is tagged or untagged
  Re-use the same “trick” as in the .1CB stream identification functions
    Managed object that indicates that a frame is:
      Tagged
      Untagged
      Any

## Slide 7: Baseline proposal
msdu_mask details:
  each (offset, length) couple defines a field of length bits that must match a length-bit value defined for the stream identification function instance
  Number of (offset, length) couples is specified
    If the number of couples equals 0, the msdu parameter is ignored
  Unit of offset and length: bits
    Max offset and length values have to be fixed
  offset = 0 points to the first bit of the mac_service_data_unit
  Length = number of consecutive bits

## Slide 8: Baseline proposal
da_, sa_, vlan_id_ mask details
  da_ and sa_ masks are 48-bit long
  vlan_id_mask is 12-bit long
  Masks allow “ternary” match:
    Mask’s bits set to ‘1’ indicate a bit position that must match
    Mask’s bits set to ‘0’ indicate a bit position that always match (don’t care)
  An all-zero mask indicates that the corresponding parameter is ignored

## Slide 9: Additions and changes to 802.1CB
Text contribution

## Slide 10: Changes in 802.1CB
Clause 6 : addition of a new passive stream identification function
  Clause 6.8
    Not baptized yet: denominated as “Extended Stream identification function” a.k.a. “EsId”
    Passive identification function that sits at the EISS’ interface with the upper layers
    Takes specific EISS’s indication primitive parameters as input:
      source_address, destination_address, vlan_identifier, mac_service_msdu
    The function defines a set of bit fields, obtained by masking these input parameters
    The stream_handle produced by the function is derived from the matching of the bit field(s) with values specific to an instance of the identification function.

## Slide 11: Changes in 802.1CB
Clause 9 “Stream Identification Management”
  Addition of a new tsnStreamIdIdentificationType
    OUI: 00-80-C2, Type number: 5
  Addition of managed objects (tsnStreamIdParameters) defining the masks sets and the values to be matched: Sub-clause 9.1.6
    See next slide
Clause 5 “Conformance”:
  EsId optional in Talkers, Listeners
  EsId recommended in Relay systems
Annex A “PICS”:
  Reflects
  Informative annex: example use of the function

## Slide 12: Changes in 802.1CB
Clause 9.1.6 “Managed objects for Extended Stream identification”
Name | Description
tsnCpeEsIdDestMacMask (9.1.6.1) | 48-bit ternary mask to be applied to the destination_address parameter passed up by the EM_UNITDATA.indication primitive
tsnCpeEsIdDestMacMatch (9.1.6.2) | Destination MAC address to be matched with the masked destination_address parameter
tsnCpeEsIdSrcMacMask (9.1.6.3) | 48-bit ternary mask to be applied to the source_address parameter passed up by the EM_UNITDATA.indication primitive
tsnCpeEsIdSrcMacMatch (9.1.6.4) | Source MAC address to be matched with the masked source_address parameter
tsnCpeEsIdTagged (9.1.6.5) | Value indicating if the frame is tagged, untagged, or any
tsnCpeEsIdVlanIdMask (9.1.6.6) | 12-bit ternary mask to be applied to the vlan_identifier parameter passed up by the EM_UNITDATA.indication primitive
tsnCpeEsIdVlanIdMatch (9.1.6.7) | VLAN identifier to be matched with the masked vlan_identifier parameter
tsnCpeEsIdMsduFieldNb (9.1.6.8) | Number of bit fields to be matched in the mac_service_data_unit parameter passed up by the EM_UNITDATA.indication primitive (max ?)
tsnCpeEsIdMsduFieldN (9.1.6.9) | Bit field mask, defined by the couple (tsnCpeEsIdMsduFieldOffsetN [9.1.6.9.1], tsnCpeEsIdMsduFieldLengthN [9.6.1.9.2]), to be applied to the mac_service_data_unit parameter passed up by the EM_UNITDATA.indication primitive. 0<N<max ?
tsnCpeEsIdMsduFieldValueN (9.1.6.10) | tsnCpeEsIdMsduFieldLengthN-bit value to be matched with tsnCpeEsIdMsduFieldN

## Slide 13
Thank you for your attention